## Slide 1
MODULE 7.3:
Characteristics of the beverage production line
TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs
Technical

## Slide 2
INFORMATION ON TYPICAL TECHNOLOGICAL LINE CHARACTERISTICS
SOME TECHNOLOGICAL LINE CHARACTERISTICS IN BAVERAGE PRODUCTION LINE
CONTENT

## Slide 3
QUIZ
1. Does the current production line use hot-fill, cold-fill, or aseptic filling technology? What are the pros and cons of each?
2. Are the main machines in the line supplied by one manufacturer or a mix of brands? How does that affect operational efficiency?
3. What sterilization method is currently applied (UHT, Pasteurization, UV...)? What are the cycle time and energy consumption like?
4. Is the line flexible in switching packaging formats (PET bottles, glass bottles, cans...)? How long does format changeover take?

## Slide 4
I.
INFORMATION ON TYPICAL TECHNOLOGICAL LINE CHARACTERISTICS IN BEVERAGE

## Slide 5
Diagram of the input water treatment process
Some technological processes of beverage industry production (1)

## Slide 6
Some technological processes of beverage industry production (2)
Process diagram of carbonated soft drink syrup dispensing technology

## Slide 7
Diagram of the technological process for the production of bottled carbonated soft drinks
Some technological processes of beverage industry production (3)
Filling
De-dusting air blowing to clean the workpiece
Blowing bottles
Datecoding prints
The date code
Capping
Close the lid
Labeling
Packing
Innocheck
Check filling & capping
Datecoding
Palletizing
Full goods
Finished products
Pallet
Packing
Label
Carton shrink film, paper box
OPRP
OPRP
Cooling
Carbonation round CO2
Filter 0.15mm
Final beverage
Preform feeding
Preform checking
PET bottle predom
Closure feeding & checking
Plastic lid

## Slide 8
Technological process diagram for production
of bottled pure drinking water
Some technological processes of beverage industry production (4)
Nitrogen extractor
Capping machine
Filling machine
PET bottle blowing machine
PET preform inspection machine
PET preform
Pasting & checking machine
Packing machine
Nex barrel printer
Pallet trimmer
Forklift vehicle
Store
Printer date
Wire tester with
Ozone mixer
Filter 0.45 um
RO water
Filter 100rsesh
Bottle cap
Grape heart
Cap testing machine
Pallet
Shrink film
Core

## Slide 9
Technological Process Diagram for the
Production of Hot Filling Products
Some technological processes of beverage industry production (5)
Storing in pre-run tank
De - aerating
Homogenizating
Filter 1.5mm
Pasteurising
Cooling
Filting 0.8mm
Filling
Bottle neck rinsing
Capping
Date coding
Innocheck
Inverting
Cooling
Filling
Pasteurizing
Storing
Final plup
FP predoser
PET bottle
blowing
Predom checking
Prefom dedusting
Rinsing
Gassner
Shink labelling
Date coding
Shink packing
Palletzing
Final juice
Label
Shinkfilm
Pallet
Finished goods
Cap
Preform

## Slide 10
Energy use norms for the beer
and non-alcoholic beverage industry from 2025-2030
Circular No. 19/2016/TT-BCT dated September 14, 2016, issued by the Ministry of Industry and Trade, on regulations regarding energy consumption levels in the beer and beverage manufacturing industry.

## Slide 11
Energy use norms for the period from 2025 to 2030
Circular No. 28/2024/TT-BCT issued by the Ministry of Industry and Trade stipulates the energy consumption norms in the beer and non-alcoholic beverage manufacturing industry.

## Slide 12
High Energy In density Inefficient Energy Use Lack of Energy Monitoring and Management
High Operation Costs
Environmental Impact
Emerging Initiatives
The current situation of energy consumption at some enterprises

## Slide 13
Factors affecting energy consumption
.
Monitoring and renovating existing systems in the direction of energy saving, reducing wasted and unnecessary energy;
Changing habits and increasing users' awareness of energy saving;
Applying modern technologies, replacing outdated old devices with new devices that use less energy, helping to increase efficiency with the same energy consumption, using new alternative energy sources;

## Slide 14
II.
SOME TECHNOLOGICAL LINE CHARACTERISTICS IN BAVERAGE PRODUCTION LINE

## Slide 15
Consumption reduction solutions
1. Production Line Optimization
2. Heat recovery and reuse.
3. Cooling System Optimization
5. Smart Energy Management
4. Use of renewable energy

## Slide 16
1. Production Line Optimization
SCADA Application, Consumption Monitoring Sensor Periodic maintenance of heat exchangers, motors Optimize operating speed according to actual load

## Slide 17
2. Heat recovery and reuse
Heat recovery from steam and flush water Reuse of condensate into boilers Save 15–30% of total thermal energy

## Slide 18
3. Refrigeration System Optimization
Inverter compressor: 20-40% saving High Efficiency Refrigerant: NH₃, CO₂ TES system – cold storage at night

## Slide 19
4. Renewable energy
Solar power on the roof of the factory – reducing load during peak hours Biomass boilers, utilizing rice husk/sawdust Biogas from wastewater treatment to boiler incineration

## Slide 20
5. Smart Energy Management
Measurement and warning system for exceeding the threshold AI + IoT Operational Data Analytics Optimize equipment schedules 10–15% saving

## Slide 21
Q & A
1. What is the current OEE (Overall Equipment Effectiveness) of the line? What are the biggest causes of losses (downtime, breakdowns, product defects)?
2. Is energy, water, and steam consumption monitored by production stage? Which stage shows the highest waste?
3. What is the defect rate during filling and packaging? What are the most common causes?
4. Are any inline quality control systems installed (e.g., fill level inspection, weight check, cap integrity, QR code scanning)?

## Slide 22
THANK YOU!