## Slide 1
MODUL 8.3:
Typical Energy Efficiency Measures in the Beverage Industry
TECHNICAL STAFFS
TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs

## Slide 2: CONTENT
Overview of the Beverage Industry
Energy Consumption Profile in Beverage Industry
Method for Identifying Energy Saving Potential
Energy Saving Opportunities
Implementation Roadmap in the Factory

## Slide 3
Q & A
1. What are the main forms of energy used in the factory (electricity, steam, hot water, compressed air…)? Which is the most consumed?
2. Does the factory regularly monitor energy indicators (e.g., kWh/ton of product, kg steam/liter of beverage)? What are the trends over the past 3 years?
3. To what extent has the Energy Monitoring System (EMS) been deployed? Is energy tracked by area or process?

## Slide 4
2. Technological process in the Beverage Industry
Technological process (1)
Diagram of the technological process of producing non-carbonated beverages

## Slide 5: Diagram of the technological process for the production of carbonated beverages
Technological process (2)
2. Technological process in the Beverage Industry

## Slide 6: Technological process diagram for dispensing carbonated soft drink syrup
Technological process (3)
2. Technological process in the Beverage Industry

## Slide 7: Types of energy used in the line - Electricity is used in almost all equipment in the production line and other auxiliary system equipment such as lighting systems, refrigeration and air conditioning systems, air compressors,... - Steam is used to heat production. - DO oil is used to run backup generators, forklifts, fire pumps, internal vehicles.
2. Energy Consumption Profile in Beverage Industry

## Slide 8
2. Energy Consumption Profile in Beverage Industry
Overview of energy consumption in beverage production
These values vary by type of beverage (soft drinks, beer, juice, bottled water) and production scale.
Process Area | Approximate % of Total Energy Consumption
Steam generation / Heating | 30% - 50%
Refrigeration / Cooling | 20% - 35%
Compressed Air Systems | 10% - 15%
Packaging Equipment | 5% - 10%
Pumps & Motors | 5% - 10%
Lighting & HVAC | 3% - 7%
Typical Energy Consumption Breakdown in Beverage Production

## Slide 9
2. Energy Consumption Profile in Beverage Industry
Example Table of Energy Use by Beverage Type (from industry reports)
hl* = hectoliter (100 liters)
Beverage Type | Energy Use (kWh/hl*) | Steam Share (%) | Electricity Share (%)
Carbonated Soft Drinks | 15 - 20 | 40 - 50 | 50 - 60
Beer | 20 - 30 | 45 - 55 | 45 - 55
Bottled Water | 10 - 15 | 25 - 35 | 65 - 75
Juice | 18 - 25 | 40 - 50 | 50 - 60

## Slide 10: 3. Method for Identifying Energy Saving Potential
Using energy audits
Evaluation indicators: SEC (kWh/liter of product), industry benchmarks
Collect current energy usage data
Analyze and evaluate energy consumption
Identify major energy consumption and wastage points
Select and evaluate energy-saving solutions
Prioritize solutions based on economic feasibility and effectiveness
Implement, monitor, and optimize
Training and awareness raising

## Slide 11: 4. Energy Saving Opportunities – Steam
Boiler optimization: oxygen control, economizer refent, flue gas utilization
+ Optimizing the combustion process;
+ Reducing heat loss;
+ Recovering heat from flue gases
+ Upgrading to advanced technology equipment
+ Regular maintenance and proper operation
Steam

## Slide 12: 4. Energy Saving Opportunities
+ Using inverter-driven compressors
+ Selecting high-efficiency refrigeration technology
+ Heat recovery systems
+ Regular maintenance and cleaning
+ Implementing intelligent control systems
+ Improving insulation of cold storage and machine rooms
+ Replace old compressors with high-efficiency equipment
+ Optimize evaporation/condensation temperatures
+ Use variable frequency drives (VFD) for compressors, pumps, condenser fans
+ Enhance insulation for cold storage and piping
Refrigeration and Air Conditioning Systems

## Slide 13: 4. Energy Saving Opportunities
+ Reducing compressed air leakage
+ Using inverter-driven air compressors
+ Optimizing system operating pressure:
+ Efficient design and maintenance of compressed air piping:
+ Recovering waste heat and condensate
+ Implementing compressed air energy management and monitoring systems
Compressed Air Systems

## Slide 14: 4. Energy Saving Opportunities
+ Heat Recovery from Wastewater and Return Flows
+ Optimizing Water and Chemical Usage
+ Efficient Water Heating Systems
+ Scheduling and Automation of CIP Cycles
+ Temperature Control
+ Regular Maintenance and System Monitoring
CIP and Hot Water Systems

## Slide 15: 4. Energy Saving Opportunities
+ Replace with LED lamps, install light sensors
+ Implementing Lighting Controls
+ Optimizing Lighting Design
+ Energy-efficient Electrical Equipment
+ Adjust Power Factor Correction (PFC)
+ Manage loads according to peak/off-peak hours
+ Regular Maintenance
+ Power Factor Correction
+ Energy Monitoring and Management
Upgrading Lighting Systems

## Slide 16: 4. Energy Saving Opportunities
+ Implement Energy Management Systems (EMS) or Building Management Systems (BMS).
+ Monitor energy consumption in real-time to identify inefficiencies.
+ Train staff on energy-saving practices.
Energy Management and Monitoring

## Slide 17: 4. Energy Saving Opportunities
+ Opportunities for solar, biomass, and other renewables
+ Benefits and challenges of adoption
+ Case studies and pilot projects
Renewable Energy Integration

## Slide 18: 4. Energy Saving Opportunities
+ Cost-benefit analysis of energy-saving measures
+ Prioritization based on payback period and feasibility
+ Steps for implementation and continuous improvement
Economic Analysis and Implementation Strategy

## Slide 19: QUIZ
1. Is the boiler equipped with an economizer or flue gas heat recovery system? What is the flue gas temperature loss?
2. Are steam line leaks regularly checked and maintained? What is the estimated pipeline energy loss?
3. What is the average COP (Coefficient of Performance) of the chiller system? Is it load-dependent or constant operation?
4. Is waste heat from the condenser recovered for other uses (e.g., water pre-heating)?
5. Is compressed air leakage monitored, and is system pressure optimized? What is the estimated leak rate (%)?
6. Are air compressors controlled via VSD (Variable Speed Drive) or ON/OFF only?

## Slide 20: 5. Implementation Roadmap in the Factory
Survey and assess current energy use
Plan and select energy-saving solutions
Invest and install equipment
Monitor and optimize operation
Evaluate effectiveness and scale up
Advanced training and continuous upgrading

## Slide 21
Numerous energy-saving solutions have been successfully implemented in Vietnam as well as in other countries:
Improvement of Technology and Equipment Upgrades
Utilizing Renewable Energy Sources and Heat Recovery
…….
These case studies will be presented in the next module.

## Slide 22
THANK YOU!