## Slide 1: TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs
Module 4:
Current and potential of EE in paper and pulp industries in Vietnam
TECHNICAL STAFF

## Slide 2: Small group discuss and presentation
Devided the class into 4 group
Discuss in 15 mins
What sector do you think using the highest energy in Vietnam?
Identify the designated energy users in the paper and pulp company
What energy source your company mainly use?
What potential of EE in your company
Presentation in 5 mins

## Slide 3: Characteristics of energy consumption in Vietnam’s industry
The industry is the leading energy consumer sector in Vietnam, based on electricity consumption and final energy consumption
Vietnam currently has 3,068 DEUs (up from 2,496 in 2017), consuming 51,393,648 TOE, with DEUs in the industrial sector making up the majority—2,599 facilities consuming 50,570,115 TOE. The Vietnamese industry has significant potential for energy efficiency.
In the list of DEUs in 2023, there are 103 enterprises in the paper and pulp industry
By 2025, Vietnam requires 100% of designated energy-using enterprises to implement energy management systems as mandated by Decision 280/QD-TTG from the Prime Minister approving the National Program for Energy Efficiency for the 2019-2030 period.
The application of Energy Management Systems in Vietnam is still limited and weak. Many enterprises only implement these systems to meet legal requirements.

## Slide 4: Number of Designated Energy Users (DEUs)
Number of DEU and corresponding energy consumption, 2017-2021 (Source: Compiled from the DEUs List)
Number of DEUs
Energy using of DEUs (kTOE)
103 DEUs of paper and pulp

## Slide 5: EE targets for Vietnam's industrial sectors by 2030
Industries | By 2025 |  | By 2030 | 
 | From | To | From | To
Steel industry(%) | 3 | 10 | 5 | 16.5
Chemical industry(%) | 7 |  | 10 | 
Plastic manufacturing industry(%) | 18 | 22.46 | 21.55 | 24.81
Cement(%) | 7.5 |  | 10.89 | 
Textile and Garment(%) | 5 |  | 6.8 | 
Beverages and Beer(%) | 3 | 6.88 | 4.6 | 8.44
Paper and pulp (%) | 8 | 15.8 | 9.9 | 18.48

## Slide 6: Specific Energy consumption and Energy Savings Potential
C3 Energy efficiency scenario of the Vietnam Energy Outlook 2019 report

## Slide 7: Current status of energy use in industry
Proportion of energy consumption: The industrial sector accounts for about 47% of the total energy consumption in the country.
Industries with high energy consumption:
  The steel production, cement, textile, wood processing, and chemical industries.
  These industries consume approximately 70% of the total energy in the industrial sector.
Energy efficiency: Energy consumption efficiency remains low, with significant waste due to outdated technology and inefficient management.

## Slide 8: AVERAGE ELECTRICITY PRICE (2010 – 2024)
Chart: Graph of electricity price form 2009 to 2024
| Năm 2009 | Năm 2010 | Năm 2011 | Năm 2012 | Năm 2013 | Năm 2014 | Năm 2015 | Năm 2016 | Năm 2017 | Năm 2018 | Năm 2019 | Năm 2020 | Năm 2021 | Năm 2022 | Năm 2023 | Năm 2024
 | 948 | 1058 | 1242 | 1369 | 1508 | 1622 | 1622 | 1622 | 1622 | 1720 | 1864 | 1864 | 1864 | 1864 | 1920 | 2103
Electricity price comparison table of Vietnam with some countries in the world (Source: EVN 2022)
Electricity price of countries in the world
Converted to Vietnamese dong

## Slide 9: Causes of high energy consumption
Outdated technology: Many enterprises still use old technology such as: Conventional boilers, Old digesters (batch or non-continuous), Open headbox paper machines, Old refiners or beaters which consumes high amounts of energy and causes environmental pollution.
Lack of investment in innovation: Insufficient capital and motivation to invest in energy-efficient equipment and technology.
Low awareness of energy efficiency: Some enterprises have not prioritized energy efficiency measures in their production processes.

## Slide 10: Challenges in energy management and utilization
Technological challenges: Many enterprises use outdated technology, resulting in low energy performance and environmental pollution.
Cost challenges: The initial investment costs for energy-efficient technologies are high, causing many enterprises to hesitate to make changes.
Lack of strong supporting policies: Although there are policies encouraging energy efficiency, they are still not effective enough to drive widespread adoption of energy efficiency measures among enterprises.

## Slide 11: Trends in sustainable development in industry
Green industry: Enterprises are gradually paying more attention to using renewable energy and developing sustainable production.
International trend: Multinational corporations have higher standards for energy and environmental requirements when collaborating, especially in industries such as textiles and electronics.
Digital transformation and energy optimization: Applying digital technology to monitor and optimize energy usage in production.
New trends all place a certain emphasis on reducing greenhouse gas emissions in production and have become collaboration criteria for many major international corporations. This issue is becoming increasingly important and challenging for the industrial development of Vietnam.

## Slide 12
Paper and pulp industry in Vietnam

## Slide 13: Energy Intensity in Key Industries in Vietnam
Figure: Energy Intensity Improvement in Key Industries during VNEEP Phase 2 Changes of energy intensity in key industries

## Slide 14: Paper and pulp industry in Vietnam
Industry Overview:
• Global Ranking: Vietnam is among the top 10 largest paper-consuming countries in the world.
• Production Capacity: 5.3 million tons of paper per year.
• Paper Consumption in 2023: Over 5.9 million tons, with demand expected to grow further.
Product Segments:
• Printing and writing paper: 10%.
• Packaging paper: 75%.
• Other types (e.g., tissue, specialty paper): 15%.

## Slide 15: Paper and pulp industry in Vietnam
Production Status:
• Domestic Pulp Production: Approximately 1.2 million tons per year.
• Dependency on Imports: Over 60% of pulp demand is imported.
Raw Materials:
• Mainly derived from plantation wood (acacia, eucalyptus) and recycled paper.
• Limitations in natural raw materials and processing technology.

## Slide 16
Paper and pulp industry in Vietnam
Environmental Impact:
• Paper production consumes significant amounts of water and chemicals, causing water pollution.
• Solid waste from pulp production increases waste treatment pressures.
Market Trends:
• Growth in Packaging Industry: Driven by the e-commerce boom.
• Stable Demand: For tissue paper and printing paper.
Forecast:
• Average annual growth of 10% until 2030.
• Growth driven by domestic consumption and exports.

## Slide 17
Paper and pulp industry in Vietnam
Current Challenges:
• Many factories still use outdated, energy-intensive technologies.
• Automation levels remain low compared to developed countries.
Improvement Directions:
• Investment in Recycling Technologies: Enhance recycling efficiency and energy savings.
• Adopting Digitalization: Integrate digital tools into management and production processes.
Notes: There are a lot of old, small factories using the old Chinese technologies for the the yankee dryer have bad design and the vacuum pump working not so good for that the water content of raw material is very high at the beginning of the dryer. Instructor will talk about it in the class

## Slide 18: Energy Consumption in the Paper and Pulp Industry
The paper and pulp industry is among the highest energy-consuming sectors in manufacturing.
Primary Energy Sources:
• Electricity, coal, natural gas, and biomass energy.
• Significant energy consumption occurs during drying, pulp production, and machinery operation.
Key Energy Metrics:
• Average Energy Consumption: 18–30 GJ/ton of product, higher than in advanced countries. In Europen countries, the average is about 10.8 GJ/ton
• Electricity Costs: Account for 10–15% of total production costs.
• Thermal Energy Sources: Primarily coal and biomass energy for steam production.
• Efficiency: Energy efficiency remains low due to outdated technologies.

## Slide 19: Energy Consumption in the Paper and Pulp Industry
Key Energy-Consuming Processes:
• Pulp Production: Energy is used for grinding, cooking, and chemical processing.
• Paper Manufacturing: High energy demand during drying (steam and electricity).
• Auxiliary Systems: Air compressors, pumping systems, and wastewater treatment.
Energy Costs and Competitive Pressure:
• Energy Costs: Represent 15–20% of the total production cost of paper in Vietnam.
• Competition: Intense competition from countries with modern technologies, such as China and Japan.
Environmental Impact of Energy Consumption:
• CO2 Emissions: From the use of coal and oil in thermal energy production.
• Pollution: Air and water pollution from old boiler technologies.
• Environmental Standards: High pressure to meet international environmental regulations.

## Slide 20: EEMs in the Paper Industry - (1)
Internal Solutions:
Optimize production processes by upgrading equipment (boilers, air compressors).
Improve pipe insulation to reduce heat loss in steam lines.
Install variable frequency drives (VFDs) for energy-intensive machinery.
Renewable Energy Solutions:
Transition from coal to biomass or natural gas.
Use solar energy to power auxiliary systems.
Energy Recycling Technologies:
Recover waste heat from boilers for reuse.
Implement CHP (Combined Heat and Power) systems to simultaneously produce electricity and steam.

## Slide 21: EEMs in the Paper Industry – (2)
Automation:
Install an Energy Management System (EMS) to monitor and control energy use efficiently.
Apply digital technologies to optimize machinery operations.
Optimization of Boiler and Steam Systems:
Upgrade to high-efficiency boilers or replace with fluidized bed boilers using biomass energy.
Insulate steam pipelines to reduce heat loss.
Recover waste heat from boiler systems for reuse.
Recover high-pressure condensate for reuse.
Enhance feedwater quality and reduce boiler blowdown.
Use bark, paper sludge, and production waste as fuel.
Install biomass boilers to supply steam for production.

## Slide 22: EEMs in the Paper Industry – (3)
Energy Management System (EMS)
Applications:
• Install energy monitoring systems to measure and manage energy consumption in each production stage.
• Identify energy waste points early.
Benefits:
• Reduce energy consumption by 5-10% through stringent controls.
• Improve the operational efficiency of the entire production line.

## Slide 23: EEMs in the Paper Industry – (4)
Waste Heat Recovery
Solutions:
• Install heat recovery equipment to capture exhaust heat from boilers.
• Use recovered heat for paper drying or water heating in the pulping process.
Benefits:
• Increase energy utilization efficiency by 10-15%.
• Lower operating costs by utilizing surplus energy.

## Slide 24: EEMs in the Paper Industry – (5)
Enhanced Training and Awareness
Content:
• Train staff on energy-saving operational methods.
• Encourage improvement ideas from technical teams and workers.
• Conduct regular energy audits to identify improvement opportunities.
Benefits:
• Enhance energy management efficiency and reduce waste caused by operational errors.

## Slide 25: EEMs in the Paper Industry – (6)
Adopting Renewable Energy
Long-Term Solutions:
• Install solar energy systems on factory rooftops to supply power for auxiliary systems.
• Integrate renewable energy systems with the existing power grid.
Practical Examples:
• Some large paper mills in Vietnam have saved up to 20% on electricity costs by using solar energy.
Benefits:
• Reduce dependence on the national power grid and lower production costs.

## Slide 26: EEMs in the Paper Industry in the world
Electric air heating
Technology description
Traditionally, pulp is dried using superheated steam generated from fossil fuel sources. However, using resistive heating to warm air means that renewable electricity can be used, thus reducing associated emissions. Additionally, the significant power demand can be managed by power controllers to minimise load disruption on electricity grid.

## Slide 27: EEMs in the Paper Industry in the world
Electric air heating
Other projects
Finland: UPM Electric boiler: Paper mill company, UPM, will install 8 electric boilers in German and Finnish mills in 2023 in line with their hopes to reduce CO2 emissions from fuels by 65% by 2030.
Source: https://www.packaging-gateway.com/news/upm-eight-electric-boilers-mills/
Norway: Vafos pulp electric heating: Vafos, a Norwegian Pulp company partnered with ABB in 2022 to replace oil-fuelled boilers with electric air heaters which are controlled by power controllers to minimise the effect on the grid.
Source:https://new.abb.com/news/detail/91305/pulp-plant-decarbonizes-by-switching-to-electric-drying
The new boilers will increase mill capacity and lower emissions. Credit: Tomi Mäkitalo/commons.wikimedia.org.

## Slide 28: Discuss
Which EEMs do you believe have the potential to be implemented within your organization? What steps would you need to take to implement this EEM?

## Slide 29
THANK YOU