## Slide 1
Module 8.4:
Typical energy efficiency measures in the paper and pulp production line.
TRAINING PROGGRAM FOR INDUSTRIAL ENTERPRISES
Technical staff

## Slide 2: Content
The typical energy efficiency measures (EEMs) in the paper and pulp production line is presented including:
EEMs in preliminary treatment
EEMs in chemical paper production
EEMs in mechanical pulp production
EEMs in paper production

## Slide 3: I. EEMs in preliminary treatment (1)
For example. - Replacing pneumatic conveyors with belt conveyors
Pneumatic conveyor:
Motor efficiency
Drive system efficiency
Air transmission system efficiency
Product loss
Belt conveyor:
Motor
Drive system efficiency
Energy savings of 80-95 %, wood chips 1-2 %
Maintenance costs can be significantly higher

## Slide 4
Example – Unloading wood chips and automatic thickness checking:
Screening:
  Screen by thickness
  Jet Screen
  OPTI
  Gyratory screen
  CSCS gyratory chip screen (4 sizes)
  SCL gyratory chip screen (3 sizes)
Results:
  Reduced cooking energy
  Increased paper pulp yield
  Increased by-product yield
  Less wood chip damage
  Handling of non-conforming wood chip pieces
  HQ-sizer (oversized and too thick)
  Reconfigure the chip structure using Chip Optimizer (oversized and too thick)
  Re-cutter (for oversized wood chips only)
  Other types:
  Disc screen
      I. EEMs in preliminary treatment (2)

## Slide 5
Wood Chip Screening Mesh (Panel Type) Benefits:
Long lifespan
Low maintenance cost
Low energy consumption
Increased productivity in wood pulping
What is important?
Low amount of wood chips that are too thick being transferred
Low amount of oversized wood chips being transferred
Maintenance performance with changes in speed and size
Consistent performance over time
No damage from wood chips
Reduced wear on the screen surface
      I. EEMs in preliminary treatment (3)

## Slide 6: I. EEMs in preliminary treatment (4)
Wood Chip Conditioning – Oversized Wood Chips In the past:
Thin slicing machines and re-cutting machines were used. These machines had drawbacks – they created splinters and pins.
Typical wood chip cutting machines can produce up to 15% pins along with 2%-8% splinters, depending on the cutting conditions, moisture content, and machine load. Common re-cutting machines can produce even higher rates of splinters.
Pyramid Wood Chip Conditioning
Creates cracks along the splintered wood chips
Increases the surface area
Enhances solution permeability
Reduces splinter production

## Slide 7: II. EEMs in chemical paper production (1)
Kraft Pulp Production – Using Pulping Additives to Increase Productivity Pulping additives:
Enhance solution permeability
Improve cooking balance
Reduce cooking time
Benefits:
Increase pulp production (reduce pulp discard)
Reduce energy consumption (36 kWh per ton of wood)
Reduce input raw materials
Improve productivity
Reduce bleaching chemicals
Reduce sulfur emissions

## Slide 8: II. EEMs in chemical paper production (2)
Kraft Pulp Production – Optimizing the Control of the Dilution Factor
Minimize the dilution of black liquor
Reduce the average amount of water evaporated from diluted black liquor
Optimization through:
Control the water flow from the shower in the final washing stage to optimal levels by:
  Considering steam costs
  Bleaching chemical costs
  Impact on wastewater quality
  Other variable parameters

## Slide 9: II. EEMs in chemical paper production (3)
The pulping digester is known as a crucial component in the pulp grinding process flow because it requires 5% to 50% of the online operating time, making this part of the pulping process require a significant capital investment.
Improving the performance of the digester can significantly reduce losses during production, operating costs, and negative environmental impacts, while increasing paper yield and quality.
Using computer-based models and control systems for continuous digesters can regulate the grinding process, thus minimizing machine downtime caused by digester issues and facilitating continuous pulp production and operation.
Kraft Pulp Production – Continuous Cooking Vessel Control System

## Slide 10: II. EEMs in chemical paper production (4)
Kraft Pulp Production – Conversion of Batch Digesters
Batch digesters are suitable for a variety of products.
Use indirect heat and cold discharge
Use indirect steam instead of direct steam
Heat is recovered from the remaining liquor
  Pre-steam wood chips
  Preheat white liquor
  Preheat water used in the process

## Slide 11: II. EEMs in chemical paper production (5)
Kraft Pulp Production – Digester Discharge/Pressure Relief Heat Recovery
Reducing the pressure in the digester generates steam that can be used for:
Steaming wood chips – there are two methods:
Pressure relief from the first stage is commonly used to heat wood chips in the steaming vessel
Pressure relief from the second stage can be used as a substitute for direct steam in the wood chip digester
Heating water at the production facility
Evaporating black liquor, which is used as thermal energy in multi-stage evaporation equipment

## Slide 12: II. EEMs in chemical paper production (6)
Kraft Pulp Production – Digester Discharge/Pressure Relief Heat Recovery
Reducing the pressure in the digester generates steam that can be used for:
Steaming wood chips – there are two methods:

## Slide 13: II. EEMs in chemical paper production (7)
Bleaching – Heat Recovery from the Bleaching Plant's Wastewater
The wastewater from the bleaching plant can contain a significant amount of heat, and it would be wasteful to discharge this water without recovering the heat. Heat exchangers can be installed to recover some of this heat for other useful processes around the plant, including hot water heating.
Bleaching
Recovery

## Slide 14: II. EEMs in chemical paper production (8)
Bleaching– Improving brown liquor washing technology.
Traditional brown liquor washing technology consists of a series of 3 to 4 washing drums, where a fiber pad under vacuum pressure is sprayed with water to dissolve solids. Modern washing systems replace vacuum pressure units with vacuum diffusion or wash press machines. These systems are more efficient in removing solids;
They require less electricity or steam
Reduce bleaching chemicals
Notably, wash presses have proven to improve efficiency and are becoming increasingly popular in the paper industry.

## Slide 15: II. EEMs in chemical paper production (9)
Bleeching– Heat exchange by Chlorine dioxide
ClO2 solution is typically chilled to maximize ClO2 concentration before being used in the bleaching plant. However, heating ClO2 before mixing it into the mixture reduces the need for steam in the bleaching plant, making it an important energy conservation method. Preheating can be done by using secondary heat sources with the installation of heat exchangers in the ClO2 supply circuit.
Bleach
Pre-heat

## Slide 16: II. EEMs in chemical paper production (10)
Bleaching – Other Methods
Extended cooking
Preliminary wood removal using oxygen
Ozone bleaching
Oxidation recovery in the direct alkali recovery system
Biological bleaching
Wash press machines

## Slide 17: II. EEMs in chemical paper production (11)
Recovery of Chemicals - Concentration of Solids in Black Liquor
The black liquor concentrator is designed to increase the solid content of black liquor before it is burned in the recovery boiler.
Increasing the solid content means less water evaporates in the recovery boiler, which can significantly improve the efficiency of the steam generation process.
Currently, there are two types of black liquor concentrators: the submerged tube concentrator and the falling film concentrator.

## Slide 18: II. EEMs in chemical paper production (12)
Recovery of Chemicals– Finished Composite Tubes for Recovery Boilers
Recovery boilers, which have carbon steel tubes for steam generation, are often severely corroded and frequently fail. This has led to the need to find more advanced alloys to produce these tubes.
Research has resulted in the development of a new welding coating for cast-extruded alloy tubes. These advanced alloys allow us to use black liquor with higher dry solid content, thereby increasing the thermal efficiency of the boiler and reducing the frequency of boiler shutdowns.

## Slide 19: II. EEMs in chemical paper production (13)
Chemical Recovery – Monitoring Fouling in Recovery Boilers
Controlling fouling on the heat transfer surfaces in recovery boilers can improve machine operational efficiency, reduce downtime, and create more flexible shutdown schedules.
A handheld infrared monitoring system has been developed to detect early signs of faulty components and slag formation, preventing damage from impact and allowing for cleaner cleaning before the fouling solidifies.
This system is said to provide clear images of areas inside the boiler that accumulate dirt and allows for inspection of any area within the combustion chamber.
Benefits:
  Increased thermal efficiency
  Improved boiler productivity
  Reduced boiler shutdowns and gas emissions
  Enhanced safety for the boiler

## Slide 20: II. EEMs in chemical paper production (1)
Chemical Recovery – Four-Stage Air Injection
Many recovery boilers have a three-stage air injection system but use the third stage sparingly.
By fully utilizing the third stage and adding a fourth air injection port, the transition of gas and fouling in the pipes are reduced.
This can reduce the frequency of recovery boiler cleaning, thereby saving energy by decreasing the number of boiler shutdowns and reheating cycles.

## Slide 21: III. EEMs in mechanical pulp production (1)
Mechanical Pulp Production
Mechanical Pulp Production is the oldest method of pulp production. This process uses mechanical energy to weaken and separate fibers from wood and waste paper through a grinding process.
The advantage of mechanical pulp production is that it produces higher yields compared to chemical pulp production (up to 95%). However, because this process does not break down the wood, the fiber strength and pulp durability are lower.
The weakness of the paper becomes more severe because the mechanical grinding process also produces shorter fibers. As a result, most mechanical pulp is typically used for low-quality papers such as newspapers, magazines, and catalogs. The mechanical pulp production method requires more careful screening of materials to remove impurities like dust, debris, and wood chips compared to chemical pulp production.
  Pulp Production by Grinding Method
  Pulp Production by pulp grinding machine
  Thermo-Mechanical Pulping (TMP)
  Chemithermomechanical Pulping (CTMP)

## Slide 22: III. EEMs in mechanical pulp production (2)
Mechanical Pulp Production – Continuous Pulping Aids
The continuous pulping aid process for commercially purchased pulp involves mixing dry pulp ingredients with water in a large tank to produce a fibrous paper slurry
Usually, this process is carried out in batches, however switching to a continuous process can result in energy savings due to improved process efficiency. Energy savings of up to 40% can be achieved by reducing requirement to use grinding aid motor power.

## Slide 23: III. EEMs in mechanical pulp production (3)
Mechanical Pulp Production – Efficient Continuous Grinding Aid Impeller
The impeller design of the new grinding aid machine has been optimized for energy consumption by using computational fluid dynamics simulations to study the interaction between the impeller and the paper slurry. According to reports, replacing an existing impeller with a newly optimized impeller can reduce impeller motor consumption anywhere from 10% to 30%.

## Slide 24: III. EEMs in mechanical pulp production (4)
Mechanical Pulp Production – Drum Pulper
The drum pulper allows mills to produce pulp from recycled paper and packaging paper products.
The drum pulper is a rotating, inclined drum with a separating screen used to mix recycled paper fibers, water, and deinking chemicals. The machine's lighter mechanical action allows the contaminants to remain intact during the fiber separation process.
The drum pulper consumes less energy compared to traditional mechanical pulping machines, uses less water, and reduces fiber breakage.

## Slide 25: III. EEMs in mechanical pulp production (5)
Mechanical Pulp Production – Heat Recovery from Deinking Waste
The deinking wastewater is typically discharged at a heated temperature and serves as a low-grade heat recovery source at a pulp mill that processes recycled paper fibers.
Installing heat exchangers in the wastewater circuit can recover some of the heat for useful purposes, such as heating water at the production facility.
For example, a paper mill that produces newsprint and specialty paper products from three paper machines uses approximately 60% recycled fiber from old newspapers and magazines as raw material. The mill’s wastewater stream has a temperature of about 48°C with a flow rate of m³/h. A heat exchanger system would provide warm, filtered water for the mill’s paper machines, helping to offset a portion of the mill’s steam demand.

## Slide 26: III. EEMs in mechanical pulp production (6)
Mechanical Pulp Production – Heat Recovery in the TMP Process
A large amount of steam is generated as a byproduct of the thermo-mechanical pulping process. This low-pressure steam is often contaminated; however, most of the energy can be reused for other processes in the mill through heat recovery equipment. Heat recovery methods include:
  Compressing the steam mechanically or at integrated mills, where clean steam is produced and can be used in the drying section of the paper machine.
  Direct-contact heat exchangers that generate hot water for the paper machine and provide additional water for the boiler and clean steam used in other processes.
  Boilers to produce clean steam for use in various processes.
  Other equipment in the compression system where water is heated and systems such as the cyclotherm heat pump system.

## Slide 27: III. EEMs in mechanical pulp production (7)
Mechanical Pulp Production – Heat Recovery in the TMP Process
The TMP (Thermo-Mechanical Pulping) heat recovery process is applied to any mill that uses pressure ground pulp and currently does not have a heat recovery system in place (usually older mills, since most modern TMP mills are designed with heat recovery systems).
A typical heat recovery system for a pressure ground pulp mill can generate 1.1 to 1.9 tons of clean steam at the dryer for each ton of pulp.

## Slide 28: III. EEMs in mechanical pulp production (8)
Mechanical Pulp Production – Other Methods
Enhanced use of recycled pulp
Pulp production by thermo-mechanical method
Pulp production using the RTS process
Recycled paper fiber separation

## Slide 29: IV. EEMs in paper production (1)
Paper Production:
Based on experience:
  The energy required in the pressing section is four times that of the forming section.
  The energy required in the drying section is 25 times that of the forming section.

## Slide 30: IV. EEMs in paper production (2)
Wet press section

## Slide 31: IV. EEMs in paper production (3)
Moistening Section – Optimizing the Water Removal Process in the Forming and Pressing Sections
In older paper machines:
  There are too many high vacuum sections that unnecessarily add vacuum operating energy.
  This increases the load on the forming fiber and related driving forces.
  Reduces re-wetting:
  Use appropriate felts for each layer of paper produced.
  Optimize the path of the paper web and felt so that the two paths separate as early as possible.
Pressing:
  Maximize the nip pressure within the design limits.
  Optimize the roll wrapping of surface patterns.
  Felt design.
  Minimize the reduction in temperature.

## Slide 32: IV. EEMs in paper production (4)
Moistening Section – Preheating Steam Boxes
Typically, a steam box is installed to increase the temperature of the wet paper web before pressing, which reduces the viscosity of the water and allows the paper web to dry more easily.
Afterward, the steam box allows the paper machine to operate at the highest speed or consume less energy. The steam box uses energy in the form of steam, but the energy savings in the drying section will be much higher.
The additional steam increases the temperature and viscosity.
The energy savings are equivalent to the amount of water that will no longer evaporate.

## Slide 33: V. EEMs in the paper industry (1)
Moisturizing and De-watering Section in the Pressing Unit De-watering in paper mills is carried out by increasing the nip pressure and using uniform nip pressure across the width. To ensure the efficient use of the equipment's functions, full maintenance, repair, and modification activities must be provided at all times. Careful daily control is necessary to ensure that the press felt is sufficiently resilient to achieve full suction force.
W = (Pw-Dm) / (1-PW)
W: It is the value of the amount of moisture evaporated from 1 kg of dm of paper [ kg ]
Dm: It is the moisture content of the paper roll at the drying section tube [%]
Pw: It is the moisture content of the paper roll at the press guide tube [%].
The table displays the moisture evaporated from Pw % of the wet paper when producing 1 kg of paper, where the paper moisture at the end of the dryer (Dm) is 5% or 10%."
Pw % |  | 65 | 64 | 63 | 62 | 61 | 60 | 59 | 58 | 57 | 56 | 55
W (kg) | Paper moisture: 5 % (Dm) | 1,71 | 1.64 | 1.57 | 1.50 | 1.44 | 1.38 | 1.32 | 1.26 | 1.21 | 1.16 | 1.11
 | Paper moisture: 10% (Dm) | 1.67 | 1.50 | 1.43 | 1.37 | 1.31 | 1.25 | 1.20 | 1.14 | 1.09 | 1.05 | 1.00

## Slide 34: V. EEMs in the paper industry (2)
Drying Section
Water needs to be removed from the paper, and after the pressing section, the only way to remove water is through evaporation. Evaporating water requires a lot of energy, but it is the only method.
It is important to observe how the water evaporates and ensure that the equipment operates in optimal conditions.
There are three main positions in the drying section when we considering the level of energy consumption. These are the heating and processing position, the position for consuming water and steam, and the direct heating position.

## Slide 35: V. EEMs in the paper industry (3)
Drying Section – Reducing and Reusing Humid Air
The water evaporated from the paper web is removed by the dissolving air. At certain points, the air becomes saturated with water and can no longer carry more moisture, requiring a switch to fresh air. The physical properties of the air, such as its solubility, increase with temperature.
The most important aspect is that the temperature of the outgoing air is exchanged with the incoming air. This heat exchange operation is typically installed in all systems and is considered a standard. The efficiency of the exchange can vary, so it is necessary to check.
Additionally, it is important to use the full drying capacity of the air before it is released into the surrounding environment. The drying capacity of the air depends on relative humidity, not specifically; the drying power of the air also depends on temperature. The general idea is to measure the relative humidity, and if the relative humidity is low, we need to return to the process of introducing air into the drying section.

## Slide 36: V. EEMs in the paper industry (4)
Drying Section – Heat Recovery from Exhaust Pipe System
In a paper production plant, there can be many different sources of hot air exiting the exhaust pipes. This hot air contains a significant amount of energy that can be reused in the paper production processes, leading to energy savings and increased production efficiency. The first step in reusing this energy is to consider whether heat can be transferred directly between the outgoing air stream and the incoming new air stream. After this possibility is used as much as possible, the next step is to look into utilizing secondary thermal energy.
The most common method is to channel the air through water heat exchangers in the hot air pipes. In this way, a lot of thermal energy can be transferred to a secondary water pipe or other lower-temperature water sources. Another approach is to reheat the water, increasing the overall temperature on the paper machine.
The hot air left in the production process is often very humid and contains a lot of latent energy in the form of water. If the water condenses, much of this energy can be recovered. Typically, this situation occurs at low temperatures and is difficult to dissipate. A possible solution is to use a heat pump to raise the temperature, but further calculations and scientific applications are required.

## Slide 37: V. EEMs in the paper industry (5)
Drying Section – Using an Air Drying Machine by Impact Method
The process of drying air by the impact method involves blowing hot air (300°C) at high speed onto damp sheets of paper through a gas burner. The air drying process by impact results in less steam usage and slightly higher electricity consumption. This technology is mainly applied to dry coatings but is also accepted for general paper drying, replacing traditional steam cylinders.
In practice, this method involves balancing the use of thermal and electrical energy, and this balance can vary through settings, so energy savings need to be determined based on each facility.

## Slide 38: V. EEMs in the paper industry (6)
Drying Section – Using CondeBelt Dryer (CJ)
The first commercial CondeBelt dryer was installed in Finland in 1996 and in South Korea in 1999. In the CondeBelt dryer, paper is dried in a drying chamber by continuous contact with a hot steel belt, which is heated either by steam or hot gas. The moisture from the paper evaporates due to the heat from this metal belt.
This drying technology has the potential to completely replace the drying section in a typical paper mill, with a drying speed 5-15 times higher than that of conventional steam dryers. However, the CondeBelt dryer is not suitable for high-weight paper and has limited use in that regard.

## Slide 39: V. EEMs in the paper industry (7)
Drying Section – Optimizing Ventilation Temperature in the cavity
To dry paper effectively, it is crucial to remove the moisture around the paper rolls to enhance the evaporation driving force.
When increasing the surface temperature of the cylinder, it is not necessary to improve the water removal rate during the drying process. When water evaporates from the paper web, it must be removed from the drying section by sufficiently hot dry air.
When water evaporates from the paper web, it must be removed from the drying section by sufficiently hot dry air.
Functions of ventilation:
Collect and remove evaporated water from the drying section.
Create a favorable and controlled environment during the drying process.
Improve energy use and save energy during drying.
Enhance machine operation not only through the system's equipment but also by appropriately distributing and controlling the amount of steam used throughout the entire drying section.
Maintain working conditions in the machine room with good temperature, humidity, and noise levels.
Protect the building and machinery from damage caused by moisture.
Reduce emissions and mist outside the factory.

## Slide 40: V. EEMs in the paper industry (8)
Drying Section – Multi-Stage Press System
The multi-stage press system can be classified as a heat recovery system because the heat flow passes through, and the short steam generated at the time of reheating the dryer, or it belongs to a group of drying sections used again to heat the dryer.
The multi-stage press system operates by moving from the dry end to the wet end with different pressures in the heating system.
The paper drying process starts at low temperature in the pre-drying section, where the paper is gently heated. The drying process increases as water evaporates toward the dry end of the paper machine. In the dryer, steam condenses on the inner surface of the dryer. The condensed water is then returned to the separator.
To remove the condensed water, the pressure in the separator must be close to the pressure of the direct steam. In the separator, the air through the steam is reduced during the second drying stage in the multi-stage press system. The separator expels the steam, which is then released into the drying stage—new windows in the multi-stage press system.
In the second stage, the short steam is used as a drying medium. If the amount of steam is insufficient to meet the direct requirements, it can be supplemented by the second pressure control valve.

## Slide 41: V. EEMs in the paper industry (9)
Drying Section – Multi-Stage Press System

## Slide 42: V. EEMs in the paper industry (10)
Drying Section – Multi-Stage Press System
Using Heat Compressors:
Using heat compressors will increases energy efficiency in the drying process due to the reduced water vapor at the condensers. Heat compressors are used to increase the pressure of the exhaust steam from the separation devices.
The exhaust steam from the final devices in the system condenses, and the incoming water vapor has a very low pressure that cannot be directly used in the drying process.
With the steam heat compressor, this waste water is pushed to a higher pressure, reaching a level that allows the recovery of waste water for reuse in the drying process. The diagram next to this text illustrates the integrated principles of the heat compressor.

## Slide 43: V. EEMs in the paper industry (11)
Drying Section - Others
Reduce air requirements
Create void shapes
Optimize the vacuum system
Lack of clean drying surfaces
Other methods to recover waste heat

## Slide 44: DISCUSSION
If the steam consumption for drying has increased abnormally over the past week, what technical causes do you think could be responsible? How would you check and fix it?
Divide the class into 3–4 groups. Each group selects one area to analyze:
Example:
Group 1: Check the press felt
Group 2: Inspect steam traps
Group 3: Review steam cylinder pressure control
Record your group’s discussion in the following table:
Present your findings after 10 minutes of discussion.
Test location | Unusal signs | Proposed solution
… | … | …

## Slide 45: V. EEMs in the paper industry (12)
      Control System – Advanced Dryer Control
      The control system is a well-known method for optimizing changes in the paper production process, thereby reducing energy consumption, increasing productivity, and improving the quality of the industrial process.
      An example of a control system for dryers is the Dryer Management System™ software, which provides advanced control for the dryer system setup and process parameters to reduce steam usage and increase productivity.

## Slide 46: V. EEMs in the paper industry (13)
Control System – Condensation Point Control
The condensation point of the steam (in the dryer) determines the heat exchange efficiency, but it is affected by the setup of the ventilation fans.
The condensation point in paper dryers should be measured and controlled to optimize the drying process. Optimizing dryer operation helps better control quality, making the product more consistent.
Example:
Condensing equipment has helped a company control the addition rate when recycling steam to improve energy efficiency. The resulting effects include improved performance of the heating unit and better product quality due to reduced dripping in the hood.
The company uses manual control, but it is clear that the operators often do not have enough time to make timely adjustments to the steam recycling/addition rate under fluctuating conditions (such as weather effects). When the machine's capacity reaches the limit, and the hood reaches its maximum capacity, it often increases the amount of water condensation and moisture in the hood.
Condensed water droplets falling onto the paper running at 3,800 FPM around the drying section can cause product defects – weak points on the paper, holes, tears, and the cost of machine downtime. Before installing dew point sensors, the mill usually maintained a high supplemental steam flow into the dryer to eliminate the condensation in the drying equipment, which is an energy-wasting method.

## Slide 47: V. EEMs in the paper industry (14)
Control System – Reducing Air Blow Losses by Maintaining Pressure Differential As mentioned in the previous section, air blow losses can be recovered in a multi-stage press system. To optimize the use of the multi-stage press system, it is important that each component of the system is balanced. In the example below, two groups of dryers are balanced.
The balance between the two systems is created by the pressure control valve. The pressure in the condensation chamber will be lower than the pressure of the pressure valve.

## Slide 48: V. EEMs in the paper industry (15)
Control System – Reducing Air Blow Losses by Maintaining Pressure Differential
Other Controlling Factors That Can Affect the Control (Maintaining Pressure Differential) of the Multi-Stage Press System
Paper Shutdown: Condensation in the dryers immediately decreases because the dryers are no longer being cooled by the paper. If there is no condensation, nothing flows through the system, meaning steam consumption drops immediately after the paper is shut down.
Waterlogged Dryer: Due to incorrect adjustments by the operators in the process control system, measurement and control technology errors, or damage to the drainage components or steam joints, the pressure differential decreases. Then, condensation in the dryer cylinder increases and floods the siphon tube base. This can also happen if the drainage system is not designed correctly or if the size measurements do not correspond to the actual steam requirements. If the siphon tube or siphon tube base is too small, the condensate cannot be fully drained.
Heating the Paper Machine: To heat the paper machine, only a small amount of steam is needed, and the conditions are similar to the paper shutdown case.

## Slide 49: V. EEMs in the paper industry (16)
Control System – Reducing Machine Downtime
There are several ways to reduce machine downtime in the paper industry. This section describes the most important examples. Machine downtime increases specific energy consumption, labor costs, product loss, reduced output, etc.
The following cases are chosen as examples of what causes machine downtime:
  Paper Shutdown: Paper shutdown can be caused by impurities (described in more detail in the next section), inconsistent paper fibers in the stock container, poor dewatering and drying system performance, etc.
  Impurities: Debris, sand, plastic, sludge, and residues are identified as impurities. In paper production, the pulping process, material preprocessing, and papermaking processes must be equipped with impurity removal devices. Impurities can cause paper shutdowns, increase drying time, reduce quality, and damage equipment.
  Changes in Production

## Slide 50: V. EEMs in the paper industry (17)
Water Conservation
There is a close relationship between energy consumption and water in the paper and pulp industry, which is why this curriculum has a separate section on water.
Water production
Fiber reuse
Heat recovery
Etc.

## Slide 51: V. EEMs in the paper industry (18)
Water Saving – Efficient Use of White Water
White water belongs to resources.
The electric energy used to pump up, operate the pulp mixer and refiner is converted into heat energy, and is stored in the system, where the system temperature increases. Then, the heat energy is used to adjust the steam. The white water separated by the concentrator and the paper machine wire contains fiber and additives, which can be reused as raw materials.
Key points for white water reuse
The quality and production requirements are different for each mill, so the properties, distribution and fractionation of temperature, concentration, pH value, fiber, additives, etc. are also different. The recovered material, the use of white water, the quality of the product after use, the production requirements for fiber must be studied based on the current analysis value, settling test and filtration test. Based on the results of this study, establish flow schedules and material and water balances. Improvements to existing equipment and introduction of new equipment should be determined by careful study, taking into account operator input.

## Slide 52: V. EEMs in the paper industry (19)
Water Conservation – Other Measures
Strategic water management program
Good internal management
Cooling towers
Reduce water discharge from cooling towers
Reuse once-through cooling water
Reduce faucet water usage
Use water-efficient equipment
Optimize faucet water use
Water-efficient bleaching
Closed water conservation with vacuum pumps
Direct reuse of white water
Seal mechanical pumps
Chemical washing (conveyor belt)
Washing black liquor with CO2

## Slide 53: V. EEMs in the paper industry (20)
Emerging Technologies for Energy Efficiency
Gasification of black liquor
The speed-adjustable motor is coupled magnetically.
Laser-ultrasonic paper pulp consistency sensors
Steam cycle washers for unbleached pulp
Microwave wood pulping
Gas-fired paper dryers
High-performance fiber additives
Biological treatment

## Slide 54: V. EEMs in the paper industry (21)
Emerging Technologies for Energy Efficiency
Electro-hydraulic pollution removal
Two-side wave forming machine
Multi-port dryer
Pulping with green-oriented solution
Impulse drying

## Slide 55: DISCUSSION
1. If you are assigned to assess the production line at your current factory, which area would you choose to start evaluating energy-saving opportunities – and why? In your opinion, what are 3 priority actions that can be implemented immediately?
2. Each group selects one key area in the production line (Boiler / Paper machine / Pressing & Drying / Motor – Fan / Compressed air system). Identify:
Where could energy losses occur?
What technical indicators should be monitored?
What 3 immediate actions could be taken?
Discussion time: 10–15 minutes Group presentation: 3 minutes per group

## Slide 56
THANK YOU