## Slide 1: TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs
Module 7.6:
Introducing the characteristics of the technological line in the Textile Industry.
TECHNICAL STAFF

## Slide 2: Content
Introduction to the textile industry Characteristics of yarn production and spinning Characteristics of the textile industry

## Slide 3
Introduction to the textile industry

## Slide 4: OVERVIEW OF TEXTILE SECTOR
The textile and garment industry is one of the key manufacturing sectors and a major contributor to the national economy, currently ranking second in the world in terms of export value, only after China.
Number of companies in the industry: approximately 7,000
Number of workers: around 3 million
Textile and garment export turnover in 2024: USD 44 billion. The United States is the largest export market for the industry, followed by Japan, the EU, South Korea, China, and ASEAN countries.
The textile and garment industry consumes large amounts of natural resources such as water, energy, and chemicals. According to the list of key energy-using facilities in 2023, the textile and garment sector accounts for:
7% of total DEUs nationwide, of which 53% are fibre production enterprises, 22% are garment enterprises, and 25 are dyeing and finishing enterprises
Approximately 5% of total energy consumption among all DEUs
Notes: PowerPoint Presentation STK-Ban-tin-IR-ky-39-Q3-9M2024-vie.pdf Ngành Dệt May năm 2024: Xuất khẩu ước đạt 44 tỷ USD, nhiều thách thức trong chuyển đổi xanh Tầm Quan Trọng Của Ngành Dệt May Việt Nam Trong Nền Kinh Tế Xanh

## Slide 5: TEXTILE VALUE CHAIN
The value chain of Vietnam’s textile and garment industry consists of three main segments:
Spinning (fiber production)
Weaving and dyeing
Garment manufacturing

## Slide 6: TEXTILE VALUE CHAIN
 | PRODUCTION OF RAW FIBRES |  | YARN PRODUCTION | GREY CLOTH PRODUCTION | TEXTILE FINISHING | MAKING UP
Process steps | Production of Natural fibers | Production of man-made fibers | Spinning, Twisting | Weaving Knitting | Pre-treatment Dyeing Printing Finishing | Cutting Assembly Finishing Packing
Relevant environmental effects | Land use Pesticide Preservatives Warer demand | Waste water pollution Air emission Poorly biodegradable texile auxiliaries | Textile auxiliaries and chemicals use Fibre waste Noise pollution Dust emissions | Textile auxiliaries and chemicals use Noise pollution Dust emissions Waste Poorly biodegradable textile auxiliaries | Water demand Waste water pollution Textile auxiliaries Chemicals use Air emissions, Energy demand | Energy demand Waste

## Slide 7: Sơ đồ quy trình từ Sợi đến sản phẩm may mặc
Sắp xếp và mô tả từng công đoạn trong quy trình từ Sợi đến sản phẩm may mặc:
May
Vải đã xử lý
Vận chuyển & giao hàng
Sợi
Kiểm tra & Sửa lỗi
Gia công giá trị
Là (ủi) & đóng gói
Thiết kế rập & Cắt vải
Sợi thô
Vải thô
Xử lý vải
Thành phẩm

## Slide 8: FLOWCHART FROM FIBRE TO GARMENT PRODUCT
Raw fibre
Yarn
Raw fabric
Fabric processing
Processed fabric
Pattern & Cutting
Value addition
Sewing
Finished product
Ironing & packing
Dispatch and delivery
Harvesting and processing natural fibres (cotton, flax)
Spinning
Weaving or knitting fabric
Creating patterns and cutting fabric according to product design
Assembling using industrial sewing machines
Stitching hems, attaching zippers, buttons, etc
Checking & Rework
Labelling and packaging the product
Distribution to stores/export
Dyeing and printing patterns
Embroidery, printing or decorating to enhance aesthetics
Ironing the product
Finishing fabric to meet technical requirements
Woven fabric
Knitting fabric
Yarn treatment
Twisting
Producting synthetic fibres

## Slide 9: ENERGY CONSUMPTION LEVELS IN DIFFERENT STAGES OF THE TEXTILE AND GARMENT INDUSTRY
Textile sector | Electrical energy (kWh/kg) | Fuel (HO) , L/kg
Spinning | 3,6 – 3,8 | -
Knitting | 0,3 – 0,4 | -
Weaving | 2 – 2,2 | 0,02 – 0,03
Dyeing & Finishing | 1,6 – 1,7 | 0,6 – 1
Clothing M/fing | 0,8 – 1 | 0,1 – 0,2
Source: Energy saving stragies in textile industry – the case study of Mauritius

## Slide 10
II.
Characteristics of yarn production and spinning

## Slide 11: YARN PRODUCTION

## Slide 12: YARN PRODUCTION
Raw materials such as cotton and polyester are mainly imported from countries like Australia, the United States, Brazil, etc.
Production process: Fibers and cotton are spun into natural yarn by textile and spinning mills. The remaining type of yarn is synthetic yarn, which is created through petrochemical processes using raw materials such as oil and gas.
Vietnam is the 6th largest exporter of fibers and yarns in the world

## Slide 13: YARN PRODUCTION (AKA SPINNING)
QC 1
QC 2
QC 3
Saleable Waste
Contamination
Dust
Short Cotton fibre
W A S T E
Cotton Bales
Laps
Saleable Waste
Contamination
Dust
Short Cotton fibre
W A S T E
Saleable Waste
Contamination
Dust
Short Cotton fibre
W AS TE
Reusable Waste
Short Fibre Cotton
Used in other processes
QC 4
Reusable Waste
Handling waste (Cotton fibre)
W A S T E
Saleable Waste
Lickerin Waste
Imputities
Short fibre & fibre Neps
Dust
Sliver
Blended
Beat Cotton
Energy: 264 kWh
Energy: 141 kWh
Source: Material Flow Cost Accounting of a Spinning Mill by Espire Consult
QC 1 Mixing, Plucking, Blending
QC 2 Multimix, Beating
QC 3 Sorting, Beating, Scutcher
QC 4 Carding
QC 5 Breaker Drawing
QC 6 Finisher Drawing
QC 7 Simplex
QC 8 Ring
QC 9 Auto Cone
Example Material Flow Chart

## Slide 14: YARN PRODUCTION (AKA SPINNING)
Material Waste
Short Fiber
Material Waste
Short Fiber
Material Waste
Short Fiber
Drawing Sliver
QC 5
QC 6
QC 7
W A S T
E
W A S T
E
W A S T
E
Energy: 317 kWh
Drawing Sliver
Roving
Material Waste
Pneumafil
Yarn Loss (mishandling)
Material Waste
Faulty Yarn
Bobbin
QC 8
QC 9
W A S T
E
W A S T
E
Cones
Inventory
Energy :952 kWh
Energy :257 kWh
Source: Material Flow Cost Accounting of a Spinning Mill by Espire Consult
Example Material Flow Chart
QC 1 Mixing, Plucking, Blending
QC 2 Multimix, Beating
QC 3 Sorting, Beating, Scutcher
QC 4 Carding
QC 5 Breaker Drawing
QC 6 Finisher Drawing
QC 7 Simplex
QC 8 Ring
QC 9 Auto Cone

## Slide 15: TEXTILE PROCESS – COTTON FIBER
Two popular technologies for the production of cotton yarns:
  Producing pile yarns (CD)
  Producing OE yarns
The quality of the yarn output depends largely on the input materials (70% of raw materials from cotton).
Machinery and equipment have the effect of minimizing breakage fibers in the production process, accordingly. As new and modern, the lower the fiber error rate.
Cotton
Opening, blending and carding
Sliver formation
Roving
Bobbin winding
Heat setting
CD yarn
Cotton
Opening, blending and carding
Sliver formation
OE spinning machine
Heat setting
OE yarn

## Slide 16: TEXTILE PROCESS – POLYESTER FIBER
Polyester yarns include short fibers (staple fibers) and long fibers (filament yarns).
Short or long fibers are continuously blended with cotton fibers to produce different types of yarns.
Longer fibers are more applicable due to the continuity of yarns and lower cost of production.
Notes: Về công nghệ sản xuất sợi cotton, các doanh nghiệp sợi tại Việt Nam có thể sản xuất sợi CD và sợi nồi cọc đáp ứng nhu cầu thị trường thế giới. Tuy nhiên, hiện tại máy móc ngành sợi trong nước vẫn chưa được nâng cấp đồng bộ, một số nhà máy vẫn sử dụng máy móc cũ nên chất lượng sợi không đồng đều giữa các nhà máy.
Về công nghệ sản xuất sợi tổng hợp, hiện tại chỉ có 4 doanh nghiệp tại Việt Nam sản xuất sản phẩm sợi dài (sợi filament) từ hạt nhựa (công nghệ Chips spinning) là Sợi Thế Kỷ, Đông Thiên Phú, Hualon và Hưng Nghiệp Formosa. Các doanh nghiệp sản xuất sợi tổng hợp khác trong nước sản xuất sợi ngắn (sợi staple) từ xơ ngắn nhập khẩu.

## Slide 17: SOME TYPES OF FIBERS
Bio-based fibers: DuPont™ Sorona® EP - Poly Trimethylene Terephthalate, a thermoplastic polymer. Sorona is partially made with annually renewable plant-based ingredients.
Sorona® EP: Has molding characteristics equivalent to high-performance PBT (Polybutylene Terephthalate).
Biopolyester:
Partially bio-based polymer
Polyethylene Furanoate (PEF)
Bio-based TPA for PET derived from sugar
Bio Nylon 6: A more sustainable nylon made from renewable feedstocks instead of crude oil
Bio Nylon 6,6

## Slide 18: ENERGY BALANCE OF A SPINNING PROCESS
Main Energy type: Electrical Power
Major utility: Compressed Air and Humidification Plant
Largest consumer of energ : Ring Frames
7%
14%
17%
49%
13%
Back Processes (Mixing till Blow room) Carding
Drawing & Simplex Ring
Auto Cone
Source: Material Flow Cost Accounting of a Spinning Mill by Espire Consult
Example Energy Balance

## Slide 19
III.
Characteristics of the textile industry

## Slide 20: WEAVING

## Slide 21: WEAVING
Common Methods
  Power Looms
  Water Jet Looms (mostly synthetic fiber)
  Air jet Looms
  Rapier Looms
Air Jet Loom Application Suitable for
  plain and textured fabrics
  fine high-density fabrics
  High-speed bulk production
Rapier Loom Application Suitable for
  multi-color weft fabrics
  yarn-dyed fabric
  double-layered velvet fabrics
  terry fabrics
  decorative fabrics
  Much slower than air jet loom
  Moderate energy consumption

## Slide 22: ENERGY BALANCE – EXAMPLE (WEAVING)

## Slide 23: WET PROCESSING

## Slide 24: WET PROCESSING
Finishing
Stenter
Water proofing
Wrinkle free treatment
Softening treatment
Flame retardancy treatment
Odour resistance
treatment
Oleophobic treatment
Biocide treatment Coating
Finishing
Dyeing
Printing
Dyeing & Printing
Shearing
Combing
Singeing, Desizing
Scouring and Bleaching or Solomatic Bleaching
Washing
Mercerising, Drying
Stenter Shrinking
Pre-treatment

## Slide 25: TEXTILE DYEING TECHNOLOGY
Spinning, combing, sliver formation, bobbin winding
Weaving
Desizing
Boiling
Acid treatment and washing
Washing
Input materials
Water, starch, additives, steam
Enzym, NaOH
NaOH, chemicals, steam
Bleaching
H2SO4, CaOCl2 chemicals
H2SO4, H2O2, detergents
Mercerizing
NaOH, chemicals
Dye solutions
Washing
H2SO4, H2O2, detergents
Finishing and drying
Steam, starch, chemicals
Product
Sizing
H2SO4, H2O2, detergents
Dyeing and printing
Wastewater
Wastewater contains hydrolyzed starch size and NaOH

## Slide 26: A- DYEING APPROACHES
Material dyed
Twine
Yarn
Knitted/woven fabric
Garment
Process
Batch
Continuous
Dyeing techniques
Gel dyeing (in the production of artificial fibers)
Pigment dyeing (with binder)
Diffusion dyeing
Exhaust dyeing
Ozone dyeing
Ozone can be used on indigo or black sulfur fabrics.
Use of ozone requires up-front investment in the ozone machine and the generators, along with safety training for workers.
Dyeing methods

## Slide 27: B- FABRIC DYEING
Cellulosic Fabric Dyeing (Cotton, Viscose, lyocell, linen, hemp etc.)
  Reactive Dyes
  Temperature Required around 65 deg C for which machines work at atmospheric pressure
Synthetic Fabric / Blended (Polyester, PC, Nylon etc.)
  Disperse Dyes
  Temperature Required Above 100 deg C for which machines work above atmospheric pressure
Batch/Discontinuous
  Open Width form Dyeing: Open Jiggers and Pressure Jiggers, Beam,
  Rope form Dyeing: Jets, Winches, Soft flow machines / HT machines (Knitted fabric)
Semi Continuous
  Pad Batch / Cold Pad Batch (CPB) (For Cellulosic Materials and alternative to reactive dyeing)
  Pad Jig
  Pad Roll
Continuous
  Chemical Steam Pad
  Pad Dry Steam (PDS)
  Pad Dry Pad Steam (PDPS)
  Pad Dry Cure (PDC)
  Pad Thermosol Dyeing

## Slide 28: DYEING– BASIC STEPS
Step 1
  Colouring agents (mostly powder form, dye) dissolved in "dye liquor" according to a given recipe.
  Dyestuffs diffuse from "liquor" to the substrate
Step 2
  Dyestuff accumulates on the surface of the yarn/fabric => the question of the affinity of the dyestuff to the fibre
Step 3
  Penetration of the fibre with the dye (slower than surface accumulation) => prerequisite given for hydrophilic fibres (micropores); in the case of hydrophobic fibres => heating necessary (often over 100 degrees)
  Addition of salts to overcome electrostatic surface barriers
Step 4
  Fixation of dyestuffs (heat, auxiliaries)

## Slide 29: C- FABRIC PRINTING
In industry, 03 types of machines are used for printing the fabric:
  Rotary Printing
  Flatbed / Panel Printing
  Digital Printing
Normally fabric is printed through two methods
  Pigment Printing: Surface Printing where the design is fixed with the help of binders and fixers. Curing is done through dry heat in curing chambers above 100 oC (depending upon the color recipe)
  Reactive Printing: The colour design is attached to fabric as a result of chemical reaction. Curing is done in a high temperature (close to 100 oC) moist environment. This type of fabric requires washing after printing.

## Slide 30: D- FINISHING
In Textiles, two types of Finishing Processes are used
  Chemical Finishing in Stenter Machines: Either direct firing of natural gas or indirect heating through Thermal Oil
  Mechanical Finishing: Mostly steam is used for indirect heating at the following machines
    Calendars
    Comfort
    Sanforizer

## Slide 31: Typical energy requirements for textile wet processes – by product form, machine type, and process
(Carbon Trust, 1997)

## Slide 32: ELECTRICAL ENERGY USE IN TEXTILE

## Slide 33: Discussion
Which machine in the spinning line consumes the most electricity? What is the difference between sword weaving and air weaving in terms of energy costs? Why does the temperature in memory printing have to be as high as 100 degrees Celsius?

## Slide 34: GARMENT

## Slide 35: Sewing technology and energy consumption in garment factories
Raw material warehouse
Batches
Label
Fusing
Printing
Thêu
Preparation for sewing
Sewing
Intermediate pressing
Thread cutting
Inspection
Stain removal
Pressing
Folding
Labeling
Packing
Hoàn thiện và đóng gói
Washing, Dyeing, Tumbling, etc.
Treatment
Spreading
Cutting
Cutting
Design
Pattern construction
Preparation for cutting
Design, Pattern cons, Prep, Cutting
Finished product warehouse
Boiler, LNG, LPG, CNG,…
Compressed air
Electrical Energy

## Slide 36: Sewing technology and energy consumption in garment factories
Fuel/Gas
Boiler
Transformation station
HVAC
Lighting
Air compressor
Vacuum
Logistics
Raw material warehouse
Batches
Label
Fusing
Printing
Embrodering
Preparation for Sewing
Sewing
Intermediate pressing
Thread cutting
Inspection
Stain removal
Pressing
Folding
Labeling
Packing
Finishing and packing
Washing, Dyeing, Tumbling,…
Treatment
Spreading
Cutting
Cutting
Design
Pattern construction
Preparation for cutting
Design, pattern, prep, cutting
Finished product warehouse
Boiler, LNG, LPG, CNG,…
Compressed air
Electricity
Administrative/Social

## Slide 37: ENERGY BALANCE OF A GARMENT FACTORY
Chart: 
| 50 | 16 | 26 | 1.5 | 3.5 | β | 45 | 25 | 17 | 2 | 7 | 1 | 42 | 17 | 24 | 3 | 9 | 5 | 45 | 22 | 21 | 2 | 5 | 4 | 44 | 16 | 13 | 6 | 4 | 2 | 51 | 26 | 12 | 5 | 4 | 2 | Air Conditioning | Lighting | Sewing Machines | Pumps/Fans/Blowers | Compressor | Other Equipment
Energy Consumption(%) Avg | 46 | 20 | 19 | 3 | 5 | 3
Air Conditioning | 
Lighting | 
Sewing Machines | 
Pumps/Fans/Blowers | 
Compressor | 
Other Equipment | 

## Slide 38: ENERGY USING IN A GARMENT FACTORY – VIETNAM
Garment factory (2,440 workers)
Garment factory(728 workers)

## Slide 39: Discussion
Stage | Main Equipment | Primary Energy Source | Notes/Largest energy Consumption
1. Spinning |  |  | 
2. Yarn Brushing Machine |  |  | 
3. Simplex |  |  | 
4. Automatic taper thread |  |  | 
5. Fiber lake |  |  | 
6. Air Weave |  |  | 
7. Sword weaving |  |  | 
8. Continuous dyeing |  |  | 
9. Complete |  |  | 
10. Apparel |  |  | 
Fill in the following table:

## Slide 40
THANK YOU!