## Slide 1: TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs
Module 9.6:
Case Studies on Energy Efficiency Measures in the Textile Industry.
TECHNICAL STAFFS

## Slide 2: CONTENT
REDUCE WASTE AND INCREASE EE USING CHP SYSTEM
LEVI STRAUSS & CO. WATER<LESS™ PROGRAM

## Slide 3: I. REDUCE WASTE AND INCREASE EE USING CHP SYSTEM (1)
Key information:
Project: Tamijuddin Textile Mills Limited
Capacity: 6MWe Location: BSCIC Industrial Estate, Konabari, Gazipur, Bangladesh.
Industry: Textiles
Application: Combined heat and power
Installation by: Clarke Energy
Engine Manufacturer: INNIO Jenbacher
Engine Type: 4 x JMS 420
Fuel Type: Natural gas
Source: https://www.energy-xprt.com/articles/tamijuddin-textile-mills-reduce-waste-and-increase-energy-efficiency-case-study-1146411?utm_source=chatgpt.com

## Slide 4: REDUCE WASTE AND INCREASE EE USING CHP SYSTEM (2)
Challenges
The textile industry consumes large amounts of energy, especially in dyeing, printing, and finishing (wet processes).
A stable and continuous supply of both electricity and heat is essential.
Significant energy losses occur in power and heat transmission.
Objective: Reduce fuel use, CO₂ emissions, and energy costs
The CHP solutions
CHP system using natural gas as fuel.
Working principle: Simultaneously generates electricity and useful heat from one energy source.
Key advantages:
    Maximize use of waste heat
    Minimize transmission losses
    Lower energy costs
    Reduce environmental impact

## Slide 5: REDUCE WASTE AND INCREASE EE USING CHP SYSTEM (3)
Technology Implementation
Main Equipment:
  4 x INNIO Jenbacher JMS 420 GS NL
  Total power output: 6 MW
Integrated waste heat recovery system:
  Recovers exhaust heat from gas engines
  Efficiently converts hot water into low-pressure steam for use in wet processes
System located near point of use → reduces transmission losses

## Slide 6: REDUCE WASTE AND INCREASE EE USING CHP SYSTEM (4)
Outcomes & Benefits
Significant reduction in energy waste
Increased overall plant efficiency
Lower fuel and operating costs
Enhanced energy independence
Reduction in CO₂ emissions
A reference model for medium-large textile dyeing plants in Vietnam

## Slide 7: II. LEVI STRAUSS & CO. WATER<LESS™ PROGRAM (1)
Desizing
Rinsing
Bleaching
Neutralization
Stone Washing (abrasion)
Rinsing
Drying
KMnO4
Application
Neutralization
Washing (abrasion)
Softening
Drying
DENIM GARMENT WASHING

## Slide 8: LEVI STRAUSS & CO. WATER<LESS™ PROGRAM (2)
Mechanical processes
Rinse wash
Water jet fading
Stone wash
Whiskering
Microsanding including sandblasting
Mechanical abrasion
Laser treatment
Chemical processes
Acid wash, ice or snow wash
Hydrogen peroxide wash or bleach washing
Enzyme wash
Ozone fading
Spray techniques
Overdyeing and tinting
DENIM GARMENT WASHING

## Slide 9: LEVI STRAUSS & CO. WATER<LESS™ PROGRAM (3)
Low liquor ratio in stone wash:
Water savings counted: ½ Stone Wash bath
Average water savings: 2.4 liters / jean
Energy Saving: Steam used for ½ Stone Wash bath
Frequency of use: Moderate
Critical issues
  Back staining may occur if this technique is not properly applied.
  Low liquor ratio stonewash can be difficult in a belly washer machine.
  It is not recommended to use a liquor ratio below 3:1.
  Advances in enzyme and dispersant chemistry make this technique possible
ADVANTAGES OF STONE WASH (1)

## Slide 10: LEVI STRAUSS & CO. WATER<LESS™ PROGRAM (4)
Water savings counted: Two total baths, a de- size and a rinse
Average water savings: 11.8 liters / jean
Energy Saving: Electricity and Steam used for 2 baths
Frequency of use: High
Method: When a stonewash or enzyme wash follows a desize bath in a finish formula, it traditionally requires four baths: a desize bath, a rinse, a stonewash or enzyme bath, and another rinse. Combining the desize step with the stonewash/enzyme wash followed by a rinse reduces the process to a total of two baths.
Critical Issues:
Not recommended for fabrics that bleeds a lot.
An extra dispersant in the bath may be required to avoid back staining
Traditional | Proposed
Desizing ↓ Rinsing ↓ Washing (stone) ↓ Gentle wash | Desizing + Stone ↓ Rinsing
ADVANTAGES OF STONE WASH (2)

## Slide 11: LEVI STRAUSS & CO. WATER<LESS™ PROGRAM (5)
Remove de-size step
Water savings counted: One de-size bath
Average water savings: 5.9 liters / jean
Energy Saving: Electricity and Steam used for One de-size and One Rinsing bath
Frequency of use: High
Critical issues
  Possible if Water Soluble Sizing material is used in Denim Mill – needs encouragement from the Brands / Buyers
  In the case of a heavy weight fabric or a fabric that is sensitive to abrasion, a rinse step might still be necessary
  Challenges with shrinkage may arise

## Slide 12: LEVI STRAUSS & CO. WATER<LESS™ PROGRAM (6)
Increasing Ozone Concentration
Water savings counted: A bleach bath and a generic neutralization bath
Average water savings: 12 liters / jean
Energy Saving: Electricity and Steam used for One bleach and One Neutralization bath
Frequency of use: Moderate
Method
  Higher concentrations of ozone achieve more pronounced lightening effects, effectively replacing many uses for wet bleach baths.
  Lightening a garment with a wet bleaching agent typically requires three wet baths: a bleach bath, a neutralize bath, and a rinse bath. If ozone use comes in the middle of a finish formula, it saves all three baths.
  If ozone use is the first step in a formula, it only saves two baths because the garments need to be wet before being loaded into the machine.
Critical Issues
  Ozone can be used on indigo or black sulfur fabrics only.
  Use of ozone requires up-front investment in the ozone machine and the generators, along with safety training for workers

## Slide 13: LEVI STRAUSS & CO. WATER<LESS™ PROGRAM (7)
Spray potassium permanganate (KMnO4) on raw garments
Water savings counted: One neutralization bath
Average water savings: 5.8 liters/jean
Energy Saving: Electricity and Steam used for One Neutralization bath and One Drying Cycle
Frequency of use: High
Method
  Applying the spray at the beginning of the finish formula – before the garments ever get wet – allows the neutralization agent to be added to the first existing wet bath.
  The neutralization bath is removed, and the rinse that follows neutralization is also potentially removed.
Critical Issues
  This technique works best with dark finishes
  Be aware of potential back staining

## Slide 14: LEVI STRAUSS & CO. WATER<LESS™ PROGRAM (7)
1. Analysis: In the case studies given (CHP, Water<Less™ of Levi's...), which model do you see that can be applied or referenced for your business? Why (In order to successfully implement these initiatives (which can be expanded to enterprises in the textile and garment industry in Vietnam), what factors should be noted? - Technical? Financial? People? ...)
2. At your factory, have you invested in a large-scale energy project? Describe the effectiveness of the project? Do you have any recommendations to share and replicate for enterprises in the same field?

## Slide 15
THANK YOU!