## Slide 1: TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs
Module 4.8:
Current and potential of EE in the Plastic industry in Vietnam
TECHNICAL STAFF

## Slide 2: Discussion and presentation
Divide the class into 4 groups
Discussion time: 15 minutes
What sector do you think using the highest energy in Vietnam?
Identify the designated energy users in a plastic manufacturing facility.
What are the main sources of energy used in your company?
What energy-saving solutions are being implemented in your company?
Presentation time: 5 minutes

## Slide 3: Characteristics of energy consumption in Vietnam’s industry
The industry is the leading energy consumer sector in Vietnam, based on electricity consumption and final energy consumption.
As of 2023, Vietnam has 3,491 designated energy users (DEUs) with a total energy consumption of approximately 40,586,299 TOE. Among them, the industrial sector accounts for the majority, with 2,864 establishments consuming around 39,583,611 TOE (97.5% of the total DEUs). This demonstrates a significant potential for energy efficiency improvement in Vietnam’s industrial sector.
Vietnam's plastics industry has more than 4,000 enterprises, of which 90% are small and medium-sized enterprises. As for DEUs, there are 290 DEUs in the plastic industry (2023), it consumes 897,099 TOE, accounting for 2.2% of total DEU energy consumption and 2.3% of industrial DEU consumption.
By 2025, Vietnam requires 100% of designated energy-using enterprises to implement energy management systems as mandated by Decision 280/QD-TTG from the Prime Minister approving the National Program for Energy Efficiency for the 2019-2030 period.
The application of Energy Management Systems in Vietnam is still limited and weak. Many enterprises only implement these systems to meet legal requirements.

## Slide 4: 3. NUMBER OF DESIGNATED ENERGY USERS (DEUS)
Number of DEU and corresponding energy consumption, 2017-2023 (Source: Compiled from the DEUs List)
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2023
Energy using of DEUs (kTOE) | 24126 | 26750 | 35997 | 34294 | 51394 | 40586
Number of DEUs | 2496 | 2605 | 3006 | 2961 | 3068 | 3491

## Slide 5: EE targets for Vietnam's industrial sectors by 2030
Industries | By 2025 |  | By 2030 | 
 | From | To | From | To
Steel industry(%) | 3 | 10 | 5 | 16.5
Chemical industry(%) | 7 |  | 10 | 
Plastic manufacturing industry(%) | 18 | 22.46 | 21.55 | 24.81
Cement(%) | 7.5 |  | 10.89 | 
Textile and Garment(%) | 5 |  | 6.8 | 
Beverages and Beer(%) | 3 | 6.88 | 4.6 | 8.44
Paper (%) | 8 | 15.8 | 9.9 | 18.48

## Slide 6: AVERAGE ELECTRICITY PRICE (2010 – 2024)
Chart: Graph of electricity price form 2009 to 2024
| Năm 2009 | Năm 2010 | Năm 2011 | Năm 2012 | Năm 2013 | Năm 2014 | Năm 2015 | Năm 2016 | Năm 2017 | Năm 2018 | Năm 2019 | Năm 2020 | Năm 2021 | Năm 2022 | Năm 2023 | Năm 2024
 | 948 | 1058 | 1242 | 1369 | 1508 | 1622 | 1622 | 1622 | 1622 | 1720 | 1864 | 1864 | 1864 | 1864 | 1920 | 2103
Electricity price comparison table of Vietnam with some countries in the world (Source: EVN 2022)
Electricity price of countries in the world
Converted to Vietnamese dong

## Slide 7: Specific Energy consumption and Energy Savings Potential
C3 Energy efficiency scenario of the Vietnam Energy Outlook 2019 report
Sector | Product | Savings potential (%)
Drinks | Beer | 9–12
 | Non-alcoholic beverages | 4–9
Plastic | Consumer plastic | 9–13
 | Construction plastic | 5–14
 | Packaging | 4–12
 | Plastic bottle | 5–14.5
 | Plastic bag | 11–17
Paper | Pulp | 6.8
 | Packaging | 3.8
 | Printing paper | 4.4
 | Toilet paper | 3.8
Chemistry | Rubber SVR 10CV, 20CV | 9.4–32.7
 | Rubber SSVR 10, 20 | 9.8–32.7
 | Fertilizer | 1.4–5.4
 | Water-based paint | 20–30
Heavy industrial products | Finished steel | 13
 | Cement | 14
 | Textile yarn | 14

## Slide 8: Current status of energy use in industry
The plastics/rubber industry is one of the major energy consuming industries, with ~7.6 billion kWh/year (2019) and 18–22% of revenue spent on energy.
This consumption is approximately equal to or lower than heavy industries such as paper (20–30%), and higher than the textile industry (~8%).
However, the plastics industry still consumes much less than industries such as steel, cement and chemicals – (approximately 70% of the total energy in the industrial sector)
Energy efficiency: Energy consumption efficiency remains low, with significant waste due to outdated technology and inefficient management.

## Slide 9: Causes of high energy consumption
Outdated technology in plastic such as: Old Hydraulic molding machines, Outdated heating systems, Inefficient Cooling Systems/chillers, Manual extruders with low automation, No waste recovery or recycling integration, Old air compressors. Which consumes high amounts of energy and causes environmental pollution.
Lack of investment in innovation: Insufficient capital and motivation to invest in energy-efficient equipment and technology.
Low awareness of energy efficiency: Some enterprises have not prioritized energy efficiency measures in their production processes.
As a result, the efficiency in the Plastics Industry remains low and offers good opportunities for improvement

## Slide 10: Challenges in energy management and utilization
Technological challenges: Many enterprises use outdated technology, resulting in low energy performance and environmental pollution.
Cost challenges: The initial investment costs for energy-efficient technologies are high, causing many enterprises to hesitate to make changes.
Lack of strong supporting policies: Although there are policies encouraging energy efficiency, they are still not effective enough to drive widespread adoption of energy efficiency measures among enterprises.

## Slide 11: Trends in sustainable development in industry
Green industry: Enterprises are gradually paying more attention to using renewable energy and developing sustainable production.
International trend: Multinational corporations have higher standards for energy and environmental requirements when collaborating in Plastic industries.
Digital transformation and energy optimization: Applying digital technology to monitor and optimize energy usage in production.
New trends all place a certain emphasis on reducing greenhouse gas emissions in production and have become collaboration criteria for many major international corporations. This issue is becoming increasingly important and challenging for the industrial development of Vietnam.

## Slide 12
Plastics Industry

## Slide 13: Vietnam’s Plastic Manufacturing Industry
Overview:
The plastic manufacturing industry in Vietnam has been growing rapidly, contributing significantly to the national economy.
This growth is driven by increasing domestic consumption and export demand.
Number of Enterprises: Over 2,000 companies are actively engaged in the plastic manufacturing sector.
Production Growth:
2020: 7.9 million tons, an increase of 6.8% compared to 2019.
2022: 9.54 million tons, an increase of 1.9% compared to 2021.
Revenue:
2022: $25.18 billion, an increase of 5.68% compared to 2021.

## Slide 14: Vietnam’s Plastic Manufacturing Industry
Product Structure of Vietnam’s Plastic Industry
Packaging Plastics: Account for 35-40% of total production.
Construction Plastics: Make up approximately 25% of total production.
Household and Technical Plastics: The remainder, with an increasing share.
Export Markets
United States: In 2021, $1.85 billion, accounting for 37.5% of total plastic product export turnover.
Japan: In 2021, $696.9 million, accounting for 14.13% of total turnover.
EU and ASEAN: Export turnover has shown steady growth over the years.

## Slide 15: Vietnam’s Plastic Manufacturing Industry
Advantages
Strong Competitive Capacity: Diverse products, high quality, and competitive pricing.
Tariff Preferences: Benefiting from free trade agreements (FTAs) and the EU’s Generalized System of Preferences (GSP).
Abundant Workforce: A young labor force with reasonable labor costs.
Challenges
Dependence on Imported Raw Materials: A significant reliance on imported plastic materials leads to cost fluctuations.
International Competition: Facing competition from countries such as China, Thailand, and Malaysia.
Environmental Pressure: Increasing restrictions on plastic use and rising demand for eco-friendly products.

## Slide 16: Vietnam’s Plastic Manufacturing Industry
Product Transformation
Reduce the proportion of packaging plastics, increase production of construction and technical plastics.
Investment in Technology: Implement advanced technologies and automation in manufacturing.
Development of Green Products: Focus on producing recycled plastics, biodegradable plastics, and environmentally friendly products.
Growth Forecast
Projected production of 10.92 million tons by 2024, with a compound annual growth rate (CAGR) of 8.44% from 2024 to 2029.
Market Expansion: Continue to target new markets and increase market share in the U.S., EU, and Japan.
Sustainable Development: Focus on green production practices and minimizing environmental impact.

## Slide 17: Benchmarking in the plastic Industry
Benchmarking | Other Relevant Requirements
According to Article 5 of Circular 29/2024/TT-BCT, benchmarks for the plastic production (electricity consumption from 3,000,000 kWh/year) are as follows: | 
1. Plastic packaging Plastic bags: 0.95 kWh/kg Plastic bottles: 1.45 kWh/kg Packaging plastic: 0.62 kWh/kg 2. Plastic for construction materials PVC: 0.35 kWh/kg HDPE & PPR: 0.58 kWh/kg 3. Household plastic: 1.0 kWh/kg 4. Engineering plastic: kWh/kg | Manage and monitor the production process to determine the amount of energy consumed. Facilities with SEC higher than the benchmarking must report and justify the reasons to the competent authorities and submit an implementation plan to meet the benchmarking requirements based on the energy audit report. Report to the local DOIT by January 31 each year on the implementation status of the benchmarking of the facility (as specified in Article 5 of the Circular)

## Slide 18: Plastic Production Process
The plastic production process consists of several closely related stages, from raw material handling to shaping and finishing the product. Each stage plays an important role in ensuring quality and production efficiency. The main stages include:
1
Raw Material Selection and Preparation
2
3
Heating and Extrusion
4
5
Cooling and Cutting
8
6
7
Blending and Pelletizing
Shaping the Product
Product Finishing
Quality Inspection
Packaging and Storage

## Slide 19: EEMs in the Plastic Industry
Introduction:
The plastic industry is one of the largest energy-consuming sectors, particularly in processes such as heating, extrusion, and molding.
Implementing energy-saving solutions not only reduces production costs but also protects the environment and enhances competitiveness.
Main Energy Sources:
Electricity: Accounts for 60-70% of total energy consumption, used in machinery and production systems.
Fossil Fuels: Coal, oil, and gas are used in heating processes.
Challenges:
Low Energy Efficiency in Many Production Facilities:
Energy Waste Due to Outdated Machinery and Ineffective Management

## Slide 20: EEMs in the Plastic Industry
Renovating the Heating System
Characteristics: Heating accounts for a significant portion of energy consumption.
Solutions:
Use a recirculating heating system: Utilize waste heat for reuse in the production process.
Effective insulation: Reduce heat loss from heating equipment.
Benefits: Save 20-30% energy in the heating process.
Using High-Efficiency Machinery
Characteristics: Old machinery consumes a lot of energy and operates inefficiently.
Solutions:
Invest in new-generation, energy-efficient machinery.
Perform regular maintenance to maintain operational efficiency.
Benefits:
Reduce electricity consumption by 15-25%.
Increase production efficiency.

## Slide 21: EEMs in the Plastic Industry
Application of VFD (Variable Frequency Drive) Technology
Characteristics: Machinery such as extruders and injection molding machines operate continuously, consuming significant amounts of electricity.
Solutions: Install VFDs to adjust motor speed according to actual demand.
Benefits:
Reduce electricity consumption by 20-40%.
Extend the lifespan of the equipment.
Enhancing Automation
Characteristics: Manual production processes lead to energy waste and uneven performance.
Solutions:
Use automated control systems to optimize machinery operation.
Implement smart sensors for energy management.
Benefits:
Increase operational efficiency by 15-20%.
Reduce errors and unnecessary energy consumption.

## Slide 22: EEMs in the Plastic Industry
Optimizing the Cooling System
Characteristics: The cooling system accounts for a significant portion of energy consumption.
Solutions:
Use a closed-loop cooling system to reduce water and energy loss.
Improve cooling technology by using air instead of water.
Benefits:
Reduce cooling costs by 10-15%.
Contribute to environmental protection by reducing water consumption.
Using Renewable Energy
Characteristics: Manufacturing facilities are often dependent on the grid and fossil fuels.
Solutions: Install solar power systems to reduce reliance on the grid.
Benefits: Reduce CO₂ emissions and long-term energy costs.

## Slide 23: EEMs in the Plastic Industry
Characteristics: Manufacturing facilities are often dependent on the grid and fossil fuels.
Solutions: Install solar power systems to reduce reliance on the grid.
Benefits: Reduce CO₂ emissions and long-term energy costs.
Characteristics: Energy management is inefficient, leading to significant waste.
Solutions:
Implement an energy management system (ISO 50001).
Monitor and assess energy use efficiency at each stage of production.
Benefits: Save 5-10% energy through better management.

## Slide 24: EEMs in the Plastic Industry
Set Up a Regular Maintenance Plan
Create a list of equipment that requires maintenance → categorize based on priority level.
Determine maintenance frequency (based on operating hours, days, months, years).
Use scheduling software (Excel or CMMS - Computerized Maintenance Management System) to manage the maintenance plan.
Integrate operational data to flexibly adjust the maintenance plan.
Key Inspection Points in the Energy System
Steam system: check steam traps, leaks, pressure regulators, and gas filters.
Compressed air: check oil filters, safety valves, leaks, and water drainage from tanks.
Chiller: check pressure cutoff – evaporation, gas refilling, cooling fans.
Pump/fan/motor: inspect bearings, vibration, lubrication, and shaft alignment.
Lighting: replace broken bulbs, check control and sensor systems.

## Slide 25: EEMs in the Plastic Industry in the world
Pyrolysis recycling
Technology description
Pyrolysis is the breakdown of material at high temperatures in the absence of oxygen. Pyrolysis can be used to convert mixed plastic waste into liquid hydrocarbons, which can be used again by the petrochemical industry.
Relevance for net zero
Improved recycling would help reduce the need for virgin production and can reduce downcycling in which a material is recycled into a lower value end. However, behavioural barriers also need to be overcome to increase plastics collection rates, and secondary production is unlikely to ever fully replace the need for primary production.
Credit: Alex Tullo/Will Ludwig/C&EN

## Slide 26: EEMs in the Plastic Industry in the world
Pyrolysis recycling
Initiatives
Norwegian company Quantafuel has developed a technology that combines pyrolysis with catalysis to convert mixed plastic wastes to synthetic fuels. Its first commercial plant started operating in late 2019 in Denmark and will process 18 kt of plastic waste a year. The company has backing from companies such as major chemical producer BASF.
Japan: Development of Technology for Producing Raw Materials for Plastics Using CO2 and Other Sources: NA
Quantafuel’s Plastic-to-liquid (Ptl) plant in Skive is the first of its kind in the world.
Source: NEDO

## Slide 27: EEMs in the Plastic Industry
Pyrolysis recycling
Initiatives
The Finish refining company Neste announced in 2019 partnerships with Germany waste management company Remondis and Belgian recycler Ravago in order to develop thermochemical recycling technologies. The project aims to process over 1Mt of waste plastics per year by 2030 onwards. In 2023, a range of companies including Neste applied pyrolysis in production of PEX pipes.
The Thermal Anaerobic Conversion (TAC) technology, which was developed by UK-based company Plastic Energy and converts end-of-life plastics to oil (called Tacoil), is in use at two commercial-scale plants in Spain (operational since 2014 and 2017). Plans are underway to develop another plant in Netherlands in cooperation with Saudi Arabian company SABIC, as well as a plant in Malaysia in partnership with Petronas.

## Slide 28: Q & A

## Slide 29: Conclusion and Recommendations:
Conclusion:
Energy conservation in the plastic industry not only helps reduce costs but also protects the environment, aligning with the trend toward sustainable production.
Recommendations:
Businesses need to invest in modern technology and effective energy management systems.
The government should support policies, incentives, and loans to encourage businesses to transition to more efficient technologies.
Enhance workforce training on energy-saving practices and efficient usage.
THERE ARE SUBSTANTIAL OPPORTUNITIES FOR SIGNIFICANTLY IMPROVING EE”

## Slide 30
Dự án Thúc đẩy tiết kiệm năng lượng trong các ngành công nghiệp Việt Nam
THANK YOU !