## Slide 1
Module 9. Case studies on EEMs in the plastics industry.
TECHNICAL STAFF
TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs

## Slide 2: Case study
Year of operation: 1971 Address: Kieu Ky commune - Gia Lam district – Hanoi
Product: Production of bags, tents, tarpaulins derived from plastic
76 One Member Limited Liability Company

## Slide 3: Factory production process
Material mixer
System is stable
Film forming system
Extruder
Machine
Reening system
Stretching system
Coating machine or membrane complex
Blind receiver
Machine
May
PP or PE granules and additives, colorants
PP plastic
Additives
Color
Pre- filter
Extruder
Mixed ingredients after mixing
Mix well
Additives
Through the silk spray table
Melted mixture after filtration
Filter tank
Through heat lamination, creating patterns
Through cooling, stretching
Cut and pack
Scroll Receipt
Silk
Fiber Mesh
Non-woven fablric
Non Woven Fabric Roll
Waste products
Finish product

## Slide 4: Current status of the factory's air compressor system
The factory uses 04 air compressors with a capacity of 75kW and 01 22kW air compressor for backup in Area A of the factory
No | Air Compressor | Amount | Power
1 | Fusheng – Taiwan | 01 | 22
2 | Chicago Pneumatic – Belgium | 02 | 75
3 | Fusheng – Taiwan | 02 | 75
The air compressor system is designed in sync with the moisture separation air conditioner which is arranged and operated according to the central controller. These air compressors operate in alternating mode and when the pressure is lower than the set pressure, all 4 machines operate together to reach the set pressure. These air compressors are cooled by cooling towers, so the working efficiency of air compressors is relatively high.

## Slide 5: Air compressor construction

## Slide 6: Operating parameters
Parameter | Unit | Value
Ambient Temperature | oC | 33
Ambient humidity | % | 77,7
Closing Pressure | bar | 6,25
Shear Pressure | bar | 6,65
Air Compressor |  | 
Air compressor working pressure 2&3 | bar | 8,5
Air compressor working pressure 4 & 5 | bar | 8
Shell Temperature | oC | 33,7– 36,5
Inlet water temperature | oC | 28,6 – 30,2
Outlet water temperature | oC | 29,7 – 33,5
Drain water temperature | oC | 34,3 – 35,2
Exhaust compressed air temperature | oC | 34,9 – 36,5

## Slide 7: Measured electricity statistics
Parameter | Unit | Air Compressor 2 | Air Compressor 3 | Air Compressor 4 | Air Compressor 5
Operating capacity with load | kW | 84,0 | 83,5 | 93,9 | 89,2
Operating capacity with no load | kW | 42,6 | 35,1 | 40,2 | 44,0
Power Factor | - | 0,83 | 0,81 | 0,81 | 0,95
No- load operation ratio | % | 58 | 43 | 17 | 31
The loaded running capacity of the air compressors is relatively high compared to the rated capacity. Air compressors when idling have a capacity ranging from 35.1 to 44 kW; causing unnecessary power consumption when in standby mode. The cos ρ power factor of air compressors is maintained relatively large. Air compressors No. 2 and 3 in the central air compressor room are regularly operated in standby mode because the air compressor system in Zone A is centrally controlled, so the machines will operate in the mode of calling the machines in turn when the load demand increases.

## Slide 8: Compressor measurement results for 3 days

## Slide 9: Analysis of the operation of the air compressor system
No | Parameter | Unit | Time |  |  | Average
 |  |  | 13/07 | 14/07 | 15/07 | 
1 | Base load | kW | 202 | 206 | 212 | 207
2 | Peak load | kW | 383 | 372 | 366 | 374
3 | No-load power | kW | 122 | 141 | 144 | 136
4 | Time operating at base load | h | 19.09 | 21.72 | 22.61 | 21
5 | Time operating at peak load | h | 0.95 | 1.96 | 2.88 | 2
6 | No-load operation time (all 4 machines) | h | 0.98 | 0.48 | 0.14 | 1
7 | Total measurement time | h | 21 | 24 | 26 | 24
According to the measurement results, after checking the loaded/no-load running time, it was found that the idle rate of large machines ranged from 17-58%, which is a very large fluctuation. Normally, for screw air compressors, it should be maintained at a no-load level of 10-15% so that the machine runs stably and efficiently. When idling, the compressor engine still rotates but does not produce compressed air, too much idling time will cause waste of energy.

## Slide 10: Proposed solution
The inverter will run at the top, the old one will run in the background. This not only helps the machines to operate for a long time but also minimizes the idle time of the air compressor.
The built-in inverter will work efficiently even when running at low frequencies.
The following example shows the relationship between the energy consumption of the compressor station and the compressed air output.
"Installing an inverter for an air compressor" in combination with a common controller

## Slide 11: Compressed air station controller
Remote RUN/STOP control. Set the desired pressure value. Setting up a running schedule for each machine in real time helps optimize operation. Track the power consumption for the compressed air system, helping to manage costs in the compressed air system. Increase equipment life, save energy Warning of errors in case of machine malfunction.
Installation and connection of the coordinating controller in the compressed air station is done easily, at low cost, allowing the connection of many different models and types of air compressors.

## Slide 12: Control system

## Slide 13: Investment costs
Ginter Chart
No | Device | Amount | Pricing (millionVND) | Cost (million VND)
1 | PLC Controller | 1 set | 55 | 55
2 | Compressor Switchgear Relay | 4 sets | 5 | 20
3 | Control Software | 1 set | 35 | 35
4 | Cost of inverters, 02 inverters of 55 kW | 2 pcs | 65 | 130
5 | Calibration Installation Cost | 1 batch | 30 | 30
6 | Other ancillary costs |  |  | 10
 | Total |  |  | 280

## Slide 14: Energy efficiency
No | Device | Air Compressor2 | Air Compressor3 | Air Compressor4 | Air Compressor5 | Total
1 | Loaded Power (kW) | 84 | 83,5 | 93,9 | 89,2 | 
2 | Idle Power (kW) | 42,6 | 35,1 | 40,2 | 44 | 
3 | Load Rate (%) | 42 | 57 | 83 | 69 | 
4 | Idle Rate (%) | 58 | 43 | 17 | 31 | 
5 | Amount of electricity before implementation (kW) | 60 | 63 | 85 | 75 | 283
6 | Amount of electricity saved after implementation (kW) | 25 | 15 | 7 | 14 | 60

## Slide 15: Energy efficiency calculation

## Slide 16: Conclusions for case studies
Compressed air is a critical component in many industrial plants including those in the plastics industry. Compressed air is used for the purposes of shutting and closing control valves, performing cleaning and many other functions in the operating control mechanism of equipment Energy savings in compressed air systems can have a variety of solutions, including those that involve the strict management of leak sources and the use of compressed air by workers in the production line. In this typical case, 01 solution for the compressed air system of a plastic factory is presented, showing the diverse energy saving potential that can be obtained from a factory in the plastics industry.

## Slide 17: Case study 1 (1)
Tien Phong Plastics applies double-layer extrusion technology, especially for HDPE twisted ribbed pipe products.
Background:
CÔNG TY TNHH SẢN XUẤT THƯƠNG MẠI NHỰA TIẾN PHONG
Địa chỉ: U01 - L68 - Khu đô thị Đô nghĩa - Yên Lộ - Yên Nghĩa - Hà Đông
Application: HDPE twisted ribbed pipe manufacturing

## Slide 18: Information: HDPE twisted ribbed pipe manufacturing
Overview: Investment in Battenfeld‑Cincinnati Double-Layer Extrusion Line
In 2011, Tiền Phong installed a KryoSys pipe extrusion line from Battenfeld‑Cincinnati (Austria) at their Hải Phòng factory
This enabled domestic production of HDPE pipes up to 2 m diameter, including double-layer twisted ribs/spira structures, replacing imported lines .
While the capital cost wasn't disclosed, such turnkey systems typically range between USD 800,000–1 million, depending on capacity and automation.
Case study 1 (2)

## Slide 19: Case study 1 (3)

## Slide 20: Case study 1 (4)
Strategic & Intangible Benefits
Market leadership: Being first in Asia with ≥2 m HDPE line sets Tiền Phong
Product quality & standards: Full compliance with ISO 4427 and DIN/EN for spiral HDPE
Export-readiness: Supplying ASEAN region with local production and competitive pricing.
Brand positioning: Advanced, energy-efficient, and environmentally preferable.
Notes: https://www.k-online.com/en/Media_News/News/Vietnamese_company_to_install_first_2000-mm-diam_pipe_extrusion_line?utm_source=chatgpt.com

## Slide 21: Process steps
Case study 1 (5)

## Slide 22: Case study 1 (6)
Energy & Material Savings Impacts
The KryoSys design features internal cooling, improving efficiency and reducing cooling length, which directly lowers energy consumption plasticsnews.com.
Benefits from:
  Co-extrusion of two layers (virgin + recycled/resistant compound), reducing material cost per meter by ~10–20%
  Faster cycle times due to advanced cooling
  Better dimensional accuracy, reducing scrap/waste

## Slide 23: Case study 1 (7)
Item | Estimated Value
Investment cost | USD 800,000
Annual production | 10,000 ton
Material savings | 10% at USD 1,200/ton → USD 120/ton → USD 1.2M/year
Energy savings | 15% of ~5,000 MWh/year @ USD 0.10 → USD 75k/year
Scrap reduction benefits | USD 50k/year
Auxiliary systems (cooling, dies, hauling, control units) | - $100,000 – $300,000
Installation, training, commissioning | - $30,000 – $50,000
Total annual benefit | USD 1.325M/year
Payback period | 1-2 year
Estimated Cost‑Benefit (Hypothetical Model)

## Slide 24
Payback Period
Benefit Category | Impact | Notes
Energy savings | Moderate (~10–15%) | Due to higher extrusion efficiency, better heat control, optimized material flow
Material cost reduction | High (15–30%) | Inner layer can use cheaper materials (e.g., regrind, recycled HDPE) without affecting performance
Improved productivity | High | Faster line speeds, less downtime, better product consistency
Labor savings | Moderate | Automation reduces manual adjustments and errors
Estimated payback period | 2–4 years | Depending on production volume and material cost savings
Case study 1 (8)

## Slide 25: Case study 1 (9)
Conclusion
Tiền Phong's strategic investment in double-layer HDPE twisted pipe extrusion delivered rapid ROI,
Major material savings using recycled/compound co-extrusion
Solid energy reductions via efficient cooling
Improved quality and reduced scrap
Strengthened competitive brand presence and export capability
All these align with their goal to lead in high-tech pipe manufacturing, capturing both economic and strategic value.

## Slide 26: Case study 2 (1)
1. Initial Situation
Many plastic injection factories in Vietnam (especially those using old hydraulic injection machines) see up to 80% of total factory electricity consumption from these machines, as the hydraulic oil pump motor runs at 100% capacity continuously, even when high pressure is not needed.
This leads to:
Energy waste during low-pressure stages (e.g., cooling).
High maintenance costs, frequent breakdowns, and faster degradation of hydraulic oil.

## Slide 27: Case study 2 (2)
Solution: Retrofitting Hydraulic Plastic Injection Machines with MH800 Servo Technology in Vietnam
Notes: https://www.indiamart.com/proddetail/retrofitting-of-injection-molding-machine-by-servo-system-22031139348.html

## Slide 28: Case study 2 (3)
Clamping Force | 0-800 ton
Machine Type | injection molding
Capacity | 0-700 ton
Brand | DELTA,INOVANCE,SYNMOT,VEICHI,ARCUCHI
Automation Grade | Semi-Automatic
Maximum Injection Pressure | 250 bar
Benefit of Hybrid Servo System :
1. High qualified Experienced Engineering Team of Electrical & Hydraulic for Easily Retrofitting of servo system in place of your old Induction Motor in Injection Molding .
2. ROI in about One Year.
3. 40 to 80% energy saving by servo system.
4. 24X7 service supports.
5. Induction Motor replace with servo Motor ( capacity of motor also get reduced ).
6. More Efficient Internal gear Pump replace your currently Used Fixed Pump.
7. Life of machine Seals , Motor , Oil , pump all most become double because of lower oil heating with servo system.
8. Oil heating problem become minimum.
9. Low maintenance cost of system after retrofitting .
10. Noise free System , noise reduce up to 20 DB.
Notes: https://www.quantafuel.com/

## Slide 29: Case study 2 (4)
Energy Saving Results
Energy consumption reduced by 20–80%, depending on load and cycle.
Typical example: The cooling phase often takes the most time but requires low pressure → servo can effectively reduce load and save energy.

## Slide 30: Case study 2 (5)

## Slide 31: Case study 2 (6)

## Slide 32: Case study 2 (7)

## Slide 33: Case study 2 (8)
Item | Estimate
Retrofit installation cost | USD 5,000–10,000 (depends on machine size)
Energy savings | 30–80% of machine electricity consumption
Example savings (75 kW machine, 8 hrs/day) | 75 kW × 40% × 8 hrs = 240 kWh/day
Annual savings (300 days/year) | 72,000 kWh
Financial benefit (@$0.10/kWh) | USD 7,200/year
Payback time | USD 10,000 / 7,200 = ~1.4 years
Cost–Benefit Analysis (per machine estimate)
If the machine operates more shifts/day, savings and ROI are even faster. Additional benefits: Lower maintenance costs, less oil loss, fewer breakdowns.

## Slide 34: Case study 2 (9)
Additional Outstanding Benefits
Reduces defective products due to better pressure control and faster system response.
Lowers maintenance costs (motors, valves, oil).
Extends equipment lifespan, ensures smoother operations.
Easy installation: Retrofit is compatible, quick to implement, and includes 24/7 technical support.
Widespread Applicability
This solution has been successfully implemented:
In Vietnam by DAT Group (MH800 retrofit).
In Asia and Europe by manufacturers like Woojin, Bosch Rexroth, Haitian – achieving 70–80% energy savings.

## Slide 35: Case study 2 (10)
Conclusion
Upgrading old hydraulic injection molding machines with MH800 servo retrofits offers clear economic and operational benefits:
40–80% electricity savings,
Payback period under 2 years,
Improved operation and product quality.
This is a practical and cost- effective solution for plastic factories in Vietnam.

## Slide 36: Q & A

## Slide 37
THANK YOU!