## Slide 1
Module 4.1:
Current status and potential of energy efficiency in the steel industry in Vietnam.
MANAGEMENT OFFICERS
TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs

## Slide 2: Small group discuss and presentation
Devided the class into 4 group
Discuss in 15 mins
What sector do you think using the highest energy in Vietnam?
Identify the designated energy users (DEUs) in the steel enterprises?
What energy source your company mainly use?
What potential of EE in your company
Presentation in 5 mins

## Slide 3: GLOBAL INDUSTRIAL ENERGY USAGE
Total Final Energy Consumption (TFC) by Sector from 1990 to 2020-2022
Notes: OECD Europe includes: Austria, Belgium, Czech Republic, Denmark, Finland, France, Germany, Greece, Hungary, Iceland, Ireland, Italy, Luxembourg, the Netherlands, Norway, Poland, Portugal, Slovakia, Spain, Sweden, Switzerland, Turkey, and the United Kingdom.
Changing focus from the U.S. stage of energy management to the work stage now.
Borrowed this slide from DOE. The stand out part of this is that industry consumes 50% of world energy. When you look at many developing countries, industrial energy use can be as large as 70- 80% of their total use.
This does not go unrecognized. Many countries have developed energy management system standards or other types of national programs to help their industry. These countries include Denmark, Ireland, China, Korea, Japan, Spain, Thailand, Germany, Sweden, United Kingdom. So there is a ground swell of energy management standards that have been developed our are in the process of being developed.

## Slide 4: FINAL ENERGY CONSUMPTION BY INDUSTRY IN VIETNAM
2023 ENERGY STATISTICS REPORT

## Slide 5: CHARACTERISTICS OF ENERGY CONSUMPTION IN VIETNAM’S INDUSTRY
The industry is the leading energy consumer sector in Vietnam, based on electricity consumption and final energy consumption
Vietnam currently has 3.491 (update in 2023) , consuming 51,393,648 TOE, with DEUs in the industrial sector making up the majority, 2.864 facilities consuming 40,586,299 TOE. The Vietnamese industry has significant potential for energy efficiency.
In the list of DEUs in 2023, there are 117 enterprises in the steel industry
By 2025, Vietnam requires 100% of designated energy-using enterprises to implement energy management systems as mandated by Decision 280/QD-TTG from the Prime Minister approving the National Program for Energy Efficiency for the 2019-2030 period.
The application of Energy Management Systems in Vietnam is still limited and weak. Many enterprises only implement these systems to meet legal requirements.

## Slide 6: NUMBER OF DESIGNATED ENERGY USERS (DEUS)
Number of DEU and corresponding energy consumption, 2017-2021 (Source: Compiled from the DEUs List)
Number of DEUs
Energy using of DEUs (kTOE)
The Steel industry has about 117 DEUs

## Slide 7: EE TARGETS FOR VIETNAM'S INDUSTRIAL SECTORS BY 2030
Industries | By 2025 |  | By 2030 | 
 | From | To | From | To
Steel industry(%) | 3 | 10 | 5 | 16.5
Chemical industry(%) | 7 |  | 10 | 
Plastic manufacturing industry(%) | 18 | 22.46 | 21.55 | 24.81
Cement(%) | 7.5 |  | 10.89 | 
Textile and Garment(%) | 5 |  | 6.8 | 
Beverages and Beer(%) | 3 | 6.88 | 4.6 | 8.44
Paper (%) | 8 | 15.8 | 9.9 | 18.48

## Slide 8: AVERAGE ELECTRICITY PRICE (2010 – 2024)
Chart: Graph of electricity price form 2009 to 2024
| Năm 2009 | Năm 2010 | Năm 2011 | Năm 2012 | Năm 2013 | Năm 2014 | Năm 2015 | Năm 2016 | Năm 2017 | Năm 2018 | Năm 2019 | Năm 2020 | Năm 2021 | Năm 2022 | Năm 2023 | Năm 2024
 | 948 | 1058 | 1242 | 1369 | 1508 | 1622 | 1622 | 1622 | 1622 | 1720 | 1864 | 1864 | 1864 | 1864 | 1920 | 2103
Electricity price comparison table of Vietnam with some countries in the world (Source: EVN 2022)
Electricity price of countries in the world
Converted to Vietnamese dong

## Slide 9: ENERGY SAVING POTENTIAL
C3 Energy efficiency scenario of the Vietnam Energy Outlook 2019 report

## Slide 10: CURRENT STATUS OF ENERGY USE IN INDUSTRY
Proportion of energy consumption: The industrial sector accounts for about 54% of the total energy consumption in the country.
Industries with high energy consumption:
  The steel production, cement, textile, wood processing, and chemical industries.
  These industries consume approximately 70% of the total energy in the industrial sector. Energy consumption in the steel sector accounting for around 5.18% of total industrial energy use in Vietnam
Energy efficiency: Energy consumption efficiency in the Steel industry remains low, with significant waste due to outdated technology and inefficient management.

## Slide 11: CAUSES OF HIGH ENERGY CONSUMPTION
Outdated technology: Many steel enterprises still rely on outdated technologies such as the blast furnace basic oxygen furnace (BF–BOF) route, open hearth furnaces, and manual rolling mills, which are highly energy-intensive and emit large amounts of CO₂. These older systems often lack modern pollution controls, use coal-fired reheating furnaces, and fail to recover waste heat, leading to low efficiency, poor environmental performance, and high production costs compared to cleaner, more efficient technologies like electric arc furnaces (EAF) and automated systems.
Lack of investment in innovation: Insufficient capital and motivation to invest in energy-efficient equipment and technology in steel industry.
Low awareness of energy efficiency: Steel enterprises have not prioritized energy efficiency measures in their production processes.

## Slide 12: CHALLENGES IN ENERGY MANAGEMENT AND UTILIZATION
Technological challenges: Steel enterprises use outdated technology, resulting in low energy performance and environmental pollution.
Cost challenges: The initial investment costs for energy-efficient technologies are high, causing steel enterprises to hesitate to make changes.
Lack of strong supporting policies: Although there are policies encouraging energy efficiency, they are still not effective enough to drive widespread adoption of energy efficiency measures among steel enterprises.

## Slide 13: TRENDS IN SUSTAINABLE DEVELOPMENT IN STEEL INDUSTRY
Green industry: Steel enterprises are gradually paying more attention to using renewable energy and developing sustainable production.
International trend: Multinational corporations have higher standards for energy and environmental requirements when collaborating, especially in steel industries
Digital transformation and energy optimization: Applying digital technology to monitor and optimize energy usage in production in steel.
New trends all place a certain emphasis on reducing greenhouse gas emissions in production and have become collaboration criteria for many major international corporations. This issue is becoming increasingly important and challenging for the steel industrial development of Vietnam.

## Slide 14
ENERGY EFFICIENCY POTENTIAL IN THE STEEL INDUSTRY

## Slide 15: ENERGY INTENSITY IN KEY INDUSTRIES IN VIETNAM
Figure: Energy Intensity Improvement in Key Industries during VNEEP Phase 2 Changes of energy intensity in key industries

## Slide 16: BENCHMARKING IN THE STEEL INDUSTRY
Benchmarking | Other Relevant Requirements
According to Clause 2, Article 5 of Circular 20/2016/TT-BCT, benchmarks for the steel industry from 2021 to the end of 2025 are as follows: Iron ore sintering: 1,960 MJ/ton Cast iron production (blast furnace): 12,400 MJ/ton Steel billet production (basic oxygen furnace- BOF): 100 MJ/ton Steel billet production (electric arc furnace- EAF): 2,500 MJ/ton Steel billet production (induction furnace): 2,500 MJ/ton Hot rolling of long steel: 1,600 MJ/ton Cold rolling of steel sheets: 1,500 MJ/ton | A plan must be prepared to comply with the benchmarks stated in Article 5 of Circular 20/2016/TT-BCT. DOITs must be reported to annually by January 15 regarding the implementation status of benchmarks.

## Slide 17: Energy consumption rate of billet steel industry
Country / Region | Technology | Energy Consumption Intensity (GJ/ton) | Notes
Vietnam | Average | 20 – 30 GJ/ton | Depends on production line and modernization level (higher than global standard)
China | Modern | 16 – 18 GJ/ton | Improved technology, utilizing waste heat
Japan / EU | Advanced technology (BF–BOF) | 14 – 16 GJ/ton | Applies heat recovery, integrated power generation (e.g., coke dry quenching, TRT...)
Global (average) | BF-BOF (Blast Furnace – Basic Oxygen Furnace) | ~19 – 21 GJ/ton | Depends on process and direct reduction (DRI)
Global (EAF) | Electric Arc Furnace (EAF) | 4 – 7 GJ/ton | Uses scrap steel; significantly more energy-efficient than BF-BOF
Sources:
IEA (International Energy Agency), Tracking Industry 2024 – Steel Sector
World Steel Association, 2022, "Energy use in the steel industry"
Ministry of Industry and Trade of Vietnam, "2023 Report on Energy Consumption in Key Industrial Sectors"

## Slide 18
Energy consumption rate of steel pipe industry
Source: APEC Energy Working Group, 2021. “Energy Efficiency Technologies in Steel Industry”. UNIDO – Vietnam Ministry of Industry and Trade, 2020. "Technical Guidelines on Energy Saving in the Steel Industry"
Country / Region | Technology | Energy Consumption Rate (GJ/ton) | Notes
Vietnam | Cold rolling, pipe welding | 3.5 – 6.0 GJ/ton | Depends on furnace system, level of automation, and operational management
Japan / EU | High automation | 2.5 – 3.5 GJ/ton | Energy-saving systems, heat recovery
World (average) | Cold rolling, gas/infrared furnace | 3 – 5 GJ/ton | Equipment improvements (VFDs, heat recovery, etc.)

## Slide 19: ENERGY CONSUMPTION IN THE STEEL INDUSTRY
Main Types of Steel Products
Construction steel: Accounts for the largest share of domestic consumption, with products such as rebar and wire rods.
Steel plates and sheets: Used in the shipbuilding industry, automobile manufacturing, and other fabrication industries.
Steel pipes: Used in construction, oil and gas pipelines, and various other industrial applications.
Coated steel and galvanized sheets: Used in construction, appliance manufacturing, and the automobile industry.

## Slide 20: ENERGY CONSUMPTION IN THE STEEL INDUSTRY
Main Types of Energy Consumed in the Steel Industry
Electricity: Used in processes such as electric arc furnace steelmaking, steel rolling, and operating auxiliary equipment.
Thermal energy: Mainly from coke, natural gas, and oil, used in iron smelting, iron ore sintering, and steel billet heating. Coal and oil are used in blast furnaces and kilns to provide heat for the manufacturing process.

## Slide 21: Causes of high consumption of the steel industry
Out of date, asynchronous technology: Especially small induction ovens
Low equipment performance: Transformers, fans, rolling mills are not optimal
Lack of an energy management system: Limitations in consumption monitoring
Lack automation adoption: And lack of energy audits
Fossil fuel dependence: Less use of renewable energy

## Slide 22: EEMs IN THE STEEL INDUSTRY
1. Application of Advanced Steel Production Technologies
Use new blast furnaces with higher energy conversion efficiency.
Apply Electric Arc Furnace (EAF) technology to replace traditional blast furnaces.
Use EAF combined with high-quality scrap steel.
Implement green hydrogen steelmaking technology.
Effectiveness:
Reduce energy consumption and greenhouse gas emissions.
Enhance market competitiveness.
Improve product quality.

## Slide 23: EEMs IN THE STEEL INDUSTRY
2. Waste Heat Recovery for Power Generation
Install a waste heat recovery system from the production process.
Use Blast Furnace Energy Recovery Turbine (BPRT) technology.
Effectiveness:
Save 10% of electricity consumption.
Reduce greenhouse gas emissions.

## Slide 24
WASTE HEAT AND ENERGY REUSE SOLUTIONS
Waste heat recovery: Heat recovery from flue gas for fuel drying and preheating
Utilizing CO gas: Using CO2 from blast furnace as auxiliary fuel or electricity generation
Energy optimization: Integrating solutions to create a closed energy cycle
Reuse by-products: Utilizing dust and mineral mud to reduce energy loss
The solution of recovering waste heat from flue gas for fuel drying and preheating helps to take advantage of energy sources that are often wasted. Utilizing CO2 (in blast furnaces) as auxiliary fuel or electricity generation is also an effective way to reuse energy.
In addition, reusing dust, ore sludge and limiting energy loss during processing not only helps save energy but also contributes to environmental protection, creating a more sustainable production cycle.
EEMs IN THE STEEL INDUSTRY

## Slide 25: EEMs IN THE STEEL INDUSTRY
3. Improve Production Processes and High-Efficiency Equipment
Install a frequency converter for fan motors.
Install an automatic compensation system to maintain a stable power factor.
Effectiveness:
Reduce 25% of electricity consumption for motors.
Save 2.5% of total electricity consumption for the entire factory.

## Slide 26: EEMs IN THE STEEL INDUSTRY
4. Applying an energy management system according to ISO 50001
Build an energy management system to monitor and optimize energy use throughout the factory. Set specific energy saving goals, measure efficiency, and continuously improve. Integrate energy efficiency indicators into the KPIs of each department. Train employees on energy saving awareness and techniques. Effective:
    Reduce energy consumption by 5-10%. Improve production efficiency and meet international environmental standards.

## Slide 27: EEMs IN THE STEEL INDUSTRY
5. MANAGEMENT AND OPERATIONAL SOLUTIONS
Energy Audit: Identify hot spots and propose feasible solutions
Human resource training: Saving 3-5% energy
SCADA/EMS Energy Monitoring: Analysis and warning of abnormal consumption
Implementing an ISO 50001 energy management system can help save 5-10% of energy through establishing an energy management process. Regular energy audits help identify energy consumption "hot spots" and provide feasible improvement options.
Staff training and improved operating habits can yield 3-5% savings, while SCADA/EMS energy monitoring software applications help analyze and promptly alert on energy consumption abnormalities.

## Slide 28: EEMs IN THE STEEL INDUSTRY
6. Optimizing systems
a. Optimizing compressed air and industrial gas systems
Closely monitor and control compressed air systems.
Use measuring equipment to detect leaks and energy losses.
Efficiency:
Reduce energy consumption and operating costs.
Improve operational efficiency.

## Slide 29: EEMs IN THE STEEL INDUSTRY
b. Auxiliary systems (fans, pumps)
Savings potential: 10-15%
Replace the existing motor with high-efficiency motor IE3 or higher
Install the inverter and PID control system to optimize operation
Regular maintenance to ensure optimal performance
c. Pneumatic system
Savings potential: 10-20%
Check and fix leaks in piping systems
Optimize operating pressure to suit actual needs
Adjust the operating time of the air compressor according to
the production schedule
Use intelligent control systems to automate operations

## Slide 30: EEMs IN THE STEEL INDUSTRY
Category
Energy efficiency solutions
Energy efficiency estimate
Heating system
Optimize furnace, insulation
10-25%
Heating system
Use waste heat (smoke heat) for preheating
10-25%
Steel rolling
Inverter control for motor
5-10%
Steel rolling
High performance drive system
5-10%
Heating systems in steel production have a great potential for energy savings, up to 10-25%. Optimizing the furnace, improving the insulation system and using waste heat from flue gases for preheating are effective solutions.
In the steel rolling process, applying inverter control technology to motors and using high-efficiency transmission systems can help save 5-10% of energy. These solutions not only reduce electricity consumption but also extend the life of equipment.
d. HEATING AND STEEL ROLLING SYSTEM

## Slide 31: EEMs IN THE STEEL INDUSTRY
Production of iron by route and scrap share of metallic inputs in the Net Zero Scenario, 2018-2030

## Slide 32: EXAMPLE OF EEMS IN THE STEEL INDUSTRY IN THE WORLD
Initiatives
The process was validated in industrial environment in China by the LanzaTech BaoSteel New Energy Company, 2012 and Shougang LanzaTech New Energy Technology Company, 2013. Lanzatech also has test facilities in New Zealand and Chinese Taipei.
First commercial plant began operation in 2018 in China, by Lanza Tech, Shougang Group and TangMing; produced 30 million litres of ethanol for commercial sale in its first year of operation.
Conversion of steel offgases to fuel (blast furnace)
Belgium: Arcelor LanzaTech Carbalyst (Steelanol) Ghent: Large-scale demonstration plant has been inaugurated in Ghent, Belgium, under the Steelanol project by ArcelorMittal and Lanzatech with a capacity of 80 million litres of ethanol upon completion. The process has been previously successfully tested at the site in 2016.

## Slide 33
Hoa Phat
Using BF-BOF and hot rolling technology. Invested in waste heat recovery system (WHR) and applied ISO 50001 standard on energy management.
Pomina
Operates EAF furnace and has implemented a modern power monitoring system, helping to optimize production and reduce energy consumption.
TISCO
Using old blast furnaces and steel rolling lines, resulting in higher energy consumption compared to modern enterprises.
Vina Kyoei
Applying Japanese EAF furnace technology with good energy saving efficiency, we are one of the pioneers in energy optimization.
INDUSTRY LEADING ENTERPRISES

## Slide 34
INDUSTRY LEADING ENTERPRISES
Pomina
Improved EAF feeding, applied inverter
Result: 12% reduction in electricity consumption
Hoa Phat
Heat recovery, ISO 50001, automatic control
Result: Energy saving > 15%
Vina Kyoei
Applying Japanese technology, good control of electricity
Result: energy consumption 20% lower than industry average
Some steel enterprises in Vietnam have pioneered the application of energy-saving solutions and achieved encouraging results. Pomina has improved the electric arc furnace (EAF) charging process and applied inverter technology, helping to reduce electricity consumption by 12%.
Hoa Phat Group has synchronously deployed heat recovery solutions, applied ISO 50001 energy management system and automatic control system, achieving energy savings of over 15%. Vina Kyoei, with the application of Japanese technology and good power control, has achieved energy consumption 20% lower than the industry average.

## Slide 35
CONCLUSION AND RECOMMENDATIONS
Awareness and commitment: Raise awareness and commitment from leadership
Assessment and planning: Energy audit and roadmap development
Solution Deployment: Prioritize high efficiency, low cost solutions
Monitoring and Improvement: Measure results and continuously improve
The Vietnamese steel industry has great potential for energy savings, from 10-20% of total energy consumption. To effectively exploit this potential, businesses need strong commitment from the management, conduct energy audits to identify savings opportunities, and develop a suitable implementation roadmap.

## Slide 36: Quiz
Which technologies and equipment in the steel production process cause significant energy waste?
Which energy-saving solutions are likely to be applicable to your plant?”
What barriers and challenges are you likely to face in implementing such solutions?

## Slide 37
THANK YOU