## Slide 1: TRAINING PROGRAMME FOR IEs
MANAGEMENT OFFICERS
Module 7:
Characteristics of typical technological lines in the steel manufacturing industry.

## Slide 2
STEEL PIPE AND GALVANIZED STEEL MANUFACTURING INDUSTRY

## Slide 3
FOCUS ON THE PRODUCTION OF CONSTRUCTION STEEL AND ROLLED STEEL
Reinforcing steel bar
Key products serving the construction industry.
Hot rolled coil (HRC)
Widely used in the manufacturing industry
Structural steel (U, I, H beams)
Applied in construction structures and mechanical engineering
Steel pipe
Used in piping systems and construction

## Slide 4: CONTENT
Features of billet steel production technology
1.1. Blast furnace (BOF) and electric arc furnace (EAF) technology
1.2. Rolling and processing stage
1.3. Integration and synchronization
1.4. Application of advanced technology
1.5. Toward to “green” steel production
1.6. Automation and quality control
1.7. Diverse scale
1.8. Comparison table of energy consumption by technology
Features of pipe steel production technology
2.1. Production line
2.2 heat and surface treatment process
2.3. Energy supply system
Notes: Hợp đồng hiệu quả năng lượng (EPC): là hợp đồng ký kết giữa ESCO và Khách hàng để thực hiện dịch vụ sử dụng năng lượng tiết kiệm và hiệu quả.
– Hợp đồng chia sẻ mức tiết kiệm năng lượng: ESCO chịu mọi rủi ro tài chính và kỹ thuật của dự án bằng cách thu xếp tài chính để thực hiện dự án đầu tư lắp đặt các trang thiết bị hiệu quả năng lượng tại cơ sở sử dụng năng lượng của khách hàng
– Hợp đồng đảm bảo mức tiết kiệm năng lượng: ESCO chịu trách nhiệm cung cấp, thiết kế, lắp đặt, đo lường và đảm bảo hiệu quả giải pháp sử dụng năng lượng tiết kiệm và hiệu quả cho khách hàng.

## Slide 5
FEATURES OF BILLET STEEL PRODUCTION TECHNOLOGY

## Slide 6
Blast furnace (BOF)
Energy intensityty of BOF in Vietnam is 12.400 MJ/ton
Blast furnace technology, like that of Hoa Phat Group, is a closed chain from iron ore to finished steel. The advantages are low energy consumption and production of high-quality steel with few impurities.
Electric arc fur (EAF)
Energy intensityty of EAF in Vietnam is 2.500 MJ/ton
EAF technology is popular among small and medium-sized enterprises, utilizing recycled steel scrap, helping to reduce raw material costs and in line with sustainable development trends.
1. BLAST FURNACE (BOF) AND ELECTRIC ARC FURNACE (EAF) TECHNOLOGY

## Slide 7
1.1. BLAST FURNACE (BOF) TECHNOLOGY
Blast furnace (BOF): Closed production from iron ore to finished steel, allowing for better quality control and
reduced dependence on scrap.
Raw materials for steel production
- Iron ore
Iron ore is the main source of iron, consisting of hematite (Fe2O3) and magnetite (Fe3O4). After mining, iron ore is refined to create concentrate, ensuring the required iron content.
- Coke
Coke is an essential raw material in the ironmaking process, produced from coal through a process of burning in an oxygen-deficient environment. Coke provides heat and acts as a reducing agent in the reduction of iron oxide in the blast furnace.
- Limestone
Limestone (converted into quicklime in a blast furnace)
- Scrap Steel
Alloying elements such as manganese, nickel, chromium, and molybdenum are used to increase the mechanical properties, strength, and wear resistance of steel.

## Slide 8
CHARACTERISTICS OF BLAST FURNACE SYSTEM AT HOA PHAT
 | Information
Number of blast furnaces | Hoa Phat Dung Quat has 4 blast furnaces, each furnace ~1,080m³
Capacity | Total capacity ~5 million tons of pig iron/year
Input materials | Iron ore, coke, limestone
Operating temperature | ~1.800–2.200°C
Control technology | Modern PLC/SCADA automation and control system
Exhaust gas treatment | Has dust collection system, CO, SO₂, NOx gas treatment
Energy recovery | Integrated flue gas heat recovery (WHR) system for internal power generation
Blast furnace technology – BOF converter (BF-BOF route)
Hoa Phat Dung Quat factory uses the traditional steelmaking process from ore with three main stages:
Blast furnace iron smelting
Steelmaking from molten pig iron using converter furnace (BOF)
Finished steel rolling
✅ Advantage:
Produce high quality steel.
Proactive raw materials (ore, coke).
Suitable for large-scale, industrial production.

## Slide 9
1.2. ELECTRIC ARC FURNACE (EAF) TECHNOLOGY
Electric Arc Furnace (EAF)
Electric Arc Furnace (EAF) Process:
Input materials: Scrap steel, cast iron, DRI (direct reduced iron pellets).
Process:
  Electric Furnace (EAF): Scrap steel is melted by electricity.
  Ladle Furnace: Adjust chemical composition.
  Continuous casting: Create steel billets.
  Hot rolled/cold rolled: Similar process BF-BOF.
Advantage:
  Flexible, suitable for small markets.
  Emission reduction compared to BF-BOF.

## Slide 10
2. ROLLING AND PROCESSING STAGE
Characteristics: Use of modern rolling mills with automatic gauge control (AGC) and X-ray measurement systems to ensure high precision.
Galvanizing technology (NOF– Non-Oxidizing Furnace) is applied to enhance durability and corrosion resistance of cold-rolled steel coils.
Steel products undergo heat treatment (annealing, quenching, tempering) to improve microstructure and mechanical properties.
After steelmaking, steel billets (billet, slab, bloom) are sent to hot rolling or cold rolling mills to produce final products such as coil steel, rebar, structural steel, and steel pipes
Types of rolling | Workpiece temperature | Characteristic
Hot Rolling | > 900°C | Rolling the workpiece while it is still red hot – easy to deform, requires little force
Cold Rolling | Normal temperature | Hot rolled product – high precision, smooth surface
Intermediary Rolling | Between hot and cold | Less common
Energy consumption characteristics
Thermal energy: used for billet furnace – accounts for 60–70% of process energy.
Electricity: operate roller motor, conveyor belt, hydraulic system.
Typical consumption:
  Hot rolling: 2,5–3 GJ/ton
  Cold rolling: 1–1,5 GJ/ton

## Slide 11
3. INTEGRATION AND SYNCHRONIZATION
Value chain optimization
Large-scale technology lines are designed in a synchronized manner, from raw material processing to ironmaking, steelmaking, and finished steel rolling.
Waste reduction
A closed-loop system helps reduce waste and increase production efficiency. CO gas from the blast furnace is recovered and reused as fuel.
Production efficiency
Integrating production stages helps optimize the process and reduce production costs.

## Slide 12
4. APPLICATION OF ADVANCED TECHNOLOGY
Technology import
Many steel production lines in Vietnam are imported from countries with developed steel industries such as Italy, Japan, or South Korea.
Automation
The steel rolling lines use high automation technology, ensuring accuracy and product quality
Accuracy
Advanced technology helps produce steel with high accuracy, meeting international standards

## Slide 13
5. TOWARD TO “GREEN” STEEL PRODUCTION
Emission reduction
Vietnam's steel industry is adjusting its production lines to reduce emissions and meet international standards
Renewable energy
Using renewable energy to reduce carbon emissions
Coal gasification
Using coal gasification instead of FO oil to reduce pollution
Scrap recycling
  Enhancing steel scrap recycling in the EAF production line.

## Slide 14
6. AUTOMATION AND QUALITY CONTROL
100%
Automation
Modern technological line integrated with automation system (PLC).
Advanced
Measuring equipment
Advanced measuring equipment is used (such as X-ray thickness gauges).
International
Standard
Ensure the products meet international standards (JIS, ASTM, TCVN).

## Slide 15
7. DIVERSE SCALE
Large Enterprise
Own a large-capacity production line (millions of tons per year)
Small Factory
Focus on producing specialized steel or serving local demand.
Design Capacity
Ranging from 250,000 tons per year to 8 million tons per year

## Slide 16
8. COMPARISON TABLE OF ENERGY CONSUMPTION BY TECHNOLOGY
Technology | Actual level in Vietnam | Advanced level (EU, Japan)
BF – BOF | 22–28 GJ/ton of steel | 18–20 GJ/ton
EAF | 500–650 kWh/ton | < 400 kWh/ton
Compare with international advanced level (benchmark)
Steel Production Technology | Main Raw Materials | Energy Consumption Rate | Notes
Blast Furnace – Basic Oxygen Furnace (BF-BOF) | Iron ore, coke | 20–30 GJ/ton of steel (~5,500–8,300 kWh/ton) | Traditional technology, high CO₂ emissions
Electric Arc Furnace (EAF) | Scrap steel | 350–650 kWh/ton | Electricity-intensive, lower CO₂ emissions, more environmentally friendly
Induction Furnace (IF) | Scrap steel | 550–750 kWh/ton | Common in small plants, lower efficiency than EAF
Hòa Phát (modern BF) | Iron ore, coke | ~20–22 GJ/ton of pig iron (~5,500–6,100 kWh) | Includes furnace heat recovery, ISO 50001 certified
Pomina (improved EAF) | Scrap steel | ~500–550 kWh/ton | Integrated energy monitoring, optimized electrode usage

## Slide 17
2. CHARACTERISTICS OF STEEL PIPE
PRODUCTION TECHNOLOGY

## Slide 18
Hot Rolling Process
1. Material Loading
2. Flattening
3. Roughing Mill
4. Slitting
5. Roughing Mill
6. Tensioning
7. Coiling
8. Material Unloading
2.1. PRODUCTION LINE
Descaling Process
1. Material Loading
2. Pickling Tank 1
3. Pickling Trough
4. Rinsing Trough
5. Drying
6. Tensioning 1
7. Pickling Tank 2
8. Tensioning 2
9. Coiling
10. Material Unloading

## Slide 19
Cold Rolling Process
1. Material Loading
2. Pickling Tank
3. Stand 1
4. Stand 2
5. Stand 3
6. Stand 4
7. Coiling
8. Material Unloading
Annealing Process
1. Material Loading
2. Roughing Mill 1
3. Annealing Furnace
4. Rapid Cooling
5. Annealing Tank
6. Rapid Cooling Tower
7. Roughing Mill 2
8. Coiling
9. Material Unloading
Pipe Making Process
1. Uncoiling
2. Pickling Tank
3. Forming Roll Stand
4. High-Frequency Welding
5. Shaping Roll Stand
6. Cutting Table
7. Pipe Collection
8. Bundling
2.1. PRODUCTION LINE

## Slide 20
2.2 HEAT AND SURFACE TREATMENT PROCESS
Heat Treatment
Heat treatment (annealing, quenching, tempering) is carried out thoroughly to improve the mechanical properties of the steel.
Surface Plating
Surface plating technology (galvanizing) to increase durability and corrosion resistance.
Process | Target | Characteristic
Annealing | Reduce hardness, increase flexibility | Cool slowly in the furnace
Quenching | Increase hardness | Cool quickly after firing
Tempering | Tempering after quenching | Reheat at low temperature (150–650°C)
Normalizing | Improving microstructure | Air cooled
Carburizing, Nitriding | Increase surface hardness | Chemical and thermal combination
Typical heat treatment processes

## Slide 21
Surface Plating: Surface plating technology (galvanizing) to increase durability and corrosion resistance.
1. Degreasing
Target: Remove grease and dirt on steel surface.
Method: Use alkaline solution (NaOH) or organic solvent.
Note: If not cleaned thoroughly, the plating will not adhere firmly.
2. Pickling
Target: Remove rust (iron oxide) from steel surface.
Method: Soak in dilute acid solution, usually HCl or H₂SO₄.
Cleaning time: 5–20 minutes, depending on rust thickness.
3. Water Rinse
Target: Remove residual acid after pickling step.
Rinse with clean water and drain before moving on to the next step.
4. Fluxing
Target: Create a thin coating (ZnCl₂ – NH₄Cl) to support better zinc adhesion and prevent temporary oxidation.
Method: Dip in saline flux solution.
5. Hot-dip Galvanizing
Target: Dip steel into molten zinc bath (~450°C).
Application: Zinc and iron form a metal-metal reaction bond - Fe-Zn alloy, very good corrosion resistance.
Dipping time: depends on product thickness.
6. Cool and test
Cool with air, water or special solution.
Check plating layer: thickness, adhesion, surface (according to JIS, ASTM or TCVN standards).
Can be passivated to increase rust resistance (if required).
2.2 HEAT AND SURFACE TREATMENT PROCESS

## Slide 22
Hot Rolling Process
1. Material Loading
2. Flattening
3. Roughing Mill
4. Slitting
5. Roughing Mill
6. Tensioning
7. Coiling
8. Material Unloading
Descaling Process
1. Material Loading
2. Pickling Tank 1
3. Pickling Trough
4. Rinsing Trough
5. Drying
6. Tensioning 1
7. Pickling Tank 2
8. Tensioning 2
9. Coiling
10. Material Unloading
2.2 HEAT AND SURFACE TREATMENT PROCESS

## Slide 23: 3. ENERGY SUPPLY SYSTEM
3.1 Heat supply system and furnace
Induction kiln (billet steel) / Heating furnace (hot-rolled tube steel): Increase the temperature of the billet or coil to 1200–1300°C.
Auxiliary equipment: Combustion equipment, heat controller, chimney – exhaust fan.
3.2 Hydraulic system – lubrication
3.3 Water supply and cooling system
Cooling water circulation system: Cooling workpieces, furnaces, large motors. Inlet water treatment system: Removal of sediment, ions – protection of thermal equipment.
Hydraulic system: Provides control force to mechanical equipment. Lubrication system: Reduce friction, increase the life of the rotating equipment.

## Slide 24: 3. ENERGY SUPPLY SYSTEM
Power substation and distribution cabinet: Supply power to the whole plant. SCADA/PLC control system: Automation, process monitoring.
3.4 Electrical – Control System
3.5 Fuel and gas systems
Gas supply system: Supply NG, CO/H2 gas, blast furnace gas. Oxygen supply system, inert gas: Used in steelmaking and welding.
3.6 Compress air system
Supply compressed air to actuators, valves, cleaning equipment.
3.7 Ventilation – vacuum – inert gas treatment system
Dust extraction system: Suction of smoke and dust from furnaces, welders, rolling machines. Exhaust gas treatment system: SO2, NOx, CO, fine dust treatment.

## Slide 25: 3. ENERGY SUPPLY SYSTEM
3.8 Laboratory Systems – Testing
Product quality assurance: chemical, mechanical, ultrasonic testing,...
3.9 Other systems
System | Main Function
Fire Protection System | Fire and explosion warning, fire suppression using water, foam, CO₂ gas
Thermal Load Balancing System | Utilize excess heat – heat exchange between workshops
Internal Transportation System | Forklifts, trolleys, overhead cranes for transporting billets, steel coils, etc.
Storage and Packaging System | Preserve and transport steel billets/pipes to customers

## Slide 26: Q&A
1: What’s the difference between BOF and EAF in steel production?
2: Why are many countries shifting from BOF to EAF?
3: What is the difference between hot rolling and cold rolling in steel processing?
4: What are the environmental challenges of old steel technologies?

## Slide 27
THANK YOU