## Slide 1: TRAINING PROGRAMME FOR IEs
MANAGEMENT OFFICERS
Module 9.1:
Typical energy efficiency opportunities in steel industry production lines.

## Slide 2: CONTENT
Overview of the steel industry and its potential for energy savings Case studies Tools to monitor and evaluate the effectiveness of EE investment
Notes: Hợp đồng hiệu quả năng lượng (EPC): là hợp đồng ký kết giữa ESCO và Khách hàng để thực hiện dịch vụ sử dụng năng lượng tiết kiệm và hiệu quả.
– Hợp đồng chia sẻ mức tiết kiệm năng lượng: ESCO chịu mọi rủi ro tài chính và kỹ thuật của dự án bằng cách thu xếp tài chính để thực hiện dự án đầu tư lắp đặt các trang thiết bị hiệu quả năng lượng tại cơ sở sử dụng năng lượng của khách hàng
– Hợp đồng đảm bảo mức tiết kiệm năng lượng: ESCO chịu trách nhiệm cung cấp, thiết kế, lắp đặt, đo lường và đảm bảo hiệu quả giải pháp sử dụng năng lượng tiết kiệm và hiệu quả cho khách hàng.

## Slide 3
1. Overview of the steel industry and its potential for energy savings

## Slide 4
Overview of the Steel Industry and Energy Saving Potential
The steel industry is a highly energy-intensive sector, especially in the following processes:
Ironmaking using blast furnaces (BF) or electric arc furnaces (EAF)
Hot rolling and cold rolling
Billet reheating and continuous casting
Thermal and electrical energy account for the majority of consumption:
Thermal energy: Used in the form of coke, coal gas, DO/FO oil, or natural gas
Electricity: Used for EAF operation, steel rolling, and auxiliary systems
1. Overview

## Slide 5
Blast furnace in Hoa Phat
Arc furnace in Viet Nhat
Cold Rolled
Hot Rolled
1. Overview

## Slide 6
2. Energy efficiency measures

## Slide 7
2. Case studies (1)
Current Status Before Improvement:
The exhaust gas from the blast furnace (Blast Furnace Gas - BFG) has a high temperature (~200–250°C). After passing through the cleaning system, part of it is released through the chimney, leading to energy waste and CO₂ emissions.
The residual heat in BFG has not been fully utilized for other beneficial purposes such as steam generation or electricity production.
Proposed Solution:
Install a system to recover waste heat from blast furnace exhaust gas using heat exchangers, waste heat boilers, or ORC/Steam turbines.
The recovered heat can be used for:
Producing steam to serve internal needs (heating, drying, system operations).
Generating electricity by directing the steam to a turbine (if the capacity is sufficient).
Case study 1: Thai Nguyen Iron and Steel Joint Stock Company (TISCO)

## Slide 8
Implemented Solutions:
Recovered waste heat from the blast furnace exhaust to produce steam for power generation via turbine
Upgraded the smoke extraction fan system with variable frequency drives (VFDs)
Installed equipment to monitor and control compressed air leakage
Results:
Reduced thermal energy consumption: 8–12%
Internal power generation from waste heat: ~12 million kWh/year
CO₂ reduction: 2,000–3,000 tons/year
Estimate ROI between 2–5 years
2. Case studies (1)
Case study 1: Thai Nguyen Iron and Steel Joint Stock Company (TISCO)

## Slide 9
2. Các nghiên cứu điển hình (1)
Case study 1: Thai Nguyen Iron and Steel Joint Stock Company (TISCO)
Indicator | Estimated Value
Recovered Heat | ~100–150 GJ/h (depending on BFG flow rate)
Steam Generation | ~10–20 tons of steam/hour (low to medium pressure)
Potential Power Output | ~1–2 MW (with sufficiently large recovery system)
Fuel Savings | Reduced oil/coal consumption for boilers
CO₂ Emission Reduction | ~5,000–10,000 tons of CO₂/year (estimated)
Detailed Achieved Benefits

## Slide 10
Current Status Before Improvement
The blast furnace operates with a suboptimal pulverized coal injection (PCI) rate, resulting in high consumption of coke and auxiliary fuel (FO – fuel oil).
Collected blast furnace gas (BFG) is mostly vented or used inefficiently.
Fuel oil (FO) is still used in heating systems and auxiliary burners, increasing fuel costs and CO₂ emissions.
Proposed Solutions
Blast Furnace Technical Improvements
  Increase the hot blast air temperature to the optimal range (~1,200–1,250°C).
  Precisely control the PCI rate to gradually replace coke and reduce fossil fuel consumption.
BFG Reuse
  Collect and treat BFG through a cleaning system (cyclone – scrubber).
  Replace FO with BFG in auxiliary heat-generating equipment such as:
    Boilers, reheating furnaces, billet heating systems
    Heat transfer oil heating units
Case Study 2: Hòa Phát Steel Plant – Hải Dương
2. Case studies (2)

## Slide 11
Implemented Solutions:
Upgraded the blast furnace, controlling the ratio of hot blast and pulverized coal injection (PCI)
Installed oxygen enrichment equipment
Automated the material feeding system and temperature control
Utilized blast furnace gas (BFG) as fuel instead of fuel oil (FO)
Results:
Increased furnace efficiency: ~4%
Reduced fuel costs: 5–8%
Reduced GHG emissions equivalent to 5,000 tons of CO₂/year
2. Case studies (2)
Case Study 2: Hòa Phát Steel Plant – Hải Dương

## Slide 12
2. Case studies (2)
Case Study 2: Hòa Phát Steel Plant – Hải Dương
Indicator | Estimated Value
Reduction in coke consumption rate | ~20–30 kg per ton of hot metal
Increase in PCI (Pulverized Coal Injection) rate | From ~100 kg/ton to 140–180 kg/ton of hot metal
Reduction in FO consumption | 100% eliminated at locations replaced by BFG
Reuse rate of BFG | ~80–90% of the generated blast furnace gas
CO₂ emissions reduction | ~10,000–15,000 tons of CO₂/year
Fuel cost savings | Tens of billions of VND per year (depending on fuel prices)
Detailed Achieved Benefits

## Slide 13
2. Case studies (3)
Current Status Before Improvement
The EAF (Electric Arc Furnace) operated under a fixed voltage control mode, making it difficult to adapt to fluctuations in input resistance caused by changes in raw materials (scrap).
This led to issues such as:
Phase imbalance
Increased electricity consumption
Longer steelmaking time and higher electrode wear
Low power factor, high energy loss, and significant indirect CO₂ emissions
Proposed Solution
Install a Smart Voltage Control System (SVCS) integrated with the EAF’s automatic control system
SVCS continuously monitors the electrical load and automatically adjusts arc voltage to match variations in scrap properties
Combine optimized voltage-current control to shorten melting cycles and reduce energy loss
Integrate with an Energy Management System (EMS) to monitor and evaluate operational efficiency in real time
Case Study 3: Posco Yamato Vina Co., Ltd – Nhà Bè

## Slide 14
Implemented Solutions:
Optimized EAF (Electric Arc Furnace) operation using a smart voltage control system
Increased billet production capacity without increasing electricity consumption
Implemented full LED lighting across the entire plant
Results:
Reduced electricity consumption: 10–15 kWh per ton of steel
ROI under 2 years for both the LED system and the new EAF control system
Improved working conditions for employees
2. Case studies (3)
Case Study 3: Posco Yamato Vina Co., Ltd – Nhà Bè

## Slide 15
2. Case studies (3)
Case Study 3: Posco Yamato Vina Co., Ltd – Nhà Bè
Detailed Achieved Benefits
Indicator | Estimated Value
Reduction in electricity consumption | ~30–40 kWh per ton of steel (~5–8% reduction compared to before)
Reduction in melting cycle time | ~5–10 minutes per batch
Reduction in electrode wear | ~10–15%
Improvement in power factor | From ~0.85 to >0.95
Annual electricity cost savings | ~VND 5–10 billion (depending on production scale)
Reduction in indirect CO₂ emissions | ~3,000–5,000 tons of CO₂/year

## Slide 16
Current Status Before Improvement
Most large motors used in the pumping systems, fans, conveyors, and rolling mills were standard IE1 or IE2 motors with low efficiency.
Many motors operated at fixed speeds, with flow controlled mechanically (via valves) or manually, resulting in significant energy waste.
The load factor of many motors was below 50% of rated capacity, leading to low energy utilization efficiency.
Proposed Solution
Gradually replace standard motors with IE3 high-efficiency motors that meet international standards.
Install Variable Speed Drives (VSDs) to adjust motor speeds based on actual demand, especially for:
  Combustion air supply/exhaust fans in reheating furnaces
  Cooling water circulation pumps
  Raw material and product conveyors
Integrate automatic control systems using pressure, flow, or output temperature signals to optimize operational efficiency.
Case Study 4: Southern Steel Company – VNSTEEL
2. Case studies (4)

## Slide 17
Implemented Solutions:
Replaced standard motors with IE3 high-efficiency motors, combined with Variable Speed Drives (VSDs)
Synchronized the steam – compressed air – cooling water systems
Conducted comprehensive energy mapping for the entire plant
Results:
Saved 1.5–2 million kWh of electricity per year
Reduced peak load pressure on the power system
Return on Investment (ROI): approximately 1.5 years
Case Study 4: Southern Steel Company – VNSTEEL
2. Case studies (4)

## Slide 18: 2. Case studies (4)
Detailed Achieved Benefits
Indicator | Estimated Value
Electricity savings | ~1.5–2 million kWh/year
Reduction in peak load pressure | Significant reduction in demand on the power system
ROI (Return on Investment) | ~1.5 years
System optimization | Steam – compressed air – cooling water systems fully synchronized
Energy mapping coverage | 100% of plant energy systems mapped
Non-energy benefits | Reduced maintenance costs, extended equipment lifespan
Operational control improvement | Automatic adjustment based on real-time demand via VSDs

## Slide 19
2. Case studies
Solution Group | Real-World Example | Energy Saving Potential
Optimization of iron/steelmaking process | Hoa Phat Blast Furnace, Posco EAF | 5–10%
Waste heat recovery | TISCO, Hoa Phat | 10–15%
Variable speed drives & high-efficiency motors | VNSTEEL, Posco | 3–7%
Utilization of furnace exhaust gas | Hoa Phat | Fuel cost reduction of 5–8%
High-efficiency lighting | LED for entire factory | 60–70% of lighting electricity savings
Energy management (ISO 50001) | Some factories have started applying | 3–5%
Summary of Typical Solution Groups

## Slide 20: Q & A
In the last few year your company invested in which technology for enenrgy saving and effeciency?
In thoes invest project, how you get the funded? Or your company know any source for funding EE project?

## Slide 21
THANK YOU