## Slide 1: TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs
Module 8.2:
Energy efficiency opportunities in cement production lines
MANAGEMENT OFFICERS

## Slide 2: CEMENT INDUSTRY

## Slide 3: CONTENT
I. Information on energy efficiency (EE) opportunities for the cement industry II. Some typical measures are proposed

## Slide 4: I. INFORMATION ABOUT EE OPPORTUNITIES FOR THE CEMENT INDUSTRY
Notes: Hợp đồng hiệu quả năng lượng (EPC): là hợp đồng ký kết giữa ESCO và Khách hàng để thực hiện dịch vụ sử dụng năng lượng tiết kiệm và hiệu quả.
– Hợp đồng chia sẻ mức tiết kiệm năng lượng: ESCO chịu mọi rủi ro tài chính và kỹ thuật của dự án bằng cách thu xếp tài chính để thực hiện dự án đầu tư lắp đặt các trang thiết bị hiệu quả năng lượng tại cơ sở sử dụng năng lượng của khách hàng
– Hợp đồng đảm bảo mức tiết kiệm năng lượng: ESCO chịu trách nhiệm cung cấp, thiết kế, lắp đặt, đo lường và đảm bảo hiệu quả giải pháp sử dụng năng lượng tiết kiệm và hiệu quả cho khách hàng.

## Slide 5
1. OPPORTUNITY TO RENOVATE THE KILN SYSTEM
Problem 1: Poor sealing performance
The sealing efficiency of the kiln inlet and outlet sealing devices is insufficient, which increases the system's heat consumption. The current kiln head and tail sealing devices still use relatively old sealing designs, such as fish scale or friction block types. These sealing devices wear out quickly, resulting in suboptimal sealing performance. Severe air leakage, material spillage, and other undesirable phenomena frequently occur. This not only increases the system’s energy consumption but also negatively impacts the on-site environment and compromises the safety of workers and equipment.

## Slide 6
When the coal mill is stopped, excessive fluctuations will occur in the coal powder feeders at the kiln inlet and outlet, severely affecting the stability of the kiln system's operating conditions.
Pressure fluctuations of the Roots blower for the coal feeder are a concerning issue. All of these problems typically occur during the initial design phase of the cement production line. After retrofit measures were implemented, the thermal energy consumption index of this plant was reduced to below 700 kcal/kg.cl.
1. OPPORTUNITY TO RENOVATE THE KILN SYSTEM
Problem 2: Fluctuations in coal powder balance

## Slide 7
Calciner plays an important role in the clinker firing process. Calciner renovation helps to optimize heat transfer and reduce energy consumption. Renovation solutions include changing the internal design, using better heat-resistant materials and improving the control system.
2. CALCINER RETROFIT OPPORTUNITIES

## Slide 8
3. KILN TAIL GAS CHAMBER RETROFIT OPPORTUNITIES
The kiln tail gas chamber is where exhaust gases from the kiln are collected and treated. Retrofitting the
kiln tail gas chamber helps reduce the emission of dust and harmful gases into the environment, while also
recovering heat for reuse.

## Slide 9
4. OPPORTUNITIES FOR RENOVATING THE MATERIAL
DISTRIBUTION BOX OF THE HEAT EXCHANGER TOWER
The material distribution box of the heat exchanger tower plays the role of evenly distributing the material throughout the tower, ensuring optimal heat exchange efficiency. Renovating the material distribution box helps enhance heat exchange performance and reduce energy consumption.

## Slide 10
5. OPPORTUNITIES FOR RENOVATING THE SEALING EQUIPMENT
OF THE FURNACE HEAD AND TAIL
Renovating the sealing equipment of the furnace head and tail is an important solution to minimize gas leaks
and heat loss. Modern sealing equipment uses advanced technology, ensuring high sealing efficiency and long
service life.

## Slide 11
6. OPPORTUNITIES FOR OPTIMIZING THE COOLING RECORDER EQUIPMENT
Implement the improvement and optimization of the wind distribution and wind mixing method of the cooling grate fan. The main measures are as follows: Optimize the wind distribution of the fan in the high temperature section, adjust the wind volume and pressure of the fan so that the total wind flow in the high temperature section meets the air supply demand of the furnace, and the ventilation density and wind pressure of each position meet the cooling demand of the material on the grate surface. The ventilation beam and the fixed grate do not need to be improved, but optimize the wind distribution method of the static grate, adjust the ventilation density, and wind pressure in each position of the static grate. Replace the four cooling grate fans with high-efficiency energy-saving fans, which not only meet the air supply demand of the furnace, but also realize the purpose of reducing power consumption.

## Slide 12
6. OPPORTUNITIES FOR OPTIMIZING THE COOLING RECORDER EQUIPMENT
Equipment Code | Usage Location | Air Volume (m³/h) | Pressure (Pa) | Rated Power (KW) | Rated Current (A) | Motor Speed (rpm) | Note
471FN02 | Fixed (Front) | 37960 | 12500 | 200 | 352 | 2970 | 
471FN03 | Fixed (Right) | 27360 | 10000 | 132 | 234 | 2940 | 
471FN04 | Fixed (Left) | 27360 | 10000 | 132 | 234 | 2940 | 
471FN05 | Room 1 | 59184 | 6980 | 160 | 285 | 1480 | Old motor can be reused
471FN06 | Room 2 | 85968 | 6700 | 185 | 352 | 1470 | Old motor can be reused
471FN07 | Room 3 | 85968 | 6700 | 185 | 352 | 1470 | Old motor can be reused
471FN08 | Room 4 | 87840 | 4900 | 220 | 387 | 1450 | 
471FN09 | Room 5 | 87840 | 4900 | 220 | 387 | 1450 | 
471FN10 | Room 6 | 87840 | 4900 | 220 | 387 | 1450 | 
471FN11 | Room 7 | 87840 | 4900 | 220 | 387 | 1450 | 
471FN12 | Room 8 | 93600 | 4200 | 200 | 352 | 1450 | 
Total |  | 768760 |  | 2074 | 3709 |  | 

## Slide 13
7. OPPORTUNITIES FOR RENOVATING AND OPTIMIZING
THE COAL POWDER TRANSPORT SYSTEM AND BURNER NOZZLES
The current coal powder transport pipes are significantly larger than the actual demand, leading to waste of heat and electricity. Optimizing the pipe size based on the actual coal consumption will significantly reduce the use of fans, thereby saving both coal and electricity.
Modern burner nozzles at the kiln head have addressed the problem of material caking, but limitations remain due to high airflow rates and motor power losses. Excessive use of cold air leads to wasted energy consumption. Selecting new burner nozzles with "low primary wind, high pressure" will thoroughly resolve the material caking issue and improve energy-saving efficiency.
Reducing the amount of air required for the combustion process helps minimize heat loss, thereby saving fuel and lowering operating costs.

## Slide 14
8. OPPORTUNITY TO RENOVATE COAL POWDER STORAGE TANKS
AT THE HEAD AND TAIL OF THE FURNACE
The coal powder weighers at the kiln head and kiln tail are currently experiencing excessive fluctuations when the coal mill stops. Variations in the coal powder flow into the storage hopper significantly affect the stability of the discharge process from the coal powder hopper, causing fluctuations in the coal powder weighers.
The material flow stabilizing hopper ensures that starting and stopping the coal mill will not cause fluctuations in the coal powder weighers. This helps maintain the stability of the production process and minimize potential issues.

## Slide 15
9. OPPORTUNITY TO RECOVER HEAT FROM AQC AND SP BOILER
DISCHARGE WATER TO HEAT FEED WATER
AQC, SP Heat Recovery Furnace:
  Lines 1 and 2 have waste heat recovery furnaces from exhaust gas in cement production.
  Boiler discharge water during operation is discharged directly into the environment.
  Wastewater parameters:
    Pressure: 1.3 MPa.
    Flow Rate: 100 – 120 m³/day per production line.
    Water temperature: 25 – 28°C.
Water Supply System:
  Required make-up water volume: 150 m³/day/production line.
  Currently, the feedwater entering the deaerator is at a low temperature (25°C).

## Slide 16
9. OPPORTUNITY TO RECOVER HEAT FROM AQC AND SP BOILER
DISCHARGE WATER TO HEAT FEED WATER.
Heat recovery from AQC and SP boiler blowdown to preheat make-up water.
Install the necessary equipment:
  Boiler blowdown tank.
  Blowdown and expansion steam piping.
  Heat exchanger for feedwater heating.
  Boiler blowdown storage tank.
  Recover heat from the boiler blowdown using AQC and SP to heat the supplementary feedwater, in order to utilize waste heat and reduce energy costs. Store the blowdown water in a tank for reuse as a source of circulating cooling water.
  Operating principle: The boiler blowdown from AQC and SP is directed to the storage tank. The expansion steam from the blowdown is recovered and routed into the heat exchanger, where the supplementary feedwater is heated. The blowdown water is then stored and reused in the cooling water circulation system for the condenser.
  Benefits Analysis:
Increase the feedwater temperature:
  Supplementary feedwater (150 m³/day/line) is heated from 25°C to 90–95°C.
  Reduce energy consumption for the deaeration and feedwater heating system.
  Reduce water consumption: The blowdown water is utilized for the cooling water circulation system of the condenser, reducing the amount of fresh feedwater required.

## Slide 17
9. OPPORTUNITY TO RECOVER HEAT FROM AQC AND SP BOILER
DISCHARGE WATER TO HEAT FEED WATER.

## Slide 18
10. EXPECTED REDUCTION IN CONSUMPTION IN SPECIFIC MEASURE
Total coal consumption is expected to decrease

## Slide 19
Auxiliary System | Energy Saving Potential | Improvement Measures
Compressed Air System | 15–30% | - Reduce leaks - Optimize operating pressure - Install inverters for compressors - Recover heat from compressed air - Perform regular maintenance
Process Fans & Dust Collection | 10–25% | - Install inverters for large fans - Optimize fan blades and ductwork - Replace with high-efficiency fans - Optimize load-based operation
Cooling Water System | 10–20% | - Use inverters for pumps - Optimize cooling process - Improve pipe insulation - Install automatic control sensors
Dust Filtration System | 5–15% | - Optimize dust cleaning cycles - Reduce pressure loss across filters - Install inverters for suction fans - Replace with high-efficiency filter bags
11. ENERGY EFFICIECNCY POTENTIAL OF AUXILIARY SYSTEMS

## Slide 20
11. ENERGY EFFICIECNCY POTENTIAL OF AUXILIARY SYSTEMS
Auxiliary System | Energy Saving Potential | Improvement Measures
Lighting System | 30–60% | - Replace with LED lamps - Use daylight and motion sensors - Optimize lighting layout
Material Feeding & Conveying System | 5–20% | - Use inverters for conveyors and bucket elevators - Control based on load - Lubricate and align motors properly
Water and Chemical Pumps | 10–25% | - Install inverters - Reduce head loss - Optimize piping system
Air Conditioning & HVAC System | 10–30% | - Optimize set temperature - Use inverters for fans and compressors - Improve room insulation

## Slide 21: 12. ENHANCING INTERNAL MANAGEMENT AND EQUIPMENT MAINTENANCE
For the electrical equipment system
Regularly propagate and train employees on energy efficiency. Enhance the involvement of operational staff (Electricity savings should be based on a broad foundation and require the support of operational staff).
Monitor energy consumption based on the number of production and non-production days to identify and address energy loss points. Develop procedures and checklists to ensure that equipment shutdowns have been properly carried out.
Install automatic control devices to turn off equipment when not in use
Turn off all unnecessary lights (such as during breaks, lunch hours, shift changes, and holidays).
Install power factor correction capacitors to create a "leading" power factor to address the "lagging" power factor of equipment. These capacitors can be installed at individual devices or multiple devices to control part or the entire distribution system.
Control the surrounding temperature to extend the insulation lifespan and reliability of the motors. Avoid direct exposure to sunlight, place motors in well-ventilated areas, and keep the motors clean.

## Slide 22: 12. ENHANCING INTERNAL MANAGEMENT AND EQUIPMENT MAINTENANCE
For the refrigeration and air conditioning systems
Clean and regularly replace filters, clean the evaporator equipment and condenser coils to improve the cooling efficiency of the air conditioning system.
Set the air conditioning system temperature appropriately. The temperature should be set between 26°C and 27°C in summer, and not too high or low. Setting the temperature too low will cause the air conditioner to run longer. Each 1°C reduction in temperature will increase energy consumption by 3-4% of the air conditioning system’s power usage.
For the compressed air system
Train and raise employee awareness to operate and maintain the compressed air system effectively.
Ensure the system remains dry. Ensure proper drainage slope, discharge points, and vents to minimize rusting of pipes.
Invest in leak detection equipment or gas leak testers to measure total leakage and compressor power. Identify and fix any compressed air leaks, and prevent recurrence.

## Slide 23: 12. ENHANCING INTERNAL MANAGEMENT AND EQUIPMENT MAINTENANCE
  For office buildings
  Check the insulation thickness of walls and roofs.
  Review and seal gaps that lead to heat loss from the rooms.
  Use curtains, both inside and outside windows, to retain heat in winter and keep cool in summer.
  Install sunshades for windows to reduce heat during the summer.
  Install automatic door and gate systems.
  Install double-glazed doors and windbreak doors on the northwest side.
  Set air conditioning to temperatures above 26°C in summer and 23°C in winter.
  Turn off all lighting equipment when not in use or after working hours.

## Slide 24: II. SOME TYPICAL MEASURES ARE PROPOSED

## Slide 25: 1. Renovating the lighting system
a. Current situation
The lighting system in the workshop mainly consists of 400W, 250W, and 125W mercury vapor lamps and T8 fluorescent lamps with electromagnetic ballasts. The Company's lighting devices are all low-efficiency equipment, leading to high electricity consumption during use.
b. Describe measures
Measure: “ Renovating the lighting system”
Implementation plan
Gradually replace 219 400W mercury vapor lamps with 250W sodium vapor lamps.
Gradually replace 176 250W mercury vapor lamps with 150W sodium vapor lamps.
Gradually replace 126 125W mercury vapor lamps with 70W sodium vapor lamps.
Gradually replace 3,170 T8 fluorescent lamps, 1.2m, 36W, with electromagnetic ballasts (12W) with T5 fluorescent lamps, 1.2m, 28W, and electronic ballasts (3.5W), maintaining equivalent brightness.

## Slide 26: 1. Renovating the lighting system
Technical Specifications of Typical Lights
Technical Specifications of Typical Lights
b. Describe measures

## Slide 27: 1. Renovating the lighting system
Principles of energy efficiency
Improve lighting efficiency by replacing existing low-efficiency lighting devices with high-efficiency lighting devices while ensuring the necessary lighting quality requirements
250W sodium high-pressure lamps and metal halide fluorescent lamps
b. Describe measures

## Slide 28: 1. Renovating the lighting system
No | Specification | Unit | Value
1 | The average electricity price of the company for the first 10 months of 2015 | VND | 1.355
2 | Electricity saved after implementing the measure | kWh/year | 327.439
3 | Income from energy efficiency in one year | Million VND/year | 444
4 | Total investment cost for project implementation | Million VND | 998
5 | Simple payback period | month | 27,0
6 | Discount rate | % | 10
7 | Project lifecycle | year | 4
8 | Net Present Value (NPV) of the project | Million VND | 509
9 | Internal Rate of Return (IRR) | % | 31%
10 | Payback period of the investment project | tone/year | 30,5

## Slide 29
1. Current situation
The company's compressed air station consists of 5 air compressors, each with a capacity of 200kW (4 running and 1 backup), with manual control and pressure set for each machine from 6.3 to 6.5 bar. The idle running time of the machines is less than 10% of the total running time. When operating in idle mode, the compressors still consume about 40% of their rated power without generating compressed air, leading to energy waste.
Measures
“Install an inverter combined with a centralized controller for the air compressor station”.
2. Install inverters combined with a general controller for the compressor station

## Slide 30
Energy consumption of the air compressor station is based on the compressed air flow produced.
The chart compares the pressure fluctuations of a compressor with a frequency inverter to those of other compressors.
2. Install inverters combined with a general controller for the compressor station
b. Describe measures

## Slide 31
Function of the compressor station controller
Automatically operates the compressors in the system based on the compressed air demand of production.
Sets the operating schedule for the compressors to match production times.
Synchronizes operating hours and the number of starts: ensures stable air quality, facilitating maintenance and servicing of the compressor system.
Diagram of the connection of the controller in coordination with the air compressors.
2. Install inverters combined with a general controller for the compressor station
b. Describe measures

## Slide 32
NO | SPECIFICATIONS | UNIT | VALUE
1 | The average electricity price of the company for the first 10 months of 2015 | VND | 1.355
2 | Electricity saved after implementing the measure | kWh/year | 354.816
3 | Income from energy efficiency in one year | Million VND/year | 481
4 | Total investment cost for project implementation | Million VND | 640
5 | Simple payback period | month | 16,0
6 | Discount rate | % | 10
7 | Project lifecycle | year | 10
8 | Net Present Value (NPV) of the project | Million VND | 2937
9 | Internal Rate of Return (IRR) | % | 80%
10 | Payback period of the investment project | tone/year | 40,6
2. Install inverters combined with a general controller for the compressor station
c. Calculate the potential for EE for the measure

## Slide 33: 3. Install ENPOSS - DORCE harmonic filter devices for the rectifier system supplying power to the kiln and drying furnace units in lines 1 and 2
a. Current situation
Most of the clinker cooling fan devices of the company are equipped with inverters for control, and the fan speed is controlled by the operator depending on the production operating conditions. The inlet and outlet air direction vane valves are fully open (100%) when using the inverter
Measurement results of electricity quality in the drying & firing area
Comment: The harmonic levels in the above areas are all higher than the allowed standard.

## Slide 34: 3. Install ENPOSS - DORCE harmonic filter devices for the rectifier system supplying power to the kiln and drying furnace units in lines 1 and 2
Measure:
Currently, there are two types of measures for preventing harmonic waves on the market: using inductors (passive components) and using active components (active filters). The active filter emits pulses to reduce the distortion of the power supply.
A widely certified and commonly used product is the ENPOSS product, which can save from 7-15% of electricity consumption (according to the manufacturer's evaluation).
Illustrating the effectiveness of the ENPOSS - FORCE harmonic filter
b. Describe measures

## Slide 35: 3. Install ENPOSS - DORCE harmonic filter devices for the rectifier system supplying power to the kiln and drying furnace units in lines 1 and 2
Installation Diagram of FORCE Equipment
b. Describe measures

## Slide 36: 3. Install ENPOSS - DORCE harmonic filter devices for the rectifier system supplying power to the kiln and drying furnace units in lines 1 and 2
NO | Position | Temperature, oC | Avarage temperatura oC
1 | Cooling Tower | 320-350 | 330
2 | Clinker Cooling | 280-332 | 310
b. Describe measures

## Slide 37: 3. Install ENPOSS - DORCE harmonic filter devices for the rectifier system supplying power to the kiln and drying furnace units in lines 1 and 2
No | Parameter | Unit | Value
1 | Average electricity price of the Company in the first 9 months of 2015 | VND | 1,355
2 | Electricity saved after implementing the solution | kWh/year | 554,400
3 | Income from energy savings in 1 year | Million VND/year | 751.2
4 | Investment rate for ENPOSS FORCE harmonic filter equipment | USD/kW | 45
5 | Exchange rate | VND/USD | 21,673
6 | Total actual investment cost of the project | Million VND | 1,170
7 | Simple payback period | months | 18.7
8 | Discount rate | % | 10
9 | Project lifetime | years | 5
10 | Net profit of the project (NPV) | Million VND | 1,947.6
11 | Internal rate of return (IRR) | % | 62%
12 | Project investment payback period | months | 21.0
c. Calculate the potential for EE for the measure

## Slide 38: 4. Utilizing the waste heat from the clinker kiln flue gas and the exhaust air from the clinker cooling process to generate electricity
Principle diagram of the clinker production system
a. Current situation

## Slide 39: 4. Utilizing the waste heat from the clinker kiln flue gas and the exhaust air from the clinker cooling process to generate el
The installed capacity of the power generation system is 7.5 MW, with a load factor of 85%. The average generation capacity will be 6.4 MW.
The estimated investment cost is approximately 2.5 million USD per 1 MW of installed capacity.
b. Describe measures

## Slide 40: 4. Utilizing the waste heat from the clinker kiln flue gas and the exhaust air from the clinker cooling process to generate el
Summary of key economic and technical indicators for the power plant system for various clinker kiln capacities
NO | Economic and Technical Specifications of the Power Plant | Unit | Clinker Kiln Index (tons per day) |  | 
 |  |  | 2500T | 4000T | 5000T
1 | Installed Capacity | MW | 4,5 | 7,5 | 9,0
2 | Average Power Generation Capacity | MW | 4,0 | 7,0 | 8,6
3 | Operating time per year ( | Hour | 7200 | 7200 | 7200
4 | Electricity generation per year | MWh | 28800 | 50000 | 62000
5 | Technical Staff for Station Operation | Person | 10 | 10 | 10
6 | Total investment. | Million USD | 9-12 | 15-20 | 18-22
c. Calculate the potential for EE for the measure

## Slide 41: 4. Utilizing the waste heat from the clinker kiln flue gas and the exhaust air from the clinker cooling process to generate el
Financial indicators table for investment in energy efficiency measure No. 5.
NO | SPECIFICATION | UNIT | VALUE
1 | Total investment | Million VND | 406.369
2 | Electrical energy saved after implementing the energy efficiency measure | kWh/year | 50.688.000
3 | Average electricity price for the first 10 months of 2015 | VND/kWh | 1.355
4 | Cost savings after implementing the energy efficiency measure. | million VND/year | 68.682
5 | Simple payback period | month | 71
6 | Discount rate | % | 10
7 | Project lifespan | year | 15
8 | Net Present Value (NPV). | Million VND | 256.441
9 | Payback Period | month | 110
10 | Amount of CO2 emissions reduction | Tone /year | 42.035
c. Calculate the potential for EE for the measure

## Slide 42: 5. Installing inverters for the calciner fans 421FN02
.
Current situation
The calciner system of the plant is supplied with air by a fan with the model code 421FN02M01, with a design capacity of 132 kW, a rated current (rc) Irc = 231A, rated speed n = 2975 rpm, and voltage 380V. Operating parameters: operating current (oc) Ioc = 138A, actual power consumption is approximately 70 kW.

## Slide 43: 5. Installing inverters for the calciner fans 421FN02
According to the fan characteristics, we have:
- Q1 / Q2 = n1 / n2 : The flow rate is directly proportional to the speed.
- H1 / H2 = (n1 / n2)2 : The pressure is proportional to the square of the speed.
- P1 / P2 = (n1 / n2)3 : The power is proportional to the cube of the speed.
b. Describe measures
Proposed measure: Install an inverter for the fan motor (421FN02) with a capacity of 132 kW and input voltage of 380V.

## Slide 44: 5. Installing inverters for the calciner fans 421FN02
Energy Saving Potential Calculator for Energy Efficiency Solution No. 6
NO | SPECIFICATION | UNIT | VALUE
1 | The average operating hours per day | hour | 24
2 | The average number of operating days per year. 4o mini | day | 330
3 | The total rated power of the equipment. | kW | 132
4 | The total average actual power of the equipment. | kW | 70
5 | The energy consumption of the baseline option. | kWh/year | 554.400
6 | The percentage of energy savings compared to the baseline option. | % | 25,0%
7 | Electrical energy consumption after implementing the measure. | kWh/year | 47.800
8 | Energy efficiency after implementing the measure. | kWh/year | 138.600
9 | Reduction in CO2 emissions | tone/year | 75,0
c. Calculate the potential for EE for the measure

## Slide 45: 6. Install an inverter for the exhaust fan of the grinding system 541FN03
a. Current situation:
The cement grinding machine has a fan with model number 541FN03M01, with a design power of 850 kW and an input voltage of 6 kV. Working parameters: working current Ilv = 64, actual power consumption is approximately 645 kW. The damper opening depends on the load, the kiln output, and is controlled by the operator from the central control room, with the intake damper opened at 60%. The actual working airflow of the fan is about 70% of the rated airflow. This load level is maintained regularly, accounting for up to 90% of the fan's operating time.

## Slide 46: 6. Install an inverter for the exhaust fan of the grinding system 541FN03
Measure: Install a variable frequency drive (VFD) for a fan motor (541FN03) with a power rating of 850 kW and an input voltage of 6 kV.
b. Describe measures

## Slide 47: 6. Install an inverter for the exhaust fan of the grinding system 541FN03
  Table of financial indicators for the investment in energy efficiency measure No. 7
NO | SPECIFICATION | UNIT | VALUE
1 | The average electricity price of the company in the first 9 months of 207. | VND | 1.355
2 | The electrical energy saved after implementing the energy efficiency measure. | kWh/year | 1.021.680
3 | The income generated from energy efficiency in one year. | Million VND/year | 1.384
4 | The total investment cost to implement the project. | Million VND | 3.150
5 | The simple payback period. | month | 27,3
6 | Discount rate. | % | 10
7 | Project lifetime. | year | 10
8 | Net Present Value (NPV) of the project. | Million VND | 7150
9 | Internal Rate of Return (IRR) of the project. | % | 47%
10 | The payback period of the project. | month | 38,7
c. Calculate the potential for EE for the measure

## Slide 48
7. UTILIZING THE HOT EXHAUST GASES FROM THE CLINKER COOLING PROCESS TO SUPPLY AIR TO THE PRIMARY AIR FAN AT THE KILN HEAD
Equipment | Air flow (m³/minute) | Air pressure (kPa) | Capacity (kW) | Note
Primary air fan for the burner | 180 | 58.8 | 250 | Code: ASF300
Roots blower for kiln inlet coal dosing | 112 | 61.0 | 185 | Code: S51
Roots blower for kiln outlet coal dosing | 122 | 57.0 | 185 | Code: S51
a. Current situation

## Slide 49
Proposed solution
Install a pipeline to conduct hot air discharged from the clinker cooling process (temperature about 110-130°C) to the first air supply fan for the furnace burner. This is to increase the temperature of the air supplied to the combustion process, thereby improving the thermal efficiency of the clinker kiln.
Energy efficiency potential:
By increasing the air temperature supplied to the combustion process by about 20°C, the thermal efficiency of the furnace can increase by 1%.
The amount of fuel supplied to the kiln inlet accounts for approximately 34% of the total fuel used for the kiln.
The amount of air supplied to the kiln inlet burner accounts for approximately 10% of the total air required for the combustion process.
By increasing the temperature of the combustion air from 28°C to 130°C (an increase of 102°C), the thermal efficiency of the kiln
7. UTILIZING THE HOT EXHAUST GASES FROM THE CLINKER COOLING PROCESS TO SUPPLY AIR TO THE PRIMARY AIR FAN AT THE KILN HEAD
b. Describe measures

## Slide 50
7. UTILIZING THE HOT EXHAUST GASES FROM THE CLINKER COOLING PROCESS TO SUPPLY AIR TO THE PRIMARY AIR FAN AT THE KILN HEAD
b. Describe measures

## Slide 51
7. UTILIZING THE HOT EXHAUST GASES FROM THE CLINKER COOLING PROCESS TO SUPPLY AIR TO THE PRIMARY AIR FAN AT THE KILN HEAD
No | Parameter | Symbol | Calculation formula | Unit | Value
Part 1: Energy efficiency |  |  |  |  | 
1 | Additional water supply flow | m | - | kg/day | 150000
2 | Temperature difference | ΔT | T2 ​−T1​ | °C | 65
3 | Specific heat of water | c | - | kJ/kg.°C | 4
4 | Heating temperature | Q | Q=m×c×ΔTQ | kJ/day | 40819500
5 | Convert energy to kWh | E | E=Q/3600 | kWh/day | 11339
6 | Power generation efficiency | η | - | % | 20,5
7 | Increased electricity output | Ed | Ed=E×η​ | kWh/day | 2324
8 | Average electricity price | P | - | VND/kWh | 1572
9 | Save on annual electricity costs | Cy | Ed×P×330 | Million VND/year | 1332,2
Part 2: Benefits of blowdown water |  |  |  |  | 
10 | Recovered discharge flow rate | Wx | mx×80% | m³/day | 96
11 | Water price | Pw | - | VND/m³ | 5000
12 | Benefits of saving water every year | Cw | Wx×Pw×330 | Million VND/year | 158,4
Part 3: Summary of benefits and economic indicators |  |  |  |  | 
13 | Total annual benefit | Ct | Cy​+Cw​ | Million VND/year | 1490,6
14 | Investment costs | I0 | - | Million VND | 3500
15 | Discount rate | r | - | % | 10
16 | Net present value (NPV) | NPV |  | Million VND | 7947
17 | Internal Rate of Return (IRR) | IRR | NPV=0 => IRR | % | 35,5
18 | Payback period | Th |  | Year | 2,7
c. Calculate the potential for EE for the measure

## Slide 52
The main energy efficiency opportunities are focused on three groups of solutions:
Optimizing the operation of existing equipment, such as improving kiln operation modes, adjusting fan speeds, enhancing cement grinding efficiency, and optimizing the exhaust gas–flue gas cycle.
Replacing or upgrading high-tech equipment, such as installing variable frequency drives (VFD) for fans and mills; using high-efficiency motors; replacing lighting systems with LED lamps; or upgrading air compressors and control systems.
Recovering and reusing waste heat, particularly in the rotary kiln system and clinker cooling machines, through Waste Heat Recovery (WHR) technology. In addition, implementing an energy management system according to ISO 50001 standards and periodic energy audits are also considered foundational for maintaining and improving sustainable energy use efficiency.
CONCLUSION

## Slide 53
Discussion Question 1: Of the Energy Efficiency Measures (EEMs) presented in this module, which one(s) do you think are most feasible and beneficial for your facility? Please explain why.
Discussion Question 2: What challenges and resources would be required to implement your chosen EEM(s) at your plant?
DISCUSSION

## Slide 54
THANK YOU