## Slide 1: TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs
MANAGEMENT OFFICERS
Module 4.3.
Current and potential of EE in Beverage industries in Vietnam

## Slide 2: Small group discuss and presentation
Devided the class into 4 group
Discuss in 15 mins
What sector do you think using the highest energy in Vietnam?
Identify the designated energy users in the Beverage industry?
What energy source your company mainly use?
What potential of EE in your company
Presentation in 5 mins

## Slide 3: Global industrial energy usage
Total Final Energy Consumption (TFC) by Sector from 1990 to 2020-2022
Notes: OECD Europe includes: Austria, Belgium, Czech Republic, Denmark, Finland, France, Germany, Greece, Hungary, Iceland, Ireland, Italy, Luxembourg, the Netherlands, Norway, Poland, Portugal, Slovakia, Spain, Sweden, Switzerland, Turkey, and the United Kingdom.
Changing focus from the U.S. stage of energy management to the work stage now.
Borrowed this slide from DOE. The stand out part of this is that industry consumes 50% of world energy. When you look at many developing countries, industrial energy use can be as large as 70- 80% of their total use.
This does not go unrecognized. Many countries have developed energy management system standards or other types of national programs to help their industry. These countries include Denmark, Ireland, China, Korea, Japan, Spain, Thailand, Germany, Sweden, United Kingdom. So there is a ground swell of energy management standards that have been developed our are in the process of being developed.

## Slide 4: Final electricity consumption by sector in Vietnam

## Slide 5: Current status of energy use in Vietnam
Agriculture, forestry and fisheries
Construction
Industry
Non- energy
Household
Services
Transportation

## Slide 6: Characteristics of energy consumption in Vietnam’s industry
The industry is the leading energy consumer sector in Vietnam, based on electricity consumption and final energy consumption
Vietnam currently has 3,068 DEUs (up from 2,496 in 2017), consuming 51,393,648 TOE, with DEUs in the industrial sector making up the majority—2,599 facilities consuming 50,570,115 TOE. The Vietnamese industry has significant potential for energy efficiency. Estimated proportion of the beverage industry among key energy-using facilities: Based on compiled reports from the Ministry of Industry and Trade and data from previous years:
The number of beverage manufacturing facilities appearing on the list of key energy-using establishments each year ranges from approximately 50 to 70 facilities nationwide.
By 2025, Vietnam requires 100% of designated energy-using enterprises to implement energy management systems as mandated by Decision 280/QD-TTG from the Prime Minister approving the National Program for Energy Efficiency for the 2019-2030 period.
The application of Energy Management Systems in Vietnam is still limited and weak. Many enterprises only implement these systems to meet legal requirements.

## Slide 7: Number of Designated Energy Users (DEUs)
Number of DEU and corresponding energy consumption, 2017-2021 (Source: Compiled from the DEU List)

## Slide 8: EE targets for Vietnam's industrial sectors by 2030
Industries | By 2025 |  | By 2030 | 
 | From | To | From | To
Steel industry(%) | 3 | 10 | 5 | 16.5
Chemical industry(%) | 7 |  | 10 | 
Plastic manufacturing industry(%) | 18 | 22.46 | 21.55 | 24.81
Cement(%) | 7.5 |  | 10.89 | 
Textile and Garment(%) | 5 |  | 6.8 | 
Beverages (%) | 3 | 6.88 | 4.6 | 8.44
Paper (%) | 8 | 15.8 | 9.9 | 18.48

## Slide 9
Primary energy
In 2020, Vietnam's TPES was estimated at 95,762 KTOE, increased by only 1.5% compared with the previous year.
1
Primary energy use
The export output in 2019 was only 8,834 KTOE, a 2.4-fold decrease compared to 2010.
In 2019, energy imports reached 44,342 KTOE, a 39.6% increase compared to 2018.
2
Vietnam Energy Statistics 2020
CURRENT STATUS OF ENERGY USE IN VIETNAM

## Slide 10
Energy Intensity by Country
Considering population size, Vietnam's TPES per capita in 2018 was relatively low at only 848 kgOE/person, even lower than the ASEAN average of 1,041 kgOE/person. However, the TPES intensity per GDP was quite high. This indicates that Vietnam's energy efficiency needs improvement.
3
Amount of energy needed to produce one unit of economic output. A lower number means that economies produce economic value in a less energy-intensive way.
4
Energy intensity, 2000 to 2020
Vietnam Energy Statistics 2020
CURRENT STATUS OF ENERGY USE IN VIETNAM

## Slide 12: Key energy-consuming facility
Number of key energy-consuming facilities and corresponding energy consumption during the period 2017-2021 (Source: Compiled from the list of key energy-consuming facilities)

## Slide 13: EE targets for Vietnam's industrial sectors by 2030
Industries | By 2025 |  | By 2030 | 
 | From | To | From | To
Steel industry(%) | 3 | 10 | 5 | 16.5
Chemical industry(%) | 7 |  | 10 | 
Plastic manufacturing industry(%) | 18 | 22.46 | 21.55 | 24.81
Cement(%) | 7.5 |  | 10.89 | 
Textile and Garment(%) | 5 |  | 6.8 | 
Beverages (%) | 3 | 6.88 | 4.6 | 8.44
Paper and pulp (%) | 8 | 15.8 | 9.9 | 18.48

## Slide 14: AVERAGE ELECTRICITY PRICE (2010 – 2024)
Chart: Graph of electricity price form 2009 to 2024
| Năm 2009 | Năm 2010 | Năm 2011 | Năm 2012 | Năm 2013 | Năm 2014 | Năm 2015 | Năm 2016 | Năm 2017 | Năm 2018 | Năm 2019 | Năm 2020 | Năm 2021 | Năm 2022 | Năm 2023 | Năm 2024
 | 948 | 1058 | 1242 | 1369 | 1508 | 1622 | 1622 | 1622 | 1622 | 1720 | 1864 | 1864 | 1864 | 1864 | 1920 | 2103
Electricity price comparison table of Vietnam with some countries in the world (Source: EVN 2022)
Electricity price of countries in the world
Converted to Vietnamese dong

## Slide 15: Specific Energy consumption and Energy Savings Potential
C3 Energy efficiency scenario of the Vietnam Energy Outlook 2019 report
Sector | Product | Savings potential (%)
Drinks | Beer | 9 - 12
 | Non-alcoholic beverages | 4 - 9
Plastic | Consumer plastic | 9 - 13
 | Construction plastic | 5 - 14
 | Packaging | 4 - 12
 | Plastic bottle | 5 - 14.5
 | Plastic bag | 11 - 17
Paper | Pulp | 6.8
 | Packaging | 3.8
 | Printing paper | 4.4
 | Toilet paper | 3.8
Chemistry | Rubber SVR 10CV, 20CV | 9.4 - 32.7
 | Rubber SSVR 10, 20 | 9.8 - 32.7
 | Fertilizer | 1.4 - 5.4
 | Water-based paint | 20 - 30
Heavy industrial products | Finished steel | 13
 | Cement | 14
 | Textile yarn | 14

## Slide 16: Current status of energy use in industry
Proportion of energy consumption: The industrial sector accounts for about 47% of the total energy consumption in the country.
Industries with high energy consumption:
  The steel production, cement, textile, wood processing, chemical industries, beverages
  These industries consume approximately 70% of the total energy in the industrial sector.
Energy efficiency: Energy consumption efficiency in the beverage industry remains low, with significant waste due to outdated technology and ineffective management

## Slide 17: Energy consumption structure in the industry
Proportion of energy consumption by sector:
  Manufacturing sector: 60%
  Construction sector: 15%
  Mining sector: 10%
  Transportation and logistics sector 5%
Main types of energy used:
  Electricity: Account for the largest proportion in the energy consumption structure of the industrial sector.
  Oil and natural gas: Used in manufacturing and chemical industries.
  Coal: Mainly used in the cement and metallurgy industries.

## Slide 18: Causes of high energy consumption
Outdated technology: Many enterprises in the beverage industry still use outdated technologies, which consume high levels of energy and cause environmental pollution..
Lack of investment in innovation: Insufficient capital and motivation to invest in energy-efficient equipment and technology.
Low awareness of energy efficiency: Some enterprises have not prioritized energy efficiency measures in their production processes.

## Slide 19: Challenges in energy management and utilization
Technological challenges: Many enterprises use outdated technology, resulting in low energy performance and environmental pollution:
Cost challenges: The initial investment costs for energy-efficient technologies are high, causing many enterprises to hesitate to make changes.
Lack of strong supporting policies: Although there are policies encouraging energy efficiency, they are still not effective enough to drive widespread adoption of energy efficiency measures among enterprises.
Inefficient boiler and steam systems
Manual or semi-automatic filling and packaging systems
etc.

## Slide 20: Trends in sustainable development in industry
Green industry: Enterprises are gradually paying more attention to using renewable energy and developing sustainable production.
International trend: Multinational corporations have higher standards for energy and environmental requirements when collaborating, especially in industries such as textiles and electronics.
Digital transformation and energy optimization: Applying digital technology to monitor and optimize energy usage in production.
New trends all place a certain emphasis on reducing greenhouse gas emissions in production and have become collaboration criteria for many major international corporations. This issue is becoming increasingly important and challenging for the industrial development of Vietnam.

## Slide 21
Beverage Industry

## Slide 22: Energy Intensity in Key Industries in Vietnam
Source: Overview of Energy Use and Energy Savings in Vietnam's Industrial Sector (2017–2022)

## Slide 23: Benchmarking in the beer industry
According to Article 5 of Circular 28/2024/TT-BCT, Benchmarking for the beer industry are:
Scale (million liter/year) | Benchmark (MJ/1000 liter) | Other Relevant Requirements
> 200 | ≤ 822 | Manage and monitor the production process to determine the amount of energy consumed. Facilities with SEC higher than benchmarking must report and justify the reasons to the competent authorities and submit an implementation plan to meet the benchmarking requirements based on the energy audit report. Report to the local DOIT by January 31 each year on the implementation status of the benchmarking of the facility (as specified in Article 5 of the Circular)
>100 to ≤ 200 | ≤ 1299 | 
> 50 to ≤ 100 | ≤ 1486 | 
> 25 to ≤ 50 | ≤ 1711 | 
>5 to ≤ 25 | ≤ 2543 | 

## Slide 24: Benchmarking in the non-alcoholic beverage industry
According to Article 5 of Circular 28/2024/TT-BCT, Benchmarking for the non-alcoholic beverage industry are as follows:
Type of production | Scale (million liter/year) | Benchmark (MJ/1000 liter) | Other Relevant Requirements
Carbonated or both carbonated and non-carbonated products | > 20 | ≤ 550 | Manage and monitor the production process to determine the amount of energy consumed. Facilities with SEC higher than benchmarking must report and justify the reasons to the competent authorities and submit an implementation plan to meet the benchmarking requirements based on the energy audit report. Report to the local DOIT by January 31 each year on the implementation status of the benchmarking of the facility (as specified in Article 5 of the Circular)
Non-carbonated products | >10 | ≤ 1068 | 

## Slide 25: EEMs in the Beverage Industry
Using Variable Frequency Drives (VFDs) in Motor Systems
Install VFDs to adjust motor speed based on actual demand.
Apply VFDs to equipment such as pumps, fans, and air compressors.
Efficiency Gains:
Reduces electricity consumption by 20-30%.
Extends equipment lifespan and reduces maintenance costs.

## Slide 26
Optimizing Cooling and Air Conditioning Systems
Perform regular maintenance to ensure optimal performance.
Adjust temperature and humidity to meet production and storage requirements.
Replace outdated equipment with high-efficiency cooling systems.
Efficiency Gains:
Lowers electricity costs by 15-20%.
Maintains product quality and reduces carbon emissions.
EEMs in the Beverage Industry

## Slide 27: EEMs in the Beverage Industry
Recovering Waste Heat in Production Processes
Install heat exchangers to recover heat from exhaust gases or wastewater.
Use recovered waste heat for water heating or preheating applications.
Efficiency Gains:
Saves energy by 10-25%.
Reduces fuel costs and improves overall efficiency.

## Slide 28: EEMs in the Beverage Industry
Implementation of Aseptic Filling Technology
Use aseptic filling technology to reduce the need for heat and chemicals.
Eliminates the need for sterilization after packaging.
Efficiency Gains:
Reduces energy consumption by up to 30%.
Enhances product quality and extends shelf life.

## Slide 29: EEMs in the Beverage Industry
Utilization of Solar Energy
Install solar energy systems on the factory rooftop.
Use solar energy for applications such as lighting and water heating.
Efficiency Gains:
Reduces electricity costs by 20-30%.
Cuts greenhouse gas emissions and improves the company’s green image.

## Slide 30: EEMs in the Beverage Industry
Adopting Energy Management Systems under ISO 50001
Develop an energy management system to monitor and optimize energy usage across the entire facility.
Set specific energy-saving goals, measure effectiveness, and continuously improve.
Integrate energy-saving metrics into departmental KPIs.
Train employees on energy awareness and savings techniques.
Efficiency Gains:
Lowers energy consumption by 5-20%.
Improves production efficiency and ensures compliance with environmental regulations.

## Slide 31: EEMs in the Beverage Industry
Optimization of Steam and Hot Water Systems
• Improve insulation for pipelines and storage tanks.
• Conduct regular inspections and maintenance to minimize heat loss.
Efficiency Gains:
• Saves energy by 10-15%.
• Reduces operational costs and increases safety.
Boiler System Optimization
• Adjust air-to-fuel ratios for optimal combustion efficiency.
• Install economizers and use cleaner fuels.
Efficiency Gains:
• Improves boiler efficiency by 3-10%.
• Reduces fuel costs by up to 30% and lowers greenhouse gas emissions.

## Slide 32: EEMs in the Beverage Industry
Air Compressor System Solutions
• Install variable frequency drives (VFDs) to adjust compressor speed.
• Regularly inspect and repair compressed air leaks.
• Recover heat from compressors for other processes.
• Install Intelligent Flow Control (IFC) devices to regulate compressed air flow.
Efficiency Gains:
• Reduces electricity consumption by 15-35%.
• Recovers 50-90% of waste heat, reducing the need for additional energy.

## Slide 33: Example of EEMs in the Beverage Industry in the world
Company: Enviro-Cool (UK) Ltd.
Location: United Kingdom
Industry: Beverage Cooling Technology
Background: The beverage industry is a significant consumer of energy, particularly in refrigeration and cooling processes. Traditional beverage coolers often maintain products at low temperatures continuously, leading to substantial energy consumption. Enviro-Cool (UK) Ltd. aimed to revolutionize this aspect by developing an innovative beverage cooling system that drastically reduces energy usage while ensuring rapid cooling on demand.

## Slide 34: Example of EEMs in the Beverage Industry in the world
Development of the V-Tex Multi System:
Rapid Cooling Technology: The V-Tex Multi system utilizes a patented technology that rapidly chills beverages from ambient to optimal drinking temperatures in approximately 15 seconds. This on-demand cooling approach eliminates the need for keeping large inventories of beverages continuously chilled.
Integration of Phase Change Materials (PCM): The system incorporates a buffer store with PCM, allowing it to maintain low temperatures efficiently. This design ensures that the cooling system operates only when necessary, significantly reducing energy consumption.
Energy Savings: The V-Tex Multi system demonstrated energy savings of over 90% compared to traditional open-front beverage chillers and 74% compared to standard glass door chillers. This substantial reduction translates to significant cost savings for retailers and a lower environmental footprint.
We believe this technology is highly effective in saving energy and has a feasible investment cost in the context of Vietnam.

## Slide 35: Quiz
1. Which technologies and equipment in the beverage production process cause significant energy waste?
2. What is the extent of implementation of energy-saving solutions and energy management practices in beverage manufacturing plants today?
3. What are the main barriers and challenges in improving energy efficiency in the beverage industry?

## Slide 37
Dự án Thúc đẩy tiết kiệm năng lượng trong các ngành công nghiệp Việt Nam
THANK YOU