## Slide 1
Module 7:
Introduction production line of the pulp and paper.
Very good module with tremendous amount of relevant information. Cannot provide too many comments because I am not a technical expert on pulp and paper production. A few minor comments provided.

## Slide 2: Pulp and Paper processing overview
Paper industry is one of the key processing industries and contributes to the national economy with around $1.6 billion or 1.5% of GDP in 2019
The industry has grown with around 29% per year in the period 2015-2018 outstripping domestic demand growth (10%/year)
There are 300 enterprises in which
  220 are small and medium enterprises producing around 10% of all paper products
  80 large companies produce around 90% of all paper
  Major producers in Vietnam’s paper industry are Chanh Duong, VinaKraft, Lee & Man, SGP, and Dong Hai Ben Tre which, in 2018, have cumulative capacity of 76%
  2 companies producing Pulp from chemical wood pulp process including VINAPACO and An Hoa Paper Jsc.
Notes: OECD Europe includes: Austria, Belgium, Czech Republic, Denmark, Finland, France, Germany, Greece, Hungary, Iceland, Ireland, Italy, Luxembourg, the Netherlands, Norway, Poland, Portugal, Slovakia, Spain, Sweden, Switzerland, Turkey, and the United Kingdom.
Changing focus from the U.S. stage of energy management to the work stage now.
Borrowed this slide from DOE. The stand out part of this is that industry consumes 50% of world energy. When you look at many developing countries, industrial energy use can be as large as 70- 80% of their total use.
This does not go unrecognized. Many countries have developed energy management system standards or other types of national programs to help their industry. These countries include Denmark, Ireland, China, Korea, Japan, Spain, Thailand, Germany, Sweden, United Kingdom. So there is a ground swell of energy management standards that have been developed our are in the process of being developed.

## Slide 3: Pulp and Paper processing overview
Bleached Hardwood Kraft Pulp (BHKP) production line with chemical recovery

## Slide 4
3 typical pulp producing process.
Chemical wood pulp is produced by combining wood chips and chemicals in large vessels called digesters. There, heat and chemicals break down lignin, which binds cellulose fibers together, without seriously degrading the cellulose fibers..
Mechanical wood pulp: also called grinding wood pulp, is a pulp made by mechanical grinding of fiber raw materials. Steam and Chemical is introduced directly to wood for easier of grinding and bleaching.
Recycled pulp: is also called deinked pulp (DIP). DIP is recycled paper which has been processed by chemicals, thus removing printing inks and other unwanted elements and freed the paper fibers.
Pulp and Paper processing overview

## Slide 5
Process flow diagram of paper production
Pulp and Paper processing overview

## Slide 6
Pulp and Paper processing overview

## Slide 7
Pulp and Paper processing overview

## Slide 8: Group discuss and presentation
Divide the group into two to three subgroups. Each subgroup will select one process line to discuss in a fifteen-minute session. The discussion can be conducted through a variety of methods, such as drawing, presentation, or any other appropriate format. Each subgroup will present their selected process line to the entire group.

## Slide 9: Production process of Bleached Hardwood Kraft Pulp (BHKP)

## Slide 10: Chemi-thermomechanical pulp production technology (CTMP, PRC-APMP)

## Slide 11: Chemi-thermomechanical pulp production technology (CTMP, PRC-APMP)

## Slide 12: Chemi-thermomechanical pulp production technology (CTMP, PRC-APMP)
Diagram of BCTMP production technology

## Slide 13
The pulp production technology by the deinked method DIP

## Slide 14
Newsprint production technology from waste paper

## Slide 15
Printing and writing paper production technology

## Slide 16
Packaging paper production technology

## Slide 17: Tissue paper production technology

## Slide 18: Features of paper production technology
Depending on the type of product, the stages of paper production can have many differences. The above production line diagrams are general diagrams. Each factory may have its own stages, even if the product may be the same. Very few factories have the stage of producing pulp from the raw material of wood. The raw material area for wood paper production in Vietnam is difficult and unstable. The majority of pulp factories produce pulp from waste paper and imported pulp

## Slide 19: Energy used in the paper industry
Vietnam's paper industry consumes quite a lot of electricity, largely due to the specifics of the profession and partly due to outdated and insynchronized machinery and equipment. The cost structure in the pulp and paper production process shows that, among the three input factors that directly affect the cost of raw materials, auxiliary materials, fuel and energy, the price increase of fuels for production is the highest The energy used for the Paper industry is mainly electricity, coal, DO oil and FO oil Electricity is used throughout the pulp and paper mill, the most significant electricity consumption is in the crusher system and motors in the production line Fuel consumption is mainly to produce steam for the cooking and drying process

## Slide 20: Distribution of power consumption at a tissue paper workshop
Chart: Distribution of electricity in Tissue Workshop
| Pumper (1) | HD Cleaner (1) | Disc filter (1) - Coarse | Mixing pulp (1) | Screen (1) | Head Box (1) | Vacuum Pump (1) | Yankee Dry (1) | Reel Drum (1) | Rewinder (1)
 | 0.073186 | 0 | 0.31736 | 0.031449 | 0.011863 | 0 | 0.28396 | 0.26313 | 0.012211 | 0.0035064

## Slide 21: Distribution of power consumption in 1 printing and writing paper workshop

## Slide 22: Energy Mapping of a Tissue Paper Production Line

## Slide 23: Energy used in paper production line
For establishments producing paper from imported pulp and grade paper
  Electricity consumption is mainly in the stages of crushing and vacuum pressing. Other motors in the production line have less energy consumption. The amount of water used in the line is quite large, so the energy consumption for pumping at the stages is also a significant amount. The heat energy consumed is mainly steam for the paper drying process in twisting lines. Depending on the type of technology, different pressure levels can be used to dry paper in cross lines. Good separation of water before drying plays an important role in saving energy

## Slide 24: Energy used in paper production line
For factories with pulp processing.
The energy from steam for pulp cooking is very significant. In general, factories with pulp processing are large factories and a co-generation system of heat and electricity is suitable for these factories. The heat-electricity cogeneration system will be more efficient if it is invested synchronously with large boilers to produce superheated steam with higher pressure and steam temperature. Consumption of electricity or fuel such as DO oil for machine tools for loading and unloading, transporting raw materials can account for a significant proportion of the line. Careful consideration and evaluation of thermal power cogeneration systems can bring high efficiency in energy saving.

## Slide 25: Energy consumption for some types of products
Benchmark to produce a ton of Bleached Hardwood Kraft Pulp:
Benchmark to produce a ton of Semi-chemical pulp
No. | Material and fuel | Unit | Benchmark
Material |  |  | 
1 | Acacia, sandalwood (dry of 50%) | kg | 4.180,00
Fuels |  |  | 
1 | Electricity | MWh | 0,32
2 | Water | m3 | 45,0
3 | Steam for evaporation | ton | 2,10
4 | Steam for digester | ton | 1,78
No. | Materials | Unit | Benchmark per ton of prod.
Main materials |  |  | 
1 | Wood | Ton | 2,8
Chemicals |  |  | 
1 | NaOH | kg | 125
2 | H2O2 50% | kg | 95
3 | Na2SiO3 | kg | 55
4 | DTPA | kg | 1,2
Fuels, energy |  |  | 
1 | Steam | Ton | 0,4
2 | Electricity | Kwh | 1850
3 | Water | m3 | 45

## Slide 26: Energy consumption for some product types
Benchmark to produce a ton of newsprint production
Benchmark to produce a ton of printing paper and writing paper
No. | Materials | Unit | Benchmark
Main material |  |  | 
1 | Pulp | kg | 208
2 | Paper margin |  | 842
Chemicals |  |  | 
1 | CaCO3 | kg | 145
2 | Kaolin | kg | 18
3 | Anionic starch | kg | 10
Fuels, energy |  |  | 
1 | Water | m3 | 30
2 | Coal | kg | 0
3 | Electricity | kwh | 620
4 | Other fuels | kg | 610
No. | Materials | Unit | Benchmark
Main material |  |  | 
1 | Newspaper edge | kg | 1350
Chemicals |  |  | 
1 | CaCO3 | kg | 80
2 | AKD glue | kg | 2,5
3 | Cation starch | kg | 8
Fuels, energy |  |  | 
1 | Water | m3 | 60
2 | Coal | kg | 300
3 | Electricity | kwh | 1100

## Slide 27: Energy consumption for some product types
Benchmark to produce a ton of tissue paper production
Benchmark to produce a ton of packaging paper production
No. | Materials | Unit | Benchmark
Main material |  |  | 
1 | Pulp | kg | 208
2 | Paper edge |  | 842
Chemicals |  |  | 
1 | CaCO3 | kg | 145
2 | Kaolin | kg | 18
3 | Anion starch | kg | 10
Fuel, energy |  |  | 
1 | Water | m3 | 30
2 | Coal | kg | 0
3 | Electricity | kwh | 620
4 | Other fuel | kg | 610
No. | Materials | Unit | Benchmark
Main material |  |  | 
1 | Pulp | kg | 1.074
Chemicals |  |  | 
1 | Brightener | kg | 2,5
2 | Softener | kg | 7
3 | Wet strength | kg | 8
Fuel, energy |  |  | 
1 | Water | m3 | 21
2 | Coal | kg | 520
3 | Electricity | kwh | 700

## Slide 28
THANK YOU