## Slide 1
MANAGEMENT OFFICERS
TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs
Module 4.5.
Current and potential of EE in brick and ceramic industries in Vietnam

## Slide 2: Small group discuss and presentation
Devided the class into 4 group
Discuss in 15 mins
What sector do you think using the highest energy in Vietnam?
Identify the designated energy users in the Beverage industry?
What energy source your company mainly use?
What potential of EE in your company
Presentation in 5 mins

## Slide 3: Global industrial energy usage
Total Final Energy Consumption (TFC) by Sector from 1990 to 2020-2022
Notes: OECD Europe includes: Austria, Belgium, Czech Republic, Denmark, Finland, France, Germany, Greece, Hungary, Iceland, Ireland, Italy, Luxembourg, the Netherlands, Norway, Poland, Portugal, Slovakia, Spain, Sweden, Switzerland, Turkey, and the United Kingdom.
Changing focus from the U.S. stage of energy management to the work stage now.
Borrowed this slide from DOE. The stand out part of this is that industry consumes 50% of world energy. When you look at many developing countries, industrial energy use can be as large as 70- 80% of their total use.
This does not go unrecognized. Many countries have developed energy management system standards or other types of national programs to help their industry. These countries include Denmark, Ireland, China, Korea, Japan, Spain, Thailand, Germany, Sweden, United Kingdom. So there is a ground swell of energy management standards that have been developed our are in the process of being developed.

## Slide 4: Final electricity consumption by sector in Vietnam

## Slide 5: Final energy consumption by industry in Vietnam
Transportation
31,7%
Services
3,9%
Household 14,9 %
Non- energy
2%
Industry
45,7%
Argriculture
1,8 %
2012
2021
Industry
Non- energy
5,5%
Argriculture
5,2%
Transportation
16,7%
Services
3,2%
Household
15,3 %

## Slide 6: Current status of energy use in Vietnam
Agriculture, forestry and fisheries
Construction
Industry
Non- energy
Household
Services
Transportation

## Slide 7: Characteristics of energy consumption in Vietnam’s industry
The industry is the leading energy consumer sector in Vietnam, based on electricity consumption and final energy consumption
Vietnam currently has 3,491 DEUs (up from 2,496 in 2017), consuming 51,393,648 TOE, with DEUs in the industrial sector making up the majority—2,864 facilities consuming 50,570,115 TOE. There are 143 DEUs in Brick and Ceramic Industry that consume 1,332,655 TOE. .
By 2025, Vietnam requires 100% of designated energy-using enterprises to implement energy management systems as mandated by Decision 280/QD-TTG from the Prime Minister approving the National Program for Energy Efficiency for the 2019-2030 period.
The application of Energy Management Systems in Vietnam is still limited and weak. Many enterprises only implement these systems to meet legal requirements.

## Slide 8: Number of Designated Energy Users (DEUs)
Number of DEU and corresponding energy consumption, 2017-2021 (Source: Compiled from the DEUs List)
Number of DEUs
Energy using of DEUs (kTOE)
143 DEUs in Brick and Ceramic

## Slide 9
Primary energy
In 2020, Vietnam's TPES was estimated at 95,762 KTOE, increased by only 1.5% compared with the previous year.
1
Primary energy use
The export output in 2019 was only 8,834 KTOE, a 2.4-fold decrease compared to 2010.
In 2019, energy imports reached 44,342 KTOE, a 39.6% increase compared to 2018.
2
Vietnam Energy Statistics 2020
CURRENT STATUS OF ENERGY USE IN VIETNAM

## Slide 10
Energy Intensity by Country
Considering population size, Vietnam's TPES per capita in 2018 was relatively low at only 848 kgOE/person, even lower than the ASEAN average of 1,041 kgOE/person. However, the TPES intensity per GDP was quite high. This indicates that Vietnam's energy efficiency needs improvement.
3
Amount of energy needed to produce one unit of economic output. A lower number means that economies produce economic value in a less energy-intensive way.
4
Energy intensity, 2000 to 2020
Vietnam Energy Statistics 2020
CURRENT STATUS OF ENERGY USE IN VIETNAM

## Slide 11: AVERAGE ELECTRICITY PRICE (2010 – 2024)
Chart: Graph of electricity price form 2009 to 2024
| Năm 2009 | Năm 2010 | Năm 2011 | Năm 2012 | Năm 2013 | Năm 2014 | Năm 2015 | Năm 2016 | Năm 2017 | Năm 2018 | Năm 2019 | Năm 2020 | Năm 2021 | Năm 2022 | Năm 2023 | Năm 2024
 | 948 | 1058 | 1242 | 1369 | 1508 | 1622 | 1622 | 1622 | 1622 | 1720 | 1864 | 1864 | 1864 | 1864 | 1920 | 2103
Electricity price comparison table of Vietnam with some countries in the world (Source: EVN 2022)
Electricity price of countries in the world
Converted to Vietnamese dong

## Slide 12: Current status of energy use in industry
Proportion of energy consumption: The industrial sector accounts for about 54% of the total energy consumption in the country.
Industries with high energy consumption:
  The steel production, cement, textile, wood processing, and chemical industries.
  While Bricks and Ceramics are not the largest energy consuming industry, however, brick and Ceramics processing is complicated with many energy consumption equipment especially are kilns and spray dryers that consume large amount of heat and high potential of energy saving.
Energy efficiency: Energy consumption efficiency remains low, with significant waste due to outdated technology and inefficient management.

## Slide 13: Energy consumption structure in the industry
Proportion of energy consumption by sector:
  Manufacturing sector: 60%
  Construction sector: 15%
  Mining sector: 10%
  Transportation and logistics sector 5%
Main types of energy used:
  Electricity: Account for the largest proportion in the energy consumption structure of the industrial sector.
  Oil and natural gas: Used in manufacturing and chemical industries.
  Coal: Mainly used in the cement and metallurgy industries.

## Slide 14: Causes of high energy consumption in brick and ceramic processing
Outdated technology: Many enterprises still use old technology, which consumes high amounts of energy and causes environmental pollution. In brick manufacturing, there are many Hoffmann kiln in the form of Chinese Technology that consume high energy to produce brick. The old tunnel kiln with narrow tunnel also give low quality of brick as well as high coal consumption
Lack of investment in innovation: Insufficient capital and motivation to invest in energy-efficient equipment and technology. There are a significant energy could be saved by optimal the firing process in the kiln. The waste heat recovery oppotunities still exist in many kiln.
Low awareness of energy efficiency: Brick and ceramic enterprises have not prioritized energy efficiency measures in their production processes. The energy price still acceptable for low efficiency technology. The awareness of energy saving oppotunities is not high.

## Slide 15: Challenges in energy management and utilization
Technological challenges: Brick and ceramic enterprises use outdated technology, resulting in low energy performance and environmental pollution.
Cost challenges: The initial investment costs for energy-efficient technologies are high, causing many enterprises to hesitate to make changes.
Lack of strong supporting policies: Although there are policies encouraging energy efficiency, they are still not effective enough to drive widespread adoption of energy efficiency measures among Brick and ceramic enterprises.

## Slide 16: Trends in sustainable development in industry
Green industry: Enterprises are gradually paying more attention to using renewable energy and developing sustainable production.
Reduce energy cost trend: In general, brick and ceramic enterprises have high energy cost that can be accounted for 20 – 40% of total production cost. With the trend of energy cost higher and higher in the future, energy saving is a trend of many brick and ceramic enterprise.
Digital transformation, robot utilization and energy optimization: Applying digital technology to monitor and optimize energy usage in production. Also, recently, using robot to arrange bricks into the kiln car for brick making can reduce labor cost as well as opitimizing the brick arrangement.
Using dry brick formation procedure to reduce the requirement for drying purpose.

## Slide 17
Brick & Ceramic Industry in Vietnam

## Slide 18: The current situation of fired brick production
Current State of Fired Brick Production
Number of production facilities: Approximately 4,000 clay brick manufacturing facilities with a total designed capacity of about 25 billion bricks per year.
Annual production: Estimated to reach 60-70% of the total designed capacity.
Geographical distribution: Mainly concentrated in the Red River Delta, Central Vietnam, and Southeastern regions.
Shift Towards Non-Fired Brick Production
Number of non-fired brick production facilities: Approximately 2,500 facilities with a total designed capacity of about 15 billion standard bricks per year.
Annual production: Estimated to reach 50-60% of the total designed capacity.
Benefits:
Reduces clay consumption.
Saves energy.
Lowers CO₂ emissions.
Contributes to environmental protection.

## Slide 19: State Policies and Regulations
Decision 2171/QĐ-TTg (2021):The program for the development of non-fired construction materials in Vietnam until 2030 aims to reduce the use of fired clay bricks and lower CO₂ emissions.
Circular 13/2017/TT-BXD:Regulation on the use of non-fired construction materials in building projects.
Decision 1266/QD-TTg (18/08/2020): Approving the Strategy for the development of Vietnam's building materials for the 2021-2030 period, with a vision to 2050, emphasizing the reduction of the use of fired bricks, strengthening non-fired bricks to protect the environment
Non-fired bricks must meet standards such as: TCVN 6476:1999, TCVN 6477:2016, TCVN 7744:2013, QCVN 16:2019/BXD.

## Slide 20: Comparison of fired bricks and non-fired bricks
Criteria | Fired bricks | Non-fired bricks
Material | Clay | Industrial waste, cement, sand
Production technology | Burning at high temperatures | Pressing, vibrating, not overheated
Environmental Impact | High (CO₂ emissions, air pollution) | Low (emission reduction, environmental protection)
Production costs | Lower | Higher
Product Quality | High strength, good bearing | Variety, sound insulation, good heat insulation

## Slide 21: Overview of the Ceramic Industry in Vietnam
Vietnam’s ceramic industry has a long history, playing a significant role in the country’s culture and economy.
The diversity of ceramic types reflects the richness of art and practical applications.
Vietnam has approximately 2,000 traditional craft villages, including renowned ceramic-producing villages like Bát Tràng, Chu Đậu, and Phù Lãng.
Vietnamese ceramic products are exported to major markets such as the United States, Japan, and the EU, with export turnover reaching $711 million in 2022.

## Slide 22: Types of Ceramics in Vietnam
Types of Ceramics in Vietnam
Household Ceramics: Bowls, plates, cups, teapots, and vases.
Decorative Ceramics: Statues, bas-reliefs, ceramic lamps, and screens.
Construction Ceramics: Roof tiles, floor tiles, and wall tiles.
Artisan Ceramics: Artistic creations and souvenirs.
Technical Ceramics: Insulating porcelain products, sanitary ware, and other technical ceramic items.
Development Solutions for the Ceramic Industry
Artisan Training: Preserve and promote traditional techniques.
Technological Innovation: Adopt advanced production technologies.
Market Expansion: Strengthen trade promotion and participate in international fairs.
Craft Village Tourism Development: Combine ceramic production with experiential tourism.

## Slide 23: Fired Brick Production Technology
Handmade Kilns: Completely phased out due to outdated technology and environmental pollution.
Improved Ring Kiln: Uses plastic clay, but its longevity is limited due to the depletion of raw materials.
Modern Tunnel Kiln: Uses riverbank soil and hillside clay; high productivity, good quality, highly automated, and energy-efficient. The modern tunnel kiln is characterized by the modernization of the shaping process, with robots handling the bricks when entering and exiting the kiln. The modern tunnel kiln is divided into three types:
1. Traditional Tunnel Kiln Technology: Built with an improved flat roof and wide kiln chamber.
2. Moving Tunnel Kiln: Designed to move along tracks, allowing bricks to be arranged in a circular fixed pattern and moved sequentially through the kiln.
3. Moving Roof Tunnel Kiln: The kiln is designed as a rectangular structure buried underground. The roof panels are movable to cover the fixed rows of bricks.

## Slide 24: Fired Brick Production Technology
Old-style Tunnel Kiln with an arched roof made of refractory bricks and a narrow kiln chamber.

## Slide 25: Fired Brick Production Technology
New type Tuynel brick kiln with flat ceiling made of ceramic cotton pressed wide furnace

## Slide 26: Fired Brick Production Technology
Movable Tuynel Oven

## Slide 27: Fired Brick Production Technology
Portable Flat Ceiling Tube Oven

## Slide 28: Energy used in fired brick production:
Coal: Accounts for over 80% of the energy source, used for firing bricks.
Wood and agricultural by-products: Used to start the kiln and supplement heat at some facilities with available resources.
Electricity: Used to operate production equipment.
Energy consumption by kiln types:
• Hand kilns: 1,200-1,500 kcal/kg of brick.
• Ring kilns and old tunnel kilns: 700-900 kcal/kg of brick.
• New tunnel kilns and moving tunnel kilns, flat roof moving tunnel kilns: 400-600 kcal/kg of brick.
The significant differences between technologies show the potential for energy savings.

## Slide 29: EEMs in fired brick production
Technology improvements:
Transition to advanced kiln technologies such as flat roof tunnel kilns, moving tunnel kilns, and moving flat roof tunnel kilns.
Use of advanced product shaping processes with semi-dry extrusion lines, reducing energy needs for water evaporation.
Optimization of the drying process to minimize the impact of weather factors and better utilize solar energy for drying.
Implement energy balancing for kilns to identify opportunities to reduce heat losses during firing and better utilize heat between drying, heating, firing, and cooling stages.

## Slide 30: EEMs in fired brick production
Use of Renewable Energy: Traditional kilns previously used a lot of biomass energy. In modern technologies, coal is the primary fuel. Efforts should be made to use biomass fuels (rice husks, sawdust, and other agricultural residues) in modern kilns to supplement heat in the firing process.
Automatic Control System: Monitor and adjust the temperature in the kiln. This reduces energy waste caused by operational errors.
Enhanced Insulation: Use high-quality insulation materials in the firing and drying systems to minimize energy loss.
Energy Management System (EMS): Track energy consumption in real-time. Identify and address points of inefficiency in energy use.

## Slide 31: EEMs in fired brick production
Replace Traditional Kilns with Gas or Gas-Electric Hybrid Kilns:
• Reduce energy consumption by 30-50%.
• Better temperature control reduces the occurrence of defective products.
• Decrease environmental pollution.
Heat Recovery from Firing Kilns:
• Use excess heat to dry products before firing.
• Reduces energy consumption during the drying process.
Biomass Gasification:Rice husks, sawdust, cashew shells, and agricultural waste are renewable, inexpensive, and environmentally friendly energy sources. However, the use of raw biomass can impact product quality. The gasification process helps convert solid fuels into higher-quality gaseous fuels.

## Slide 32: EEMs in fired brick production
Automatic Control System:
Monitor and adjust the temperature and air flow in the kiln.
Reduce energy waste caused by operational errors.
Modern Machinery: Automatic clay pressing and mixing machines help reduce electricity and fuel consumption.
Energy Management System (EMS):
Track real-time energy consumption.
Analyze and eliminate unnecessary energy consumption points.

## Slide 33: Discussion
You see that these brick production stages consume the most energy Discuss the potential for more specific Energy Savings from the stated solutions

## Slide 34: Non Fired brick production
Eventhough there are several types of non fired bricks. However, only 2 types could be existed and developed in Vietnam:
Concrete block or aggregated cement brick. It is a type of non-fired brick produced from a mixture of concrete (cement, sand, mite or small gravel, water, and additives) through a pressing or casting process, without the need for autoclave. In some enterprises, ash and slag, industrial waste could be used to reduce the materials cost as well as reduce solid waste to Environment.
AAC is a type of autoclaved lightweight concrete, produced from a mixture of cement, lime (or cement), fine sand (or fly ash), gypsum, water, and aerating agent (usually aluminum powder). The chemical reaction process produces hydrogen gas, which forms small air bubbles in the structure, making the material lightweight, insulating, soundproof, and flame retardant. After casting, the mixture is autoclaved at high temperature and pressure to increase strength and stability..

## Slide 35: Concrete brick production process

## Slide 36: Concrete brick production process

## Slide 37: AAC production process
Process of an AAC lightweight concrete production chamber

## Slide 38: AAC production process

## Slide 39: EEM in concrete bricks and aggregate cement bricks
The production of concrete bricks and aggregate cement bricks (XMCL) does not need to be fired at high temperatures (800-1200°C like fired clay bricks), which saves 80-90% of the energy consumption in the production process. Concrete bricks and aggregate cement bricks use coal fired thermal power plan ash, blast furnace slag, rock mites, or construction waste as aggregates, instead of mining clay or natural stone. This reduces the energy consumed for the extraction and transportation of raw materials Modern production lines (such as hydraulic presses or vibrators) are optimized to reduce power consumption by 20-30% compared to the old technology. The replacement and conversion of presses is an energy-saving potential in the production of concrete bricks or aggregate cement Adopt automatic control system, optimize machine operation time, reduce power by 10-15%. Using an inverter in the press helps to adjust the power, saving 5-10% more energy

## Slide 40: EEM in concrete bricks and aggregate cement bricks
The use of additives (e.g. plasticizers, fast adhesives) shortens mixing and maintenance times, thereby reducing the energy required to operate the mixer and press. The additive also enhances durability, allowing to reduce the amount of cement (an energy-consuming component to produce), saving 15-25% of energy in cement production. Some factories in Dong Nai and Binh Duong have installed solar power systems, providing 20-30% of electricity demand for aggregate cement brick production lines. According to the report of the Ministry of Construction, the conversion from fired clay bricks to non-fired bricks (including concrete bricks and aggregate cement bricks) will save 1-1.5 million TOE (tons of oil equivalent) of energy per year if the target of 40-45% market share is reached by 2030. Reduce emissions by 2-3 million tons of CO2/year, contributing to Vietnam's carbon neutrality goal (COP26). Each non-fired brick factory with a capacity of 10 million QTC/year can save 50-70% of energy compared to equivalent fired brick factories

## Slide 41: EEM in Autoclaved concrete bricks (AAC)
Autoclaved concrete bricks (AAC) have great potential for energy savings by eliminating high-temperature calcination, using industrial waste, and improving autoclave technology. Autoclave is the most energy-intensive stage in AAC production (due to the need for high-pressure steam), modern autoclaves are designed to recirculate steam and heat, reducing energy consumption by 15-25%. Optimizing the steam system in the plant can save 20% of energy in steam production. Some factories in the South (such as SAKO Vietnam) integrate solar energy to power the boilers, saving 20-30% of grid electricity. The process of mixing raw materials (cement, lime, sand/fly ash, aluminum powder) uses a high-capacity mixer but is optimized to reduce mixing time, saving 10-20% of electricity. Using inverters in mixers and cutters helps to adjust the power according to the load, saving 5-10% of electricity.

## Slide 42: EEM in Autoclaved concrete bricks (AAC)
The superplasticizer reduces the amount of water by 10-15%, shortens the mixing time and energy consumption of the mixer Using pozzolan cement (combined with fly ash) instead of traditional Portland cement helps reduce energy in cement production by 20-25% (because cement is the most energy-consuming component AAC bricks are light in weight (500-700 kg/m³, compared to 1800-2400 kg/m³ of fired bricks), reducing the energy transported to the building (20-30% of the energy transported) The large size (600x200x100 mm) and the ability to cut easily reduce the construction time (15-25%) and the amount of masonry mortar (2-3%), thereby reducing the energy for the mortar mixer and labor on site The large size (600x200x100 mm) and the ability to cut easily reduce the construction time (15-25%) and the amount of masonry mortar (2-3%), thereby reducing the energy for the mortar mixer and labor on site AAC bricks have good thermal insulation (thermal conductivity 0.1-0.2 W/m.K), reduce the need for air conditioning in the building, save energy in the long term

## Slide 43: Short discussion of Non fired brick and EEMs
How do you know about the energy saving oppotunities have been described.
Do you have any experience related to the energy saving in production process of your system.

## Slide 44: Ceramic production
There are 3 types of Ceramic production including:
Folk ceramics and fine arts with bowls, plates, teapots, vases, vases, tea cups, tableware, pots, ceramic pans, ceramic statues, reliefs, ceramic paintings, decorative ceramic vases, worship items (incense burners, candlesticks). Usually produced manually or semi-industrially, using stretch enamel, colored enamel, or clear enamel. The kilns used are usually manual kilns that use coal and biomass as fuel and later many facilities have converted to intermittent gas furnaces for the firing process. Construction ceramics with products Ceramic tiles, ceramic tiles, decorative tiles, terrazzo tiles, ceramic ceramic tiles, porcelain tiles (bone porcelain). Produced industrially on a large scale, meeting technical standards such as TCVN 13113:2020 (ISO 13006:2018) and QCVN 16:2023/BX. Roller rod kilns are commonly used for the firing process. Industrial ceramics with products Insulated porcelain, engineering porcelain, heat-resistant materials, sanitary porcelain (toilets, sinks). Manufactured industrially with advanced technology, meeting international standards (such as ISO 9001:2015). Usually use Tuynel kilns for the firing process

## Slide 45: Ceramic production process
Preparation of ingredients
Product Shaping
Drying
Preliminary firing
Glazing
Fired Finish
Fired Finish
Distribute

## Slide 46: EEM in Ceramic processing
Fuel conversion. Manual ceramic kilns using coal and firewood converted into ceramic kilns help save energy, easily control the firing temperature, minimize waste products and do not pollute the environment. Currently most of the handmade pottery kilns have been eliminated. Take advantage of excess heat in intermittent furnaces that use gas. The firing of ceramics goes through 3 stages including drying, heating, firing, and cooling with the exhaust smoke temperature of the firing stage up to thousands of oC. Finding ways to take advantage of this waste heat from the smoke or excess heat from the cooling process increases energy savings. Using thermal power ash, blast furnace slag, or ceramic scrap as a substitute for clay, kaolin, or feldspar reduces the energy of mining and crushing raw materials (20-30% of energy) The drying stage (50-150°C) consumes 10-15% of the total energy. Using a continuous drying oven with a hot air recirculation system and automatic temperature control can reduce drying energy by 15-25%.

## Slide 47: EEM in Ceramic processing
The forming stage (pressure pressing, liquid casting, isostatic injection molding) uses a press or molding machine, which accounts for 10-20% of the energy. Modern presses with inverters and automation help reduce power by 10-15% compared to old machines. Viglacera's pressure press (100-200 tons) for tiles uses inverter, saving 5-10% of electricity compared to traditional mechanical presses. Technological improvement: PLC (Programmable Logic Controller) control system helps optimize the pressing cycle, reduce machine operation time. Additives (e.g. plasticizers, cooling temperature reducers) help reduce the amount of kaolin/cement or lower the firing temperature (50-100°C), saving 10-20% of thermal energy Modern industrial enamel (lead-free enamel, nano-enamel) reduces the firing time and firing temperature, saving 5-10% energy The thermal recirculation system in the furnace and dryer helps to reuse the hot gas, reducing thermal energy by 15-25%. Use solar energy to power a press, mixer, or boiler, reducing dependence on the grid (20-30% of electricity costs)

## Slide 48: Short discussion of Ceramic making
How do you know about the energy saving oppotunities have been described.
Do you have any experience related to the energy saving in production process of your system.

## Slide 49: Conclusion
  The production of fired clay bricks, unfired bricks, and ceramics all has great potential for energy savings, with unfired bricks (especially concrete and aggregate cement) leading the way thanks to the elimination of the firing process. Solutions such as modern kilns, heat recirculation, the use of industrial waste, additives to reduce furnace temperatures, and renewable energy are key to energy optimization. With the support from policies (Decision 2171/QD-TTg, Circular 13/2017/TT-BXD), Vietnam's brick and ceramic industry can achieve the goal of saving 1-1.5 million TOE/year and reducing 2-3 million tons of CO2/year, contributing to sustainable development and green construction

## Slide 50
Dự án Thúc đẩy tiết kiệm năng lượng trong các ngành công nghiệp Việt Nam
THANK YOU