## Slide 1
Module 9.5:
Case studies on energy efficiency measures in the brick and ceramic industry..
MANAGEMENT OFFICERS
TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs

## Slide 2: CASE STUDY – DONG TAM TUNNEL BRICK FACTORY
Dong Tam Co., Ltd., located at Km9, Road 391, Ky Son, Tu Ky, Hai Duong, established in 2003, producing construction bricks using a tunnel-style brick drying system with a total area of ​​about 40,000 m2, including a 6,000 m2 covered drying yard; 1,000 m2 outdoors; a 10,000 m2 soil gathering area; a 1,000 m2 covered raw soil storage house; a 500 m2 raw brick extrusion area; a 1,200 m2 tunnel drying kiln system; a 10,000 m2 finished product yard and an internal traffic system and office.
The tunnel drying kiln system of Dong Tam brick production facility was built in 2003.

## Slide 3: CHARACTERISTICS OF THE COMPANY'S TUNNEL KILN
The kiln chamber is narrow and tall, constructed with fire-resistant bricks and insulated with coal slag and thick wall layers.
The height of the brick stacks from the top of the kiln car to the arch’s peak is considerable, causing aerodynamic stratification within the kiln that is difficult to control. This results in underfired bricks at the bottom and overfired bricks at the top.
The fixed-height vaulted roof extending from one end of the kiln to the other creates a continuous large gap throughout the kiln. This allows strong airflow, which lowers the temperature at the top of the kiln cars and causes underfiring of the bricks in that area.
The firing kiln is connected to the Tuynel drying chamber. A portion of the hot air extracted from the cooling zone of the kiln, along with all high-temperature exhaust gases, is redirected to the drying chamber to assist with the drying process.
The Tuynel kiln is equipped with a rapid cooling system using fans positioned accordingly. However, during operation, this quick-cooling mechanism is not in use and needs to be restored for proper utilization.
The kiln cars are of an older, heavier design due to the thick fire-resistant materials and bulky construction. As a result, heat loss due to thermal accumulation in the kiln cars is relatively high.

## Slide 4: KILN AND DRYER STRUCTURE

## Slide 5: PRODUCTION STATUS OF THE KILN BEFORE EEMS
The rate of first-grade finished bricks is low, with approximately 17% of defective bricks caused by underfiring. These typically appear at the top of the kiln car and bottom corners.
Production activities are highly dependent on seasonal weather conditions, facing significant difficulties during the rainy season due to the lack of adequately dried green bricks for firing.
The operational efficiency of the drying chamber is low, requiring an additional auxiliary dryer during the rainy season, which consumes a large amount of energy.
Although the kiln is equipped with a piping and fan system for rapid cooling, it is currently not in use. This contributes to heat loss, as residual heat stored in the bricks and kiln cars remains high upon exiting the kiln.

## Slide 6: ENERGY BALANCE FOR KILN BEFORE EEMS
Chart: Heat energy flow in the kiln (kW)
| Do khói thải | Không khí nóng đến hầm sấy | Không khí nóng đi đến hầm sấy phụ | Nhiệt để bốc hơi nước trong lò | Tổn thất do tỏa nhiệt ra môi trường | Tổn thất do tồn trữ trong gạch ra lò | Tổn thất do tồn trữ trong xe goòng | Tổn thất do sự hình thành CO
 | 432 | 664 | 116 | 102 | 46 | 7 | 27 | 57
Exhaust fumes
Hot air to the drying tunnel
Hot air to the secondary drying chamber
Heat for water evaporation in the kiln
Heat loss to the environment
Losses due to storage in kiln-fired bricks.
Losses due to storage in wagon cars
Losses due to CO₂ formation

## Slide 7: ENERGY DISTRIBUTION IN TUNNEL KILN AND DRYER BEFORE IMPLEMENTATION
Chart: 
| Lượng Nhiệt từ khói thải đi sang hầm sấy | Lượng Nhiệt từ không khí nóng trích sang hầm sấy chính | Lượng Nhiệt từ không khí nóng trích sang hầm sấy phụ | Lượng Nhiệt cần để bốc hơi nước cho gạch trong lò nung | Tổn thất do tỏa nhiệt ra môi trường | Tổn thất nhiệt do tích lũy trong gạch và xe goòng | Tổn thất nhiệt do quá trình cháy hình thành CO
 | 386 | 593 | 104 | 91 | 62 | 32 | 51
Chart: 
| Nhiệt lượng để nâng nhiệt độ gạch mộc | Nhiệt lượng để nâng nhiệt độ xe goòng | Nhiệt lượng khói thải mang ra ngoài | Tổn thất nhiệt do tỏa nhiệt ra môi trường | Lượng nhiệt sử dụng cho bốc hơi nước
 | 67.8089 | 76.5375 | 410.83 | 20 | 403.8236
Thermal energy is used in the tunnel dryer
Thermal energy is used in the tunnel kiln
The amount of heat transferred from the exhaust gas to the tunnel dryer
The amount of heat transferred from the exhaust gas to the tunnel dryer
The amount of heat from the extracted hot air is directed to the auxiliary tunnel dryer
Heat required to raise the temperature of green bricks
Heat required to raise the temperature of the kiln car
Heat is carried away by exhaust gases
Heat loss due to heat dissipation into the environment
Amount of heat used for water evaporation

## Slide 8: CONDITION REVIEW BEFORE IMPLEMENTATION
  The drying tunnel is 26m shorter than the kiln, the drying process is short and does not meet the time required for evaporation of water to dryness. When the weather is humid, the enterprise must operate an auxiliary drying kiln with increased energy consumption of up to 410.83 kJ/kg of brick.
  The drying tunnel exhaust fan operates at high capacity, so it draws an additional 35,438 kg/hour of outside air into the drying tunnel and mixes with 41,104 kg/hour of hot air from the kiln. This additional air volume reduces the temperature of the mixture used for drying and thus reduces the drying efficiency of the drying tunnel, increasing the loss due to exhaust fumes.
  The heat loss due to exhaust fumes of the drying tunnel, calculated from the measurement results is 410.83 kJ/kg of brick, equivalent to 42% of the heat input into the drying tunnel. The amount of heat used to evaporate water in the brick is 403.8kJ/kg of brick at the time of measurement. If the heat loss due to exhaust fumes from the drying tunnel can be reduced, the amount of heat available will increase to speed up the drying speed, increasing the temperature of the bricks leaving the drying tunnel, leading to the ability to reduce the firing time and thus increase the capacity of the kiln.

## Slide 9: EXPECTED EEMs
Renovate and extend the drying tunnel by 26m, rearrange the air and smoke channels of the drying tunnel; replace the total smoke exhaust fan of the drying tunnel and change the chimney of the kiln.
Install additional inverters suitable for the fans to ensure control of the air and smoke flow of the kiln system and the drying tunnel in an energy-saving and quick-adjust manner.
Equip the production facility with the necessary rapid measuring devices and train the facility on the use of these devices so that the operation can be adjusted optimally.
Renovate the kiln in the direction of adding drop-down ceilings to ensure uniformity of the aerodynamics in the kiln, enhance the heat storage capacity of the kiln, thereby increasing the uniformity of the brick products, thereby reducing the rate of waste products of the kiln.
Modifying the trolley by using hollow bricks in the core and large refractory bricks on the top and surrounding surfaces significantly reduces the trolley weight, thereby reducing heat loss due to accumulation on the trolley.
Adjusting the trolley structure simultaneously to minimize the phenomenon of air leakage to the bottom of the trolley
Adjusting to apply a rapid cooling system for the kiln.

## Slide 10: ACTIVITIES CARRIED OUT
Survey and develop technical plans for the renovation of the kiln and drying tunnel systems
Make a list of equipment to be purchased and support businesses in choosing equipment such as exhaust fans, inverters, and ceramic insulation
Make a list of measuring devices needed to calibrate the working mode on the kiln to equip the facility.
Guide the facility in using measuring devices to operate the kiln
Guide the facility in practicing kiln calibration to achieve optimal drying efficiency and produce high-quality products.

## Slide 11: ACTIVITIES CARRIED OUT
The kiln structure has been modified with a suspended ceiling to arrange the bricks in flat blocks
The improved kiln car is constructed using hollow bricks and large refractory bricks

## Slide 12: ACTIVITIES CARRIED OUT
The method of stacking bricks on the kiln car before the modification
The method of stacking bricks on the kiln car after the modification

## Slide 13: ACTIVITIES CARRIED OUT
The inverter was installed after the modification

## Slide 14: THE RESULTS ACHIEVED FROM ENERGY EFFICIENCY ACTIVITIES
Describe | Unit | System before renovation | System after renovation | 
General information |  |  |  | 
Brick production output | bricks per hour | 3825.00 | 4074 | 
Annual brick production | bricks per hour | 30,294,000 | 32,269,981 | 
Energy consumption rate | kJ/kg bricks | 2,293.34 | 1,172.308922 | 
Energy efficiency by improving the drying system and adjusting the air flow in the drying system |  |  |  | 
Energy consumption for water evaporation in the drying system | kJ/kg bricks | 694.78 |  | 755.56
Energy efficiency due to improved drying system | kJ/kg bricks |  |  | 401.7
Energy efficiency due to increased drying efficiency | % |  |  | 58%

## Slide 15: THE RESULTS ACHIEVED FROM ENERGY EFFICIENCY ACTIVITIES
Describe | Unit | System before renovation | System after renovation
Energy efficiency due to reduced losses through flue gas. |  |  | 
Energy released through exhaust | kJ/kg bricks | 394.55 | 215.4
Energy loss is reduced | kJ/kg bricks |  | 179.15
Energy loss is reduced | % |  | 45
Energy efficiency due to reduced cumulative losses with lighter kiln car. |  |  | 
Mass of bricks on the kiln car. | kg/wagon | 3,188 | 4,253
Kiln car construction volume | kg/wagon | 6837 | 3636
Weight of the steel frame of the kiln car | kg/wagon | 663 | 663
Accumulation losses | kJ/wagon | 529397 | 391367
Accumulation losses | kJ/kg bricks | 166.1 | 92.0
Accumulation losses | kJ/kg bricks |  | 74.1
% Energy efficiency by accumulation | % |  | 45%
Total accumulated losses and emissions before project implementation | kJ/kg bricks | 560.6 | 307.4
Total loss reduced by accumulation and emissions | kJ/kg bricks |  | 253.21
% of losses reduced due to accumulation and emissions | % |  | 45%

## Slide 16: THE RESULTS ACHIEVED FROM ENERGY EFFICIENCY ACTIVITIES
Describe | Unit | System before renovation | System after renovation
Replace the coal sprinkled on the kiln with sawdust |  |  | 
Amount of sawdust sprinkled into the kiln | kg/bricks |  | 0.008145
% reduced energy | % |  | 0.52
Fuel cost savings |  |  | 
Total fuel cost | VND/hour | 632,100 | 253,438
Fuel costs are reduced | VND/hour | 378,663 | 
Fuel costs are reduced | VND/year | 2,999,010,647 | 
Cracked waste due to firing | % | 2.15 | 0.88
Poor quality products due to firing | % | 15 | 10
Revenue | VND/hour | 3,066,598 | 3,755,215
Expense | VND/hour | 1,912,500 | 2,444,696
Profit achieved | VND/hour | 1,154,098 | 1,310,520
Total profit from renovation | VND/year |  | 4,237,870,057
Investment costs | VND |  | 4,851,205,350
Payback period | year |  | 1.145

## Slide 17: CONCLUSION FOR THE CASE STUDY
The energy efficiency solution here is a comprehensive approach to improve the entire kiln, drying system, and trolley system, which should bring high efficiency in energy saving in brick production using the Tunnel Kiln.
The effectiveness of the renovation has led to significant accompanying effects, including:
Improving the quality of the finished product
Producing solid brick products while the kiln could not produce this type of product before.
Electricity savings due to the use of frequency converters and changing the way bricks are arranged to reduce air/smoke resistance
In general, each type of technology and factory, when surveyed and balanced, can help find feasible energy efficiency solutions.
Continuously searching for lessons learned, new technology applications, and new effective management methods helps the energy saving process to always be implemented.

## Slide 18: CASE STUDY – SONG DA CAO CUONG JSC
Song da Cao Cuong JSC., Song Da Cao Cuong Joint Stock Company (SCL) is a science and technology enterprise established in 2007 in Hai Duong province and headquartered at Km 28+100 meters, National Highway 18, Pha Lai War.d, Chi Linh City, Hai Duong Province.
Song Da Cao Cuong Joint Stock Company is an enterprise operating in the field of manufacturing new construction materials such as fly ash, ready-mixed dry mortar, stone tile adhesive, glue construction, AAC autoclaved light block

## Slide 19
19
STEAM SYSTEM ANALYSIS
TECHNICAL SPECIFICATIONS ANALYSIS
02
CURRENT STATUS OF STEAM SYSTEM AT FACTORY
There is no condensate recovery system and the feed water is treated at low temperature.
The steam trap system at the bottom of the autoclave is currently not working effectively, so there is a phenomenon of condensate accumulation that is not discharged promptly.

## Slide 20
20
BOILER ANALYSIS​
TECHNICAL SPECIFICATIONS ANALYSIS
02
Boiler | Unit | Price treat
Type oven steam |  | Fluidized bed combustion with fixed grate
Steam pressure | Bar | 14
Operating steam pressure | Bar | 12.5
Design capacity | tph | 8
Boiler feed water temperature | o C | 30
Boiler efficiency | Value
Direct method | 73.37%
Indirect method | 88.55%
In the calculation, the water volume is taken for 5 consecutive days when the factory is operating stably. | 
Using fans to distribute wood chips in the boiler is inefficient.
This results in inefficient mixing of air and fuel .
The excess air coefficient is relatively high, leading to increased exhaust gas losses.
The measured CO concentration in the flue gas was high (280 ÷ 16,593 ppm ) and the unburned carbon content in the ash was high.

## Slide 21
21
1) IMPROVING THE STEAM SYSTEM
PROPOSED PROJECTS
03
INSTALL FLASH CAP TO OPERATE AT PRESSURE ABOUT 1 – 3 BAR
Utilizing heat from condensed water: P = 10 – 12 bar; T = 189°C to supply to the technological line
Recovery the steam released from the autoclave discharge process
Heat water before supplying it to the boiler through a heat exchanger installed inside the dearator.

## Slide 22
22
1) IMPROVING THE STEAM SYSTEM
PROPOSED PROJECTS
03
Install a deaerator operating at 0.1 barg pressure
Deaeration of feed water and increase of feed water temperature to boiler
Use steam generated from the flash tank and from the autoclave exhaust to increase the feed water temperature
Steam piping from the boiler is required to maintain temperature and pressure in the deaerator.

## Slide 23
23
1) IMPROVING THE STEAM SYSTEM
PROPOSED PROJECTS
03
Estimated investment cost of the project | 
1. Investment costs: | Estimated investment cost including equipment, installation, testing and acceptance: VND 1,199,000,000
2. Operating costs: | The system operates entirely on steam pressure and condensate pressure, so there are no system operating costs
3. Maintenance costs | Maintenance cost within 7 years: none because the main equipment is mechanical equipment

## Slide 24
24
2) CONTROL THE COMBUSTION MODE
PROPOSED PROJECTS
03
ILLUSTRATION​ ROOM WIND NEW
COPY DRAW FACE CUT OVEN AFTER WHEN REFORM CREATE CHANNEL GUIDE ARE NOT GAS

## Slide 25
25
2) CONTROL THE COMBUSTION MODE
PROPOSED PROJECTS
03
Estimated investment cost of the project | 
1. Cost head private : | Estimated investment cost including equipment, installation, testing and acceptance: VND 100,000,000
2. Operating costs: | The system operates entirely on mechanical control and operation. Therefore, there are no operating costs.
3. Maintenance costs | Maintenance cost within 7 years: none because the main equipment is mechanical equipment
HOW TO DO: Replace​ the fuel distribution structure | Divide the main air supply chamber into 2 chambers, to control the increase in air supply to the fuel side and decrease the air supply to the non-fuel distribution side.
 | Adjust the amount of air distributed below the furnace  increase the contact between air and fuel

## Slide 26
26
3) INSTALL AN ECONOMIZER FOR MAKE-UP WATER TO UTILIZE THE EXHAUST HEAT FROM THE FLY ASH AND FLY ASH DRYING FURNACE
PROPOSED PROJECTS
03
Estimated investment cost of the project | 
1. Investment costs: | Estimated investment cost including equipment, installation, testing and acceptance: VND 1,589,500,000
2. Operating costs: | The operating costs for the system include only the cost of electricity to supply the boiler with additional water. Electric power of pump motor (kW): 15 Number of operating hours per year (h/year): 6,800 Industrial electricity price (VND/kWh): 1,611 Pump operating cost (VND/year): 164,322,000
3. Maintenance costs | Maintenance cost within 7 years: 10% lubricating oil cost for pumping system

## Slide 27
27
INVESTMENT CAPITAL
FINANCIAL ANALYSIS
04
CAPEX |  |  |  | 
STT | Item | Unit | Value before VAT | Value after VAT
1 | Equipment costs | VND | 2,192,500,000 | 2,411,750,000
2 | Labor costs | VND | 299,500,000 | 329,450,000
3 | Other cost (including management, and designing cost) | VND | 134,000,000 | 147,400,000
4 | Contingency costs | VND | 131,300,000 | 144,430,000
5 |  |  |  | 
 | Total investment cost | VND | 2,757,300,000 | 3,033,030,000
Project 1 - Improve steam system | Equipment and installation costs | VND | 897,000,000 | 986,700,000
 | Labor costs | VND | 90,000,000 | 99,000,000
 | Other costs (including management costs) | VND | 103,000,000 | 113,300,000
 | Total | VND | 1,090,000,000 | 1,199,000,000
Project 2 - Control burning mode | Labor costs | VND | 90,000,000 | 99,000,000
 | Other costs | VND | 1,000,000 | 1,100,000
 | Total | VND | 91,000,000 | 100,100,000
Sub- Project 3 - Install an economizer | Equipment costs | VND | 1,295,500,000 | 1,425,050,000
 | Labor costs | VND | 119,500,000 | 131,450,000
 | Other costs (including management costs) | VND | 30,000,000 | 33,000,000
 | Total | VND | 1,445,000,000 | 1,589,500,000

## Slide 28
APPENDIX TO SUB-PROJECT 1
Drawing of the deaerator
Drawing of the flash tank
Drawing of condensate recovery tank

## Slide 29
APPENDIX TO SUB-PROJECT 1
EQUIPMENT LAYOUT DRAWING OF STEAM SYSTEM IMPROVEMENT PROJECT

## Slide 30
APPENDIX TO SUB-PROJECT 2
ILLUSTRATION​ ROOM WIND NEW
COPY DRAW FACE CUT OVEN AFTER WHEN REFORM CREATE CHANNEL GUIDE ARE NOT GAS

## Slide 31
Current steam system with unutilized three heat resource:
- The condensate discharging at high pressure (11 bar) with high temperature;
- Exhausted steam (12 bar) at high pressure tank discharging into the environment directly.
Proposed steam system:
- Condensate and exhausted steam at high pressure tank flowed in a flash tank;
2. Improving the steam system

## Slide 32
2.2 The deaerator calculation results
2.1 Flash tank calculation results

## Slide 33
3. Controlling burning mode
The ineffective feeding system causes a number of problems:
The biomass burns incompletely;
Especially the unburned pine bran is blown out;
Not meet the standard of CO concentration in the flue gas;
The working environment is polluted;
Impact on the heath of staff around the boiler workshop as well as the entire plant.

## Slide 34
4. Other solutions without economics calculation
Install steam accumulator
Steam load variation
Frequently operates in low load mode
Steam demand suddenly increases water supply at ambient temperature
Ineffective burning mode
Ability to respond to load is slow

## Slide 35: Application of Thermal Oil for Roller kiln in India
The study was conducted by the Bureau of Energy Efficiency (BEE) in the SAMEEEKSHA (Small and Medium Enterprises Energy Efficiency Knowledge Sharing) program, focusing on the ceramic industry cluster in Morbi, Gujarat, India.
In the study in India, Thermal oil was used to recover waste heat from the cooling zone (200-400°C exhaust) and exhaust stack (250-500°C exhaust) of the roller kiln in the production of tiles. Thermal oil reaches a temperature of 200-300°C after heat absorption, which is reused to dry the raw material and heat the combustion air, resulting in a 10-25% reduction in overall energy (from 1,200-1,500 MJ/m² to 800-1,000 MJ/m²). This mechanism is based on the efficient heat transfer ability of thermal oil, optimizing heat flow, and reducing waste heat. Applying this solution in a large factory can save thousands of MWh/year, with a payback period of 2-3 years.
This research is supported by UNIDO and Indian ceramic industry partners, with the goal of promoting sustainable energy solutions in the ceramic industry.

## Slide 36
Tiết kiệm năng lượng tổng thể: 10-25%, tương đương giảm từ 1.200-1.500 MJ/m² xuống 800-1.000 MJ/m² gạch lát
Giảm khí thải CO2: 15-20%, tương đương 0.5-1 tấn CO2/m² gạch/năm
Thời gian hoàn vốn: 2-3 năm cho hệ thống dầu nhiệt (chi phí đầu tư khoảng 1-2 triệu USD cho nhà máy công suất 1 triệu m² gạch/năm)

## Slide 37
THANK YOU!