## Slide 1: TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs
Module 7.6:
Introducing the characteristics of the technological line in the Textile Industry.
MANAGEMENT OFFICERS

## Slide 2: Content
Introduction to the textile industry Characteristics of yarn production and spinning Characteristics of the textile industry

## Slide 3
Introduction to the textile industry

## Slide 4: OVERVIEW OF TEXTILE SECTOR
The textile and garment industry is one of the key manufacturing sectors and a major contributor to the national economy, currently ranking second in the world in terms of export value, only after China.
Number of companies in the industry: approximately 7,000
Number of workers: around 3 million
Textile and garment export turnover in 2024: USD 44 billion. The United States is the largest export market for the industry, followed by Japan, the EU, South Korea, China, and ASEAN countries.
The textile and garment industry consumes large amounts of natural resources such as water, energy, and chemicals. According to the list of key energy-using facilities in 2023, the textile and garment sector accounts for:
7% of total DEUs nationwide, of which 53% are fibre production enterprises, 22% are garment enterprises, and 25 are dyeing and finishing enterprises
Approximately 5% of total energy consumption among all DEUs
Notes: PowerPoint Presentation STK-Ban-tin-IR-ky-39-Q3-9M2024-vie.pdf Ngành Dệt May năm 2024: Xuất khẩu ước đạt 44 tỷ USD, nhiều thách thức trong chuyển đổi xanh Tầm Quan Trọng Của Ngành Dệt May Việt Nam Trong Nền Kinh Tế Xanh

## Slide 5: TEXTILE VALUE CHAIN
The value chain of Vietnam’s textile and garment industry consists of three main segments:
Spinning (fiber production)
Weaving and dyeing
Garment manufacturing

## Slide 6: TEXTILE VALUE CHAIN
 | PRODUCTION OF RAW FIBRES |  | YARN PRODUCTION | GREY CLOTH PRODUCTION | TEXTILE FINISHING | MAKING UP
Process steps | Production of Natural fibers | Production of man-made fibers | Spinning, Twisting | Weaving Knitting | Pre-treatment Dyeing Printing Finishing | Cutting Assembly Finishing Packing
Relevant environmental effects | Land use Pesticide Preservatives water demand | Waste water pollution Air emission Poorly biodegradable textile auxiliaries | Textile auxiliaries and chemicals use Fibre waste Noise pollution Dust emissions | Textile auxiliaries and chemicals use Noise pollution Dust emissions Waste Poorly biodegradable textile auxiliaries | Water demand Waste water pollution Textile auxiliaries Chemicals use Air emissions, Energy demand | Energy demand Waste

## Slide 7: FLOWCHART FROM FIBRE TO GARMENT PRODUCT
Raw fibre
  Harvesting and processing natural fibres (cotton, flax)
  Producting synthetic fibres
Yarn
  Spinning
  Twisting
  Yarn treatment
Raw fabric
  Weaving or knitting fabric
    Woven fabric
    Knitting fabric
Fabric processing
  Dyeing and printing patterns
  Finishing fabric to meet technical requirements
Processed fabric
Pattern & Cutting
  Creating patterns and cutting fabric according to product design
Value addition
  Embroidery, printing or decorating to enhance aesthetics
Sewing
  Assembling using industrial sewing machines
  Stitching hems, attaching zippers, buttons, etc
Finished product
Checking & Rework
Ironing & packing
  Ironing the product
  Labelling and packaging the product
Dispatch and delivery
  Distribution to stores/export

## Slide 8: ENERGY CONSUMPTION LEVELS IN DIFFERENT STAGES OF THE TEXTILE AND GARMENT INDUSTRY
Textile sector | Electrical energy (kWh/kg) | Fuel (HO) , L/kg
Spinning | 3,6 – 3,8 | -
Knitting | 0,3 – 0,4 | -
Weaving | 2 – 2,2 | 0,02 – 0,03
Dyeing & Finishing | 1,6 – 1,7 | 0,6 – 1
Clothing M/fing | 0,8 – 1 | 0,1 – 0,2
Source: Energy saving stragies in textile industry – the case study of Mauritius

## Slide 9
II.
Characteristics of yarn production and spinning

## Slide 10: YARN PRODUCTION

## Slide 11: YARN PRODUCTION
Raw materials such as cotton and polyester are mainly imported from countries like Australia, the United States, Brazil, etc.
Production process: Fibers and cotton are spun into natural yarn by textile and spinning mills. The remaining type of yarn is synthetic yarn, which is created through petrochemical processes using raw materials such as oil and gas.
Vietnam is the 6th largest exporter of fibers and yarns in the world

## Slide 12: YARN PRODUCTION (AKA SPINNING)
QC 1
QC 2
QC 3
Saleable Waste
Contamination
Dust
Short Cotton fibre
W A S T E
Cotton Bales
Laps
Saleable Waste
Contamination
Dust
Short Cotton fibre
W A S T E
Saleable Waste
Contamination
Dust
Short Cotton fibre
W AS TE
Reusable Waste
Short Fibre Cotton
Used in other processes
QC 4
Reusable Waste
Handling waste (Cotton fibre)
W A S T E
Saleable Waste
Lickerin Waste
Imputities
Short fibre & fibre Neps
Dust
Sliver
Blended
Beat Cotton
Energy: 264 kWh
Energy: 141 kWh
Source: Material Flow Cost Accounting of a Spinning Mill by Espire Consult
QC 1 Mixing, Plucking, Blending
QC 2 Multimix, Beating
QC 3 Sorting, Beating, Scutcher
QC 4 Carding
QC 5 Breaker Drawing
QC 6 Finisher Drawing
QC 7 Simplex
QC 8 Ring
QC 9 Auto Cone
Example Material Flow Chart

## Slide 13: YARN PRODUCTION (AKA SPINNING)
Material Waste
Short Fiber
Material Waste
Short Fiber
Material Waste
Short Fiber
Drawing Sliver
QC 5
QC 6
QC 7
W A S T
E
W A S T
E
W A S T
E
Energy: 317 kWh
Drawing Sliver
Roving
Material Waste
Pneumafil
Yarn Loss (mishandling)
Material Waste
Faulty Yarn
Bobbin
QC 8
QC 9
W A S T
E
W A S T
E
Cones
Inventory
Energy :952 kWh
Energy :257 kWh
Source: Material Flow Cost Accounting of a Spinning Mill by Espire Consult
Example Material Flow Chart
QC 1 Mixing, Plucking, Blending
QC 2 Multimix, Beating
QC 3 Sorting, Beating, Scutcher
QC 4 Carding
QC 5 Breaker Drawing
QC 6 Finisher Drawing
QC 7 Simplex
QC 8 Ring
QC 9 Auto Cone

## Slide 14: TEXTILE PROCESS – COTTON FIBER
Two popular technologies for the production of cotton yarns:
  Producing pile yarns (CD)
  Producing OE yarns
The quality of the yarn output depends largely on the input materials (70% of raw materials from cotton).
Machinery and equipment have the effect of minimizing breakage fibers in the production process, accordingly. As new and modern, the lower the fiber error rate.
Cotton
Opening, blending and carding
Sliver formation
Roving
Bobbin winding
Heat setting
CD yarn
Cotton
Opening, blending and carding
Sliver formation
OE spinning machine
Heat setting
OE yarn

## Slide 15: TEXTILE PROCESS – POLYESTER FIBER
Polyester yarns include short fibers (staple fibers) and long fibers (filament yarns).
Short or long fibers are continuously blended with cotton fibers to produce different types of yarns.
Longer fibers are more applicable due to the continuity of yarns and lower cost of production.
Notes: Về công nghệ sản xuất sợi cotton, các doanh nghiệp sợi tại Việt Nam có thể sản xuất sợi CD và sợi nồi cọc đáp ứng nhu cầu thị trường thế giới. Tuy nhiên, hiện tại máy móc ngành sợi trong nước vẫn chưa được nâng cấp đồng bộ, một số nhà máy vẫn sử dụng máy móc cũ nên chất lượng sợi không đồng đều giữa các nhà máy.
Về công nghệ sản xuất sợi tổng hợp, hiện tại chỉ có 4 doanh nghiệp tại Việt Nam sản xuất sản phẩm sợi dài (sợi filament) từ hạt nhựa (công nghệ Chips spinning) là Sợi Thế Kỷ, Đông Thiên Phú, Hualon và Hưng Nghiệp Formosa. Các doanh nghiệp sản xuất sợi tổng hợp khác trong nước sản xuất sợi ngắn (sợi staple) từ xơ ngắn nhập khẩu.

## Slide 16: SOME TYPES OF FIBERS
Bio-based fibers: DuPont™ Sorona® EP - Poly Trimethylene Terephthalate, a thermoplastic polymer. Sorona is partially made with annually renewable plant-based ingredients.
Sorona® EP: Has molding characteristics equivalent to high-performance PBT (Polybutylene Terephthalate).
Biopolyester:
Partially bio-based polymer
Polyethylene Furanoate (PEF)
Bio-based TPA for PET derived from sugar
Bio Nylon 6: A more sustainable nylon made from renewable feedstocks instead of crude oil
Bio Nylon 6,6

## Slide 17: SPINNING ENERGY CONSUMPTION RANGES
Source: UNIDO Sectoral Analysis on Renewable Energy and Energy Efficiency in Pakistan (2019)

## Slide 18: ENERGY BALANCE OF A SPINNING PROCESS
Main Energy type: Electrical Power
Major utility: Compressed Air and Humidification Plant
Largest consumer of energ : Ring Frames
7%
14%
17%
49%
13%
Back Processes (Mixing till Blow room) Carding
Drawing & Simplex Ring
Auto Cone
Source: Material Flow Cost Accounting of a Spinning Mill by Espire Consult
Example Energy Balance

## Slide 19
III.
Characteristics of the textile industry

## Slide 20: WEAVING

## Slide 21: WEAVING
Common Methods
  Power Looms
  Water Jet Looms (mostly synthetic fiber)
  Air jet Looms
  Rapier Looms
Air Jet Loom Application Suitable for
  plain and textured fabrics
  fine high-density fabrics
  High-speed bulk production
Rapier Loom Application Suitable for
  multi-color weft fabrics
  yarn-dyed fabric
  double-layered velvet fabrics
  terry fabrics
  decorative fabrics
  Much slower than air jet loom
  Moderate energy consumption

## Slide 22: ENERGY BALANCE – EXAMPLE (WEAVING)

## Slide 23: SPINNING ENERGY BENCHMARKING - PAKISTAN
Source: UNIDO Sectoral Analysis on Renewable Energy and Energy Efficiency in Pakistan (2019)

## Slide 24: WEAVING ENERGY CONSUMPTION RANGES
Source: UNIDO Sectoral Analysis on Renewable Energy and Energy Efficiency in Pakistan (2019)

## Slide 25: WET PROCESSING

## Slide 26: WET PROCESSING
Finishing
Stenter
Water proofing
Wrinkle free treatment
Softening treatment
Flame retardancy treatment
Odour resistance
treatment
Oleophobic treatment
Biocide treatment Coating
Finishing
Dyeing
Printing
Dyeing & Printing
Shearing
Combing
Singeing, Desizing
Scouring and Bleaching or Solomatic Bleaching
Washing
Mercerising, Drying
Stenter Shrinking
Pre-treatment

## Slide 27: TEXTILE DYEING TECHNOLOGY
Spinning, combing, sliver formation, bobbin winding
  Input materials
Sizing
  Water, starch, additives, steam
Weaving
Desizing
  Enzym, NaOH
Boiling
  NaOH, chemicals, steam
Acid treatment and washing
  H2SO4, H2O2, detergents
Bleaching
  H2SO4, CaOCl2 chemicals
Washing
  H2SO4, H2O2, detergents
Mercerizing
  NaOH, chemicals
Dyeing and printing
  Dye solutions
Washing
  H2SO4, H2O2, detergents
Finishing and drying
  Steam, starch, chemicals
Product
Wastewater
Wastewater contains hydrolyzed starch size and NaOH

## Slide 28: A- DYEING APPROACHES
Material dyed
Twine
Yarn
Knitted/woven fabric
Garment
Process
Batch
Continuous
Dyeing techniques
Gel dyeing (in the production of artificial fibers)
Pigment dyeing (with binder)
Diffusion dyeing
Exhaust dyeing
Ozone dyeing
Ozone can be used on indigo or black sulfur fabrics.
Use of ozone requires up-front investment in the ozone machine and the generators, along with safety training for workers.
Dyeing methods

## Slide 29: B- FABRIC DYEING
Cellulosic Fabric Dyeing (Cotton, Viscose, lyocell, linen, hemp etc.)
  Reactive Dyes
  Temperature Required around 65 deg C for which machines work at atmospheric pressure
Synthetic Fabric / Blended (Polyester, PC, Nylon etc.)
  Disperse Dyes
  Temperature Required Above 100 deg C for which machines work above atmospheric pressure
Batch/Discontinuous
  Open Width form Dyeing: Open Jiggers and Pressure Jiggers, Beam,
  Rope form Dyeing: Jets, Winches, Soft flow machines / HT machines (Knitted fabric)
Semi Continuous
  Pad Batch / Cold Pad Batch (CPB) (For Cellulosic Materials and alternative to reactive dyeing)
  Pad Jig
  Pad Roll
Continuous
  Chemical Steam Pad
  Pad Dry Steam (PDS)
  Pad Dry Pad Steam (PDPS)
  Pad Dry Cure (PDC)
  Pad Thermosol Dyeing

## Slide 30: DYEING– BASIC STEPS
Step 1
  Colouring agents (mostly powder form, dye) dissolved in "dye liquor" according to a given recipe.
  Dyestuffs diffuse from "liquor" to the substrate
Step 2
  Dyestuff accumulates on the surface of the yarn/fabric => the question of the affinity of the dyestuff to the fibre
Step 3
  Penetration of the fibre with the dye (slower than surface accumulation) => prerequisite given for hydrophilic fibres (micropores); in the case of hydrophobic fibres => heating necessary (often over 100 degrees)
  Addition of salts to overcome electrostatic surface barriers
Step 4
  Fixation of dyestuffs (heat, auxiliaries)

## Slide 31: C- FABRIC PRINTING
In industry, 03 types of machines are used for printing the fabric:
  Rotary Printing
  Flatbed / Panel Printing
  Digital Printing
Normally fabric is printed through two methods
  Pigment Printing: Surface Printing where the design is fixed with the help of binders and fixers. Curing is done through dry heat in curing chambers above 100 oC (depending upon the color recipe)
  Reactive Printing: The colour design is attached to fabric as a result of chemical reaction. Curing is done in a high temperature (close to 100 oC) moist environment. This type of fabric requires washing after printing.

## Slide 32: D- FINISHING
In Textiles, two types of Finishing Processes are used
  Chemical Finishing in Stenter Machines: Either direct firing of natural gas or indirect heating through Thermal Oil
  Mechanical Finishing: Mostly steam is used for indirect heating at the following machines
    Calendars
    Comfort
    Sanforizer

## Slide 33: Typical energy requirements for textile wet processes – by product form, machine type, and process
(Carbon Trust, 1997)

## Slide 34: ENERGY USE IN TEXTILE
Electricity
Thermal energy

## Slide 35: GARMENT

## Slide 36: GARMENT INDUSTRY VALUE CHAIN
The value of Vietnam's textile and garment industry in the global value chain is mainly concentrated in the processing stage (CMT – Cut, Make, Trim)
Notes: FPT Securities. 2014. Textile & Apparel industry report – Opportunities for breakthrough

## Slide 37: Sewing technology and energy consumption in garment factories
Raw material warehouse
Batches
Label
Fusing
Printing
Thêu
Preparation for sewing
Sewing
Intermediate pressing
Thread cutting
Inspection
Stain removal
Pressing
Folding
Labeling
Packing
Hoàn thiện và đóng gói
Washing, Dyeing, Tumbling, etc.
Treatment
Spreading
Cutting
Cutting
Design
Pattern construction
Preparation for cutting
Design, Pattern cons, Prep, Cutting
Finished product warehouse
Boiler, LNG, LPG, CNG,…
Compressed air
Electrical Energy

## Slide 38: Sewing technology and energy consumption in garment factories
Fuel/Gas
Boiler
Transformation station
HVAC
Lighting
Air compressor
Vacuum
Logistics
Raw material warehouse
Batches
Label
Fusing
Printing
Embrodering
Preparation for Sewing
Sewing
Intermediate pressing
Thread cutting
Inspection
Stain removal
Pressing
Folding
Labeling
Packing
Finishing and packing
Washing, Dyeing, Tumbling,…
Treatment
Spreading
Cutting
Cutting
Design
Pattern construction
Preparation for cutting
Design, pattern, prep, cutting
Finished product warehouse
Boiler, LNG, LPG, CNG,…
Compressed air
Electricity
Administrative/Social

## Slide 39: ENERGY BALANCE OF A GARMENT FACTORY
Chart: 
| 50 | 16 | 26 | 1.5 | 3.5 | β | 45 | 25 | 17 | 2 | 7 | 1 | 42 | 17 | 24 | 3 | 9 | 5 | 45 | 22 | 21 | 2 | 5 | 4 | 44 | 16 | 13 | 6 | 4 | 2 | 51 | 26 | 12 | 5 | 4 | 2 | Air Conditioning | Lighting | Sewing Machines | Pumps/Fans/Blowers | Compressor | Other Equipment
Energy Consumption(%) Avg | 46 | 20 | 19 | 3 | 5 | 3
Air Conditioning | 
Lighting | 
Sewing Machines | 
Pumps/Fans/Blowers | 
Compressor | 
Other Equipment | 

## Slide 40: ENERGY USING IN A GARMENT FACTORY – VIETNAM
Garment factory (2,440 workers)
Garment factory(728 workers)

## Slide 41
THANK YOU!