## Slide 1: TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs
Module 7.7:
Introduction to typical technological process characteristics in the seafood processing industry
MANAGEMENT OFFICERS

## Slide 2: CONTENT
Chemical composition of seafood
Changes in seafood after death
Seafood freezing techniques
High-pressure processing (HPP) techniques in seafood processing and preservation
High-temperature techniques in seafood processing and preservation

## Slide 3
Main chemical components: water, protein, lipids, carbohydrates, vitamins, minerals, …
Chemical composition of some seafood species
CHEMICAL COMPOSITION OF SEAFOOD
 |  | Component | Protein (%) | Lipid (%) | Glucid (%) | Tro (%) | Canxi mg% | Phospho mg% | Iron mg% | 
 |  | Species |  |  |  |  |  |  |  | 
 |  | Squid | 17 - 20 | 0,8 | - | - | 54 | - | 1,2 | 
 |  | Shrimp | 19 - 23 | 0,3 - 1, | 2 | 1,3 - 1,8 | 29 - 30 | 33 - 67 | 1,2 - 5,1 | 
 |  | Oyster | 11 - 13 | 1 - 2 | - | 2,2 | 0,21 | - | - | 
 |  | Shellfish | 8,8 | 0,4 | 3 | 4 | 37 | 82 | 1,9 | 
 |  | Mussel | 4,6 | 1,1 | 2,5 | 1,9 | 668 | 107 | 1,5 | 
 |  | Crab | 16 | 1,5 | 1,5 | - | 40 | - | 1 | 
 |  | Snail | 11 – 12 | 0,3 - 0,7 | 3,9 - 8,3 | 1 - 4,3 | 1310 - 1660 | 51 - 1210 | - | 

## Slide 4: The chemical composition of muscle tissue in fatty and lean fish species (%)
 | Water | Protein | Lipits | Gluxit Carbohydrate | Minerals | 
Lean fish | 80 | 16-19 | 0,1-2 | <0,5 | 0,5-2 | 
Fatty fish | 60-80 | 16-19 | 2-22 | <0,5 | 0,5-2 | 
Species
Size
Habitat
Food source
Genetic traits
Factors affecting chemical composition:
Gender
Level of expertise
Season
Age
-….
CHEMICAL COMPOSITION OF SEAFOOD

## Slide 5
CHANGES IN SEAFOOD AFTER DEATH

## Slide 6
CHANGES IN SEAFOOD AFTER DEATH

## Slide 7: FROZEN SEAFOOD TECHNOLOGY
      Purpose of the Freezing Process:
        Lowering the temperature to slow down spoilage
        The product, when thawed after freezing storage, retains quality close to the original raw material.
        Freezing and refrigeration are commonly applied for exported seafood.
  Freezing Process
  - The thermodynamics in the freezing process of food are based on the changes in the properties of water in the product due to the effect of low temperature.
  - Freezing is the process of converting most of the water in fish into ice.
  - Seafood contains about 75% water by weight.
  - Water in seafood exists in dissolved solvent form and colloidal form
  - The freezing point drops below 0°C (-10°C to -20°C).

## Slide 8: FROZEN SEAFOOD TECHNOLOGY
Freezing process
Throughout the freezing process:
Water gradually turns into ice.
The concentration of dissolved organic and inorganic salts increases.
The freezing point continues to decrease.
At -1°C to -5°C, approximately 75-80% of the water freezes.
The freezing process goes through three main stages

## Slide 9: FROZEN SEAFOOD TECHNOLOGY
Stage 1: The product temperature drops rapidly to 0°C, the solution is rapidly cooled, and crystallization nuclei begin to form.
Stage 2: (Heat cessation phase)
A large amount of heat is released to convert most of the bound water into ice.
There is very little change in temperature. Ice crystals form and gradually increase in size.
Approximately ¾ of the water in seafood is converted into ice.
Stage 3:
- The product temperature continues to decrease.
A small amount of heat is released.
A small amount of ice crystals is formed.

## Slide 10: FROZEN SEAFOOD TECHNOLOGY

## Slide 11: HPP TECHNOLOGY IN SEAFOOD PROCESSING AND PRESERVATION
    Introduction
    - HPP: High Pressure Processing
      Utilizes high pressure (400–1000 MPa) to create new food products.
      The pressure required to inactivate most microorganisms is ≥ 60,000 pounds/inch².
      Maintains the natural freshness, quality, and extends the shelf life of products.
      Pressure is applied uniformly throughout the entire food product.
Characteristics of High Pressure Processing (HPP):
Conducted at low temperatures but capable of inactivating microorganisms and enzymes.
The quality of HPP-processed foods is similar to that of fresh products.
Foods processed with HPP technology are safe and beneficial for health.

## Slide 12: HPP TECHNOLOGY IN SEAFOOD PROCESSING AND PRESERVATION
16
7
Characteristics of High Pressure Processing (HPP)
Helps improve product functionality.
The applied force is isostatic compression (multi-directional pressure).
Pressure transmission is unimpeded.
The compression is reversible.
Shell removal of mollusks and crustaceans → facilitates easier meat extraction.

## Slide 13
    Dried Fish Product
Reduces the moisture content in the product from 70–80% down to 8–10%.
+ Inhibits the growth of microorganisms.
+ Slows down the rate of undesirable reactions.
The main factors affecting drying rate
Air temperature :
+ Air temperature increases → drying speed increases
+ If the temperature is too high, the product may darken in color
      Air humidity
+ The lower the humidity, the faster the drying process
+ When the air humidity reaches around 80%, the drying process stops and the product may start absorbing moisture
HIGH TEMPERATURE TECHNIQUES IN SEAFOOD PROCESSING AND PRESERVATION

## Slide 14
Main factors affecting drying rate (continued)
- Air velocity:
+ High air velocity → uneven drying temperature
+ Low air velocity → longer drying time and poorer meat quality
+ ptimal air velocity: approximately 0.4 – 0.6 m/s
When airflow moves parallel to the fish surface, the drying process is faster. When airflow hits the fish surface at a 45-degree angle, the drying rate is the slowest.
- Warm incubation.
+ Promoting water movement within fish flesh
+ Reduces drying time and improves efficiency.
- Raw material
HIGH TEMPERATURE TECHNIQUES IN SEAFOOD PROCESSING AND PRESERVATION

## Slide 15
The relationship between moisture content and water activity
Main factors affecting the shelf life of dried products
- Water activity
+ Salted fish: High moisture– low aw
+ Dried fish: Low moisture– low aw
Temperature and insect infestation
HIGH TEMPERATURE TECHNIQUES IN SEAFOOD PROCESSING AND PRESERVATION

## Slide 16
Dried fish processing technology.
Raw materials
Salting
Storage
Desalting
Arrange fish on racks
Drying
Packaging
Pre-processing
HIGH TEMPERATURE TECHNIQUES IN SEAFOOD PROCESSING AND PRESERVATION

## Slide 17
Dried Fish Processing Technology
Raw material processing: After harvesting, the fish need to be sorted by weight and quality. For fish weighing over 5kg each, the head is removed, scales are scraped off, fins are cut, the belly is slit open to remove internal organs, and the fish is cut into 15cm pieces. For thick-fleshed fish, fillets are made by removing the bones from both sides of the fish. For fish weighing over 0.5kg each, the fish is slit along the backbone to remove the internal organs. For flat fish like pomfret, a cut is made along the backbone to remove the internal organs. After processing, the fish is washed clean and drained, and any fishy odor can be removed by using a solution of 40% water, 0.3% vinegar, and 1% ginger water.
Fish placement on racks: Before drying, use a clean cloth to rub the cut areas to smooth the surfaces. Initially, place the fish belly-side down, then turn them over after some time. After 2-3 days of drying, the fish should be left to rest (incubated) for one day, and then dried again for 2-3 more days.
Drying process: The drying time and temperature depend on the size of the raw material. During drying, the fish must be turned.
HIGH TEMPERATURE TECHNIQUES IN SEAFOOD PROCESSING AND PRESERVATION

## Slide 18
  Smoked fish products
Purpose of Smoking
Develop smell for product .
Create a new form of the product
Extend the shelf life
Eliminate microorganisms on the surface.
Reduce the moisture of the product
Factors affecting the smoking process
Raw material source
Do not use wood with high resin content because the smoke will contain a lot of soot, causing the fish products to have a darker color, a bitter taste, and reduced sensory quality.
+ The fuels used for smoking include oak, jackfruit wood, chestnut, etc
+ The fuel must be controlled to burn under incomplete combustion conditions
+ The optimal moisture content of the fuel is about 25–30%.
HIGH TEMPERATURE TECHNIQUES IN SEAFOOD PROCESSING AND PRESERVATION

## Slide 19
Factors Affecting the Smoking Process
Smoke Composition
Influences the quality + Product preservation capacity
Smoke contains about 300 compounds, including phenols, organic acids, carbonyls, hydrocarbons, and various gases such as CO₂, CO, O₂, and N₂.
Phenol compounds: There are about 20 phenolic compounds
They inhibit oxidation processes, contribute to the color and aroma of the product, and eliminate microorganisms that contaminate the food.
Alcohol compounds:
Contribute smell to smoked products
Eliminate microorganisms
Organic acids: They have preservative effects and cause protein coagulation
Carbonyl compounds: Contribute to the smell and color of the product
HIGH TEMPERATURE TECHNIQUES IN SEAFOOD PROCESSING AND PRESERVATION

## Slide 20
Technology for processing smoked fish products
HIGH TEMPERATURE TECHNIQUES IN SEAFOOD PROCESSING AND PRESERVATION
Draining
Hanging or tray placement
Preliminary drying
Smoking
Cooking
Inspection
Grading
Packaging
Finished product
Raw materials
Pre-processing
Salting
Desalting

## Slide 21
Technology for processing smoked fish products
Preparation of raw materials: The fish used for smoking includes red snapper, mackerel, tuna, carp, etc. After processing, the head, fins, scales, and internal organs are removed, and the fish is thoroughly washed. For larger fish, fillet the two sides; for smaller fish, leave them whole.
Salting: The salting ratio is determined based on the size of the fish, ensuring that the final salt concentration reaches 1.5 - 2% when the fish is salted.
Smoking: The fish are hung on hooks in the smoking room, and smaller fish are arranged evenly in trays to ensure uniform smoke distribution. The smoking temperature is approximately 40 – 60°C for cold smoking and 120 – 140°C for hot smoking
Cold smoking lasts about 3 - 4 days, while hot smoking takes about 2 - 4 hours. For cold smoking, a discontinuous method is typically applied (smoking during the day, warming the fish at night, and in the morning, the smoking room door is opened to allow steam to escape)
HIGH TEMPERATURE TECHNIQUES IN SEAFOOD PROCESSING AND PRESERVATION

## Slide 22
Canned Fish Products
The principle of the thermal processing of canned goods: destroy or inactivate enzymes and bacteria, prevent contamination from the external environment.
Canned fish retains its quality without refrigeration.
- Extends shelf life and increases the commercial value of the product
a. Selection of Thermal Processing Procedures
High-acid products (pH < 4.5): A moderate heat treatment is applied.
Medium-acid products (pH = 4.5 – 5.3)
The sterilization process requires careful control, typically based on the destruction of Clostridium botulinum spores.
Low-acid products (pH > 5.3): A high-temperature heat treatment is required.
HIGH TEMPERATURE TECHNIQUES IN SEAFOOD PROCESSING AND PRESERVATION

## Slide 23
Canned Fish Products
b. Thermal processing procedure
      Thermal Transfer Process in Canned Fish Products
      - In fish, the heat transfer process by conduction predominates.
- To prevent the fish from overheating at the points near the can wall and to increase the heat transfer rate to the coldest point, sauce, oil, or brine is added to the can
The effect of processing temperature:
  Temperature causes the fish to become tender and lose volatile compounds
Protein denaturation at high temperatures leads to the loss of 9-28% of water.
Vitamins in the B group, such as B1, B2, B12, folic acid, and nicotinic acid, are significantly lost.
Flavor changes
The color change of the fish occurs when low-quality ingredients are used.
HIGH TEMPERATURE TECHNIQUES IN SEAFOOD PROCESSING AND PRESERVATION

## Slide 24: Steamed
The doneness of steamed shrimp depends largely on the large/small uniform ratio.
The higher the uniformity, the easier it is to lose size.
The uniformity is equal to 10% large shrimp divided by 10% small shrimp.
HIGH TEMPERATURE TECHNIQUES IN SEAFOOD PROCESSING AND PRESERVATION

## Slide 25: Shrimp processing process
Raw material
Peel, remove the intestine, scrape &slice
IQF, steam
Processing procedure of white flesh fish
Grading
Remove the head
Split size
HIGH TEMPERATURE TECHNIQUES IN SEAFOOD PROCESSING AND PRESERVATION

## Slide 26: PROCESSING OF WHITE-FLESH FISH
Pretreatment Pretreatment of the fish involves the removal of ice, washing, grading according to size and de-heading, if this has not been done previously. Large fish may also be scaled before further processing.
Filleting The next step in the process is filleting, which is generally done by mechanical filleting machines. The filleting department is generally separated from the pretreatment area by a wall, to prevent workers and goods passing from the non-sterile pretreatment area to the sterile filleting area. The filleting machines comprise pairs of mechanically operated knives which cut the fillets from the backbone and remove the collarbone. Some fish fillets may also be skinned at this stage.
Trimming In the trimming department, pin bones are removed and operators inspect the fillets, removing defects and any parts that are of inferior quality. Offcuts are collected and minced. Depending on the final product, the fillets may be cut into portions according to weight or divided into parts such as loin, tail and belly flap. As a final step before packaging, the fillets are inspected to ensure they meet product standard.
Packaging/storage Fresh products are packaged in boxes with ice, the ice being separated from the products by a layer of plastic. Frozen products can be packed in a number of ways. Fillets or pieces can be individually frozen and wrapped in plastic, but the most common method is for them to be packed as 6–11 kg blocks in waxed cartons. The blocks are typically frozen and then kept in cold storage.

## Slide 27
THANK YOU