## Slide 1
Module 7.8 Introducing the characteristics of technology lines in the plastic manufacturing industry.

## Slide 2: Content
INFORMATION ON TYPICAL TECHNOLOGICAL LINE CHARACTERISTICS PLASTIC INDUSTRY
SOME TECHNOLOGICAL LINE CHARACTERISTICS IN PLASTIC PRODUCTION LINE

## Slide 3
INFORMATION ON TYPICAL TECHNOLOGICAL LINE CHARACTERISTICS PLASTIC INDUSTRY

## Slide 4: Preliminary Plastic Materials
Plastic is a structurally flexible material from organic compounds that has the ability to change shape under the effects of heat or pressure and retain that deformation at the end of the process. Flexible materials are durable, lightweight, hard to break, and come in a variety of colors.
Plastics are organic compounds derived from fossil materials such as petroleum, natural gas, coal or derived from biological materials such as corn starch, potatoes, and cassava. Plastics are recyclable to complete a cycle of the product. Currently, most of the plastic materials used in the world are derived from fossil materials.

## Slide 5: Classification of plastic materials
Thermoplastics: It is a type of plastic material that when heated to the melting point, it will be transformed in physical shape and retain that shape when the temperature decreases. This process can be applied many times, making thermoplastics a very renewable material. Some popular thermoplastics are PolyEthylene (PE) and derivatives (HDPE, LDPE and LLDPE), PolyPropylene (PP), PolyStyrene (PS), PolyVinyl Chloride (PVC). Thermoplastics account for about 75% of the global plastics consumption structure. The most used thermoplastics are PE, PP, PVC and PET. In the global plastic material consumption structure in 2017, PE (with HDPE, LDPE, LLDPE derivatives) and PP accounted for the highest proportion with 28% and 20%, respectively. Ranked 3rd in the consumption structure is PVC with 12%.
Thermosetting: is a type of plastic material that, when heated to a certain temperature, will change both in physical shape and chemical properties, creating a three-dimensional spatial structure and can no longer be remelted. Therefore, thermoset plastics are not capable of regeneration. Some popular thermosetting resins are Epoxy, Vinyl Ester, Melamine, PolyUrethane.

## Slide 6: The development of the plastic industry in the world

## Slide 7: The value chain of the plastics industry

## Slide 8: Value chain of the downstream segment

## Slide 9: Preliminary about plastic production in Vietnam
Vietnam's plastic manufacturing industry has been developing strongly, making an important contribution to the national economy.
This growth is driven by increasing domestic consumer demand and exports.
Plastic products have many diverse designs, easy to produce and are used a lot in life.

## Slide 10: Overview of Vietnam's plastic industry
Number of businesses:
+ More than 2,000 enterprises operating in the field of plastic production.
Output growth:
+ 2020: 7.9 million tons, up 6.8% compared to 2019.
+ 2022: 9.54 million tons, up 1.9% compared to 2021.
Turnover:
+ 2022: 25.18 billion USD, up 5.68% compared to 2021.

## Slide 11: Value chain of Vietnam's plastics industry

## Slide 12: Plastic product structure

## Slide 13: Trends in the development of the plastics industry
Product Conversion:
Reduce the proportion of packaging plastics, increase construction plastics and engineering plastics.
Technology investment:
Applying advanced technology and automation in production.
Green Product Development:
Production of recycled plastics, bioplastics, environmentally friendly.

## Slide 14: Future prospects
Output growth: Forecast to reach 10.92 million tons by 2024, with a CAGR of 8.44% over 2024-2029.
Market expansion: Continue to conquer new markets, increase market share in the US, EU, Japan.
Sustainable Development: Towards green production, minimizing environmental impact.

## Slide 15: BENCHMARKING IN THE PLASTIC INDUSTRY
According to Article 5 of Circular 29/2024/TT-BCT, Benchmarking for the plastic industry are:
:
Plastic products | Quy mô (triệu lít/năm) | Benchmark (kWh/kg) | Other Relevant Requirements
Packaging plastics | Bags | ≤ 0,95 | Manage and monitor the production process to determine the amount of energy consumed. Facilities with SEC higher than benchmarking must report and justify the reasons to the competent authorities and submit an implementation plan to meet the benchmarking requirements based on the energy audit report. Report to the local DOIT by January 31 each year on the implementation status of the benchmarking of the facility (as specified in Article 5 of the Circular
 | Bottles | ≤ 1,45 | 
 | Packaging | ≤ 0,62 | 
Plastic building materials | PVC | ≤ 0,35 | 
 | HDPR&PPR | ≤ 0,58 | 
Household plastics |  | 1,0 | 
Engineering plastics |  | 1,0 | 

## Slide 16
II.
SOME TECHNOLOGICAL LINE CHARACTERISTICS IN PLASTIC PRODUCTION LINE

## Slide 17: Production process
The plastic production process involves
many closely related stages, from material
processing to product shaping and finishing.
Each stage plays an important role
in ensuring quality and production efficiency.

## Slide 18: Overview of the plastic production process
The production process of conventional plastics includes the following steps:
Selection and processing of raw materials. Blending and granulating. Heating and extrusion. Product shaping. Cool and cut. Finishing the product. Quality inspection. Packaging and storage.

## Slide 19: Stage 1 – Selection and processing of raw materials
Main Ingredients:
+ Primary plastics (PE, PP, PVC, ABS...). + Recycled plastic (used in some products).
Handle:
+ Clean, dry to remove impurities and moisture. + Ensure that raw materials meet standards before production.

## Slide 20: Stage 2 – Blending and creating plastic pellets
Blend:
+ Mixing plastics with additives (plasticizers, stabilizers, colors, additives that increase mechanical properties).
Plastic granulation:
+ The mixture is extruded through a granulator to produce granular plastics. + Easy to store and use in the next stages.

## Slide 21: Stage 3 - Heating and Extrusion
Heating:
+ The resin is heated in an extruder, the temperature ranges from 180-280°C depending on the type of plastic.
Extrusion:
+ The molten plastic is extruded through the forming mold, forming a continuous plastic strip. + Usually applicable to the production of plastic packaging, plastic pipes, plastic films.

## Slide 22: Stage 4 - Product shaping
Forming Method:
Injection Molding: The molten plastic is injected into the mold, cooled and shaped.
Blown film: Forming plastic film products (bags, packaging).
Extrusion-spinning: Production of plastic fibers, plastic pipes, plastic sheets.
Application: Shaping plastic products for household, industry, packaging.

## Slide 23: Stage 5 - Cooling and trimming
Cooling:
+ Plastic products are rapidly cooled in water or air to keep their shape.
Trimming:
+ Cut off the excess, adjust the size according to the standard.
+ Make sure the product has a smooth surface, no error.
Cooling
Trimming

## Slide 24: Stage 6 - Product Completion
Finishing:
+ Printing logos, product information. + Cover the surface with protective layers (if necessary).
Enhanced Properties:
+ Using reinforcement technology to increase durability, heat resistance, and bearing strength.

## Slide 25: Stage 7 - Quality Inspection
Standard Tests:
+ Thickness, size, mechanical strength, heat resistance. + Check the uniformity and color of the product.
Eliminate defective products:
+ Substandard products are recycled or disposed of.

## Slide 26: Stage 8 - Packaging and storage
Packed:
+ Products are packed in batches or according to customer requirements.
Inventory:
+ Store in clean, dry storage, away from direct sunlight.
Preparing for Shipping:
+ Ensure the product is protected during shipping to the customer.

## Slide 27
THANK YOU!