## Slide 1
Module 8.8
Energy efficiency opportunities in the plastics production lines.
MANAGEMENT OFFICERS
TRAINING PROGRAMME FOR INDUSTRIAL ENTERPRISEs

## Slide 2: CONTENT
Introduction of energy consumption in the plastics industry
EEMs in the plastics industry

## Slide 3
Introduction of energy consumption in the plastics industry

## Slide 4: 1. Introduction
The plastics industry is one of the major energy consumers, especially in the heating, extrusion and shaping stages. The application of energy-saving solutions not only reduces production costs, but also protects the environment and improves competitiveness.
ENERGY EFFICIENCY IN PLASTIC INDUSTRY

## Slide 5: 2. The current state of energy consumption in the plastics industry
Primary Energy Source:
+ Electricity: Accounting for 60-70% of energy consumption, used in machinery and production systems. + Fossil fuels: Coal, oil, gas in the heating stages.
Challenge:
+ Low energy efficiency in many production facilities. + Waste of energy due to outdated machinery and ineffective management.
Electricity
60 – 70%
WASTE ENERGY
FOSSIL FUEL

## Slide 6
II. EEMs in the plastics industry

## Slide 7: EEMs 1 – Optimize the heating system
Character:
+ Heating accounts for a large proportion of energy consumption.
Solution:
+ Using a recirculating heating system: Utilizing waste heat for reuse in the production process.
+ Good thermal insulation: Reduce heat loss from heating appliances.
Benefit:
+Save 20-30% of energy in the heating process.

## Slide 8: EEMs 2 – Use high-performance machinery
Character:
+ Old machinery consumes a lot of energy and does not operate efficiently.
Solution:
+ Invest in new-generation, energy-saving machinery. + Periodic maintenance to maintain operational performance.
Benefit:
+Reduce power consumption by 15-25%. +Increase production productivity.

## Slide 9: EEMs 3 – Increase automation
Character:
+ Manual production processes are energy-wasting and uneven.
Solution:
+ Use an automatic control system to optimize machine operation. + Application of smart sensors in energy management.
Benefit:
+ Increase operational efficiency by 15-20%. + Reduce errors and unnecessary energy consumption.

## Slide 10: Example 1 for EEMs 1,2,3
In the production of plastic pipes, Tien Phong Plastics applies double-layer extrusion technology, especially for HDPE twisted ribbed pipe products. This technology allows:​
  Create plastic tubing with a twisted ribbed outer layer to enhance mechanical strength. The smooth inner layer reduces friction and increases fluid drainage efficiency. Use raw materials more efficiently, reduce the amount of plastic needed while still ensuring product quality.​
The use of double-layer extrusion technology not only improves product performance, but also saves energy by optimizing the production process and reducing the amount of heat required for plastic processing.

## Slide 11: Cost – Benefits analyze Example 1
Double-Layer Extrusion Technology for HDPE Pipes
Estimated Implementation Costs
Cost Component | Cost Level | Notes
Double-layer extrusion line | High | $800,000- $1M depending on size, automation, and country of origin (e.g., China, Germany, Taiwan)
Auxiliary systems (cooling, dies, hauling, control units) | Moderate–High | $100,000 – $300,000
Installation, training, commissioning | Moderate | $30,000 – $50,000
Total Estimated Investment | High | Around $400,000 – $1 million (for a medium-sized pipe plant)

## Slide 12: Cost – Benefits analyze Example 1
Double-Layer Extrusion Technology for HDPE Pipes
Payback Period
Benefit Category | Impact | Notes
Energy savings | Moderate (~10–15%) | Due to higher extrusion efficiency, better heat control, optimized material flow
Material cost reduction | High (15–30%) | Inner layer can use cheaper materials (e.g., regrind, recycled HDPE) without affecting performance
Improved productivity | High | Faster line speeds, less downtime, better product consistency
Labor savings | Moderate | Automation reduces manual adjustments and errors
Estimated payback period | 2–4 years | Depending on production volume and material cost savings

## Slide 13: EEMs 4 – Application of inverter technology
Character:
+ Machines such as extruders, injection molding machines work continuously, consuming large amounts of power.
Solution:
+ Install a frequency converter (VFD) to adjust the motor speed according to actual needs.
Benefit:
+ Reduce power consumption by 20-40%. + Extend the life of the device.

## Slide 14: EEMs 5 - Optimize the cooling system
Character: Cooling systems account for a significant proportion of energy consumption.
Solution:
+Use a closed circulation cooling system to reduce water and energy loss. + Improved air-cooled technology instead of water.
Benefit:
+Reduce cooling costs by 10-15%. +Protecting the environment by reducing water consumption.

## Slide 15: Example 2 for EEMs 4,5
Thang Long Plastic Company (2009–2010)
According to a report from the VEEIE Project (MOIT), Thang Long Plastic surveyed and invested in improvement measures including:
Installing Variable Frequency Drives (VFD) for plastic injection molding machines,
Adding automatic control systems,
Improving cooling and internal lighting systems.
Energy-saving results (VFD application on injection machines only)
Energy savings: nearly VND 716 million/year (based on an electricity price of 968 VND/kWh) – source: vneec.gov.vn
VFD investment cost: Low – specific investment cost not disclosed by the company. Market prices range from VND 20–60 million per machine.
Estimated payback period: Short (possibly <1.5 years) for the VFD component.
Electricity savings: approximately 20–30%.
Notes: Source: https://vneec.gov.vn/tin-tuc/international-cooperation/t9158/thang-long-plastic-seeks-opportunities-to-save-energy?utm_source=chatgpt.com

## Slide 16: Example 3
Binh Minh Plastic Company
SCADA (Supervisory Control and Data Acquisition) system application is an automatic monitoring, control and data collection system in the input material mixing system. SCADA controls dosing valves, electronic scales, and mixers according to pre-programmed mixing formulas Strict control of ingredient ratio, mixing rate, mixing temperature, uniform quality assurance time. Invest in injection molding machines using servo motors instead of traditional hydraulic presses. Thanks to the precise control factor in the production process and only operating under load instead of continuous operation like a hydraulic press, injection molding machines using servo motors are capable of saving 30-50% of power consumption. The company's achieved efficiency is to save 30-50% of the power consumption of the plastic injection process and Increase accuracy, reduce technical errors and optimize the production process

## Slide 17: Cost – Benefit analyze Ex 3 (1)
Investment level: Moderate
SCADA software + PLCs: $20,000–$50,000
Integration with existing mixers/scales/valves
Engineering, commissioning, and training
Criteria | Evaluation
Capital cost | Moderate
Energy savings | Low–Moderate (indirect)
Material savings | Moderate–High
Quality improvement | High
Payback period | Short (1–3 yrs)
Cost-effectiveness | Very Good, especially for medium/large factories
Assessment:
Supervisory Control and Data Acquisition (SCADA)

## Slide 18: Cost – Effectiveness analyze Ex 3 (2)
Servo Motor-Based Injection Molding Machines
Machine Size (clamping force) | Traditional Hydraulic | Servo Motor-Based
Small (100–250 tons) | $40,000–$60,000 | $55,000–$80,000
Medium (300–500 tons) | $60,000–$90,000 | $85,000–$120,000
Large (>600 tons) | $90,000–$130,000 | $120,000–$160,000
Additional upfront cost: ~20–35% higher than traditional hydraulic machines.
Investment Cost

## Slide 19: Cost – Effectiveness analyze Ex 3 (2)
Factor | Typical Range
Annual energy savings | $5,000–$15,000/machine
Maintenance savings | $1,000–$3,000/year
Material savings (indirect) | $2,000–$5,000/year
Total savings/year | $8,000–$20,000+
Payback time | 1.5 to 3.5 years
Payback Period Estimation
Depends on machine size, usage hours/day, electricity rate, and part type.
Servo Motor-Based Injection Molding Machines

## Slide 20: Cost – Effectiveness analyze Ex 3 (2)
Criteria | Evaluation
Initial investment | Moderate–High
Energy efficiency | High (30–60% reduction)
Maintenance savings | Moderate
Product consistency | High (less reject rate)
Environmental benefit | High (less noise, no oil, less heat)
Payback period | Short–Moderate (1.5–3.5 years)
Overall cost-effectiveness | Very good, especially for 2+ shift operations
Cost-Effectiveness Assessment
Servo Motor-Based Injection Molding Machines

## Slide 21: EEMs 6 - Improve energy management
Character: Ineffective energy management leads to significant waste.
Solution:
+ Adopt an energy management system (ISO 50001).
+ Monitoring and evaluating energy efficiency in each stage.
Benefit: Save 5-10% of energy through better management.

## Slide 22: EEMs 7: Other EEMs
Drying plastics with recirculating hot air
Energy efficiency: Reuse of hot air, the system minimizes the need for energy to heat new air, saving around 35% of energy consumption compared to traditional resistance dryers.​
High drying efficiency: The temperature in the drying chamber is maintained sturdily, making the drying process fast and steady.
Drying hopper
Recirculation filter
Ingredient
Plastic blowing machine
Filter with plastic blower
Heater
Compressed air supply
Coagulant filter
Dryer set no heating

## Slide 23: EEMs 7: Other EEMs
Consider the EE manual potential of the backend system
With compressed air system.
  Leak control of pneumatic systems. Ensure the lowest possible compressor inlet air temperature by keeping the compressor room ventilated and free from cooling air that leads to a hot compressor room. Adopt inverter and control the air compressor in groups. Optimum calibration for air dryers.
With pump system, fan.
  Consider controlling the flow of the pump and fan system with an inverter.

## Slide 24: Example 4 for EEMs 6,7
A plastic factory in Vietnam apply energy management system in manufacturing, focusing on compressed air systems, motor control, waste heat recovery, and HVAC optimization. These illustrate how smart, often low-cost strategies can yield substantial energy and cost savings.
Case | Investment | Annual Savings | Payback Period | Cost-Effectiveness
Compressed Air Leak Repair | Very Low | USD 30,000 | <6 months | ⭐⭐⭐⭐⭐
Air Compressor Optimization | USD 50,000 | USD 27,000 | ~2 years | ⭐⭐⭐⭐
VFD on 30 kW Fan | USD 8,000 | USD 13,100 | 9 months | ⭐⭐⭐⭐⭐
HVAC Optimization | Near-zero | USD 50,000 | Immediate | ⭐⭐⭐⭐⭐⭐ (Behavioral measure)

## Slide 25: EEMs 8 - Use renewable energy
Character:
+ Manufacturing facilities often depend on grid electricity and fossil fuels.
Solution:
+ Install solar power systems to reduce dependence on the grid. + Application of biomass energy in heating.
Benefit:
+Reduce CO₂ emissions and long-term energy costs.

## Slide 26: Example 5 (1)
Case Study: Duy Tân Plastics – Rooftop Solar (2.17 MWp)
a. Background
Duy Tân installed 2.17 MWp rooftop PV at its Binh Dương plant under a Power Purchase Agreement (PPA), with BayWa r.e. and Vu Phong Energy.
System includes 3,289 panels and inverters.
b. Performance & Impact
Generates over 3 million kWh/year and removes ~2,000 tCO₂ annually
Further, Duy Tân’s Long An facility has a 9.93 MWp rooftop system producing 13 million kWh/year—cutting CO₂ by ~8,740 t and saving up to VND 5.3 billion/year (~USD 225,000)

## Slide 27: Example 5 (2)
Factor | Duy Tân Plastics (2.17 MWp)
Installed capacity | 2,170 kWp
Annual generation | ~3,000 MWh/year
Reduction in electricity costs | ~25% (2.17/9.93 MW = ~22% of Long An)
CO₂ avoided | ~2,000 tons/year
Investment model | PPA- zero CAPEX (Capital Expenditures) for Duy Tân
Payback | Immediate OPEX (Operating Expenses) savings via PPA
Economic Analysis (Typical for Solar in Plastic Industry)
Duy Tân: Under PPA, no upfront cost; savings start immediately, contract guarantees stable, lower-cost power.

## Slide 28: Q & A

## Slide 29: Conclusions and recommendations
Conclusions:
Energy saving in the plastics industry not only helps reduce costs but also protects the environment, meeting the trend of sustainable production.
Many opportunities exist for improving EE and there are many demonstrated examples of successful implementation of EEMs
Recommendations:
Businesses need to invest in modern technology and an effective energy management system.
The Government needs to support preferential policies and loans to encourage businesses to transform technology.
Strengthening human resource training on economical and efficient use of energy.

## Slide 30
THANKS YOU!