## Slide 1
FINANCIAL APPRAISAL AND GUARANTEE/COLLATERAL ISSUES

## Slide 2
TABLE OF CONTENT
1. Feasibility study report structure
2. Review of Economic and Financial Analysis Principles
3. Eligibility criteria for sub-projects
4. Appraisal methodology
5. Data and assumptions requirements
6. Case studies and discussions

## Slide 3
1. FEASIBILITY STUDY REPORT STRUCTURE

## Slide 4
Feasibility study report structure
Chapter 1: General introduction to the project
Chapter 2: Investment necessity of the project
Chapter 3: Technical and construction solutions
Chapter 4: Site clearance and resettlement plan
Chapter 5: Environmental impact assessment
Chapter 6: Total investment cost
Chapter 7: Economic-Financial analysis
Chapter 8: Implementation organization
Chapter 9: Conclusions and Recommendations
Accompanied by a World Bank (WB) template Excel file for economic-financial analysis!

## Slide 5
2. ECONOMIC AND FINANCIAL ANALYSIS PRINCIPLES
Page 5

## Slide 6
Template for presenting economic-financial analysis in a feasibility study (FS)
CHAPTER 7: TOTAL INVESTMENT AND ECONOMIC & FINANCIAL ANALYSIS
7.1. TOTAL INVESTMENT
7.1.1: SUMMARY OF TOTAL INVESTMENT FOR THE ENTIRE PROJECT
6
No. | Description | Category A | Category B | Category C | Total
1 | 2 | 3 | 4 | 5 | 6 = 3+4+5
1 | Equipment Costs | 48,952,831,590 | 3,010,788,625 | 14,823,898,462 | 66,787,518,676
2 | Construction Costs | 142,965,289 | 5,063,235,864 | 20,241,137,774 | 25,447,338,928
3 | Compensation and Resettlement Costs | 4,971,871,697 | 20,000,000 | 260,000,000 | 5,251,871,697
4 | Project Management Costs | 875,512,572 | 186,509,966 | 658,121,239 | 1,720,143,777
5 | Consulting Costs | 3,301,555,065 | 1,040,057,597 | 2,786,096,576 | 7,127,709,238
6 | Other Costs | 2,191,084,225 | 263,631,074 | 1,058,672,519 | 3,513,387,818
7 | Contingency | 9,156,384,151 | 1,440,701,698 | 5,989,837,872 | 16,586,923,722
 | TOTAL (rounded) | 69,592,204,590 | 11,024,900,000 | 45,817,764,443 | 126,434,869,033

## Slide 7
Template for presenting economic-financial analysis in a feasibility study (FS)
7
Indicator | Result
NPV (billion VND) | 37,280
B/C | 1.18
IRR (%) | 13
Indicator | Result
NPV (billion VND) | 45,620
B/C | 1.32
IRR (%) | 14.6
7.2. FINANCIAL ANALYSIS:
+ Financial Analysis
+ Socio-Economic Indicators
Notes: Financial indicators measure the project's cash flow efficiency for the investor and its debt repayment capacity for the bank (financial NPV/IRR, DSCR, etc.).
Socio-economic indicators measure the net social welfare when considering externalities and using "economic prices" (ENPV/EIRR, benefit-cost ratio, abatement cost, health benefits, etc.).
Example applied to an energy efficiency project:
Financial: Saved electricity/fuel costs ↑ → financial NPV/IRR > hurdle rate; DSCR ≥ 1.2–1.3; no valuation of CO₂ or health impacts.
Socio-Economic: Adds the value of avoided CO₂ emissions, health benefits from reduced SO₂/PM, reduced fuel imports… → ENPV ↑, EIRR ↑, abatement cost ($/tCO₂) ↓.
"Financial analysis determines bankability; socio-economic analysis determines justifiability at the policy level."

## Slide 8
Common Issues
Several common issues in economic-financial analysis:
Failure to clearly distinguish between economic and financial costs.
Price level? (The specific year or basis for prices is often unstated or not updated).
Excessively summarized, with very little information on risks and benefits: Within a lengthy report/document, the economic-financial analysis section often provides only an Excel-based financial analysis table without sufficient context or elaboration.
Page 8
Notes: Enterprises or ESCOs often do not clearly distinguish between economic costs and financial costs, leading to potential confusion when presenting them in the application dossier.

## Slide 9
Objectives of Economic-Financial Analysis for a Proposed Project
Economic and financial analyses are conceptually similar – both aim to compare the benefits and costs of a project. These costs and benefits depend on who measures them. The project must:
Meet a minimum economic or financial rate of return, and
Be the best option among alternatives to achieve the same project objectives.
Investment in a project must be compared to the "do-nothing" scenario (i.e., the "without-project" option) or delaying the project.
Page 9

## Slide 10
FINANCIAL AND ECONOMIC ANALYSIS
 | Economic Analysis | Financial Analysis
Objective | Maximizes efficiency in the use of finite resources such as capital, labor, natural resources, etc. | Evaluates financial viability from the perspective of an economically optimized project
Scope | Broad (entire economy) | Narrow (project scope only)
Input data | Economic benefits and costs measured by "shadow prices", including inflation and all transfers such as taxes, subsidies, interest payments, etc. | Project revenues and costs measured by market prices, including inflation and items such as taxes, subsidies, interest, import duties, etc.
Results | Net Present Value (NPV) and/or Economic Rate of Return (ERR) | Monetary profits and/or Financial Rate of Return (FRR)

## Slide 11
Financial and economic analysis is used by the World Bank to determine the feasibility of a project. Governments also often require similar analyses to assess the impact of state policies, regulations, and programs on public spending and social benefits.
Financial analysis is used to determine the financial feasibility of an activity from the perspective of the implementing entity. This analysis focuses on cash inflows and outflows related to the project and uses market prices.
Economic analysis is used to determine the net impact (cost or benefit) of an activity on the economy and society as a whole (at the national and global levels). This analysis uses economic prices, taking into account the opportunity cost to society, the presence of government interventions that cause market distortions (e.g., taxes, tariffs, subsidies), and externalities.
FINANCIAL AND ECONOMIC ANALYSIS (WORLD BANK)

## Slide 12
Economic Analysis and Financial Analysis
Economic analysis evaluates the project's benefits from the perspective of the Nation and the National Economy:
At any given time, Vietnam has limited resources (skilled labor, natural resources, electrical power, investment capital).
The fundamental question during project appraisal is whether Vietnam achieves greater benefits by investing its scarce economic resources in one project over another: power distribution, renewable energy, roads, seaports, etc.

## Slide 13
Economic Analysis and Financial Analysis
For example, the cost of importing equipment to improve energy efficiency:
For the enterprise, this cost includes the full import cost (purchase price, insurance, freight – CIF) at the point of import, plus import duties (if applicable).
From the national perspective, is import duty considered a cost? Why is only CIF the economic cost?
In economic analysis, the following costs are excluded:
Interest payments – representing transfers from borrowers to capital owners.
Various taxes – representing transfers from consumers or businesses to the Government.
Import duties
Natural resource taxes

## Slide 14
Economic Analysis and Financial Analysis
In economic analysis:
Costs and benefits are accounted for in the year when resources are consumed.
Therefore, the entire capital cost (excluding taxes and transfer payments) is accounted for during the construction period (not just equity capital).
Debt repayments and interest payments are financial transactions and are not included in economic analysis.
When an energy efficiency project reduces electricity consumption, its economic benefit is not the electricity bill paid by the enterprise but the avoided fuel cost for generating the electricity and the avoided capital cost for EVN (the utility).
The hurdle rate for economic analysis is the economic discount rate (which differs from the financial hurdle rate, e.g., WACC).

## Slide 15
Economic analysis and financial analysis
Financial analysis assesses the project's benefits from the perspective of the investor or project owner (enterprise).
The enterprise evaluates benefits and costs in monetary terms.
The financial benefits of an energy efficiency (EE) project include the monetary savings from purchasing less electricity, oil, or coal; avoided O&M costs; and reduced chemical expenses. The value of energy inputs for the enterprise is based on all actual costs incurred, including taxes, fees, and import duties: i.e., all cash expenses for the enterprise.
The financial costs of an EE project include the required investments plus any additional O&M costs related to new equipment or improved operational management. Investment costs for the enterprise include customs duties and VAT.
These financial cash flows form the basis for financial analysis.

## Slide 16
Examples of financial and socio-economic analysis
Project for optimizing the motor system in the production line
CAPEX: USD 1,000,000
Annual Energy Savings: 2,000 MWh/year
Incremental O&M: USD 10,000/year
Analysis Lifespan: 10 years
Financial Analysis:
Electricity tariff (bill price): 100 USD/MWh
Discount rate / WACC: 12% (Excluding CO₂ cost, not using shadow pricing)
Socio-Economic Analysis:
Shadow Price of Electricity (Economic Price): 120 USD/MWh
Grid Emission Factor: 0.7 tCO₂/MWh
Value of CO₂ (SCC): 40 USD/tCO₂
Social Discount Rate: 8%
(Excluding taxes and interest; including CO₂ benefits)

## Slide 17
Examples of financial and socio-economic analysis
Indicator | Financial | Socio-Economic
NPV | +0.074 milliom USD | +0.919 miilion USD
IRR/EIRR | 13.8% | 25.7%
Payback Period | ~5.3 years | —
B/C Ratio | 1.07 (¹) | 1.92
Abatement Cost | — | −57.8 USD/tCO₂ (net savings)
Notes: Financial B/C: B = Present Value (PV) of bill savings, C = CAPEX + PV of incremental O&M, excluding debt interest/taxes.
Socio-Economic (Economic CBA): The international standard employs Economic Net Present Value (ENPV), Economic Internal Rate of Return (EIRR), and the Benefit-Cost (B/C) Ratio. The payback period (especially the "simple payback") is not used because this metric ignores all benefits occurring after the payback point and (in its "simple" form) does not reflect the time value of money. This contradicts the logic of social welfare analysis, where all cost and benefit flows throughout the entire project lifecycle (including the later stages) are important and are discounted using the social discount rate. While a discounted payback period exists, it is rarely a decisive criterion in Cost-Benefit Analysis (CBA).
Financial Analysis: Investors/banks focus on the financial NPV, financial IRR, Debt Service Coverage Ratio (DSCR), and Loan Life Coverage Ratio (LLCR). A simple payback period is often included alongside these to provide an intuitive sense of the capital recovery time. The B/C ratio is less commonly used in financial analysis because cash flows are typically recorded on a "net" basis (benefit minus cost), which aligns perfectly with NPV and IRR. To calculate a B/C ratio, one must separate benefits and costs (e.g., assign CAPEX + O&M to "C" and bill savings to "B"), a step practical investors do not need for decision-making. Furthermore, the classification of items as a benefit (B) or a cost (C) (particularly financial costs, taxes, and depreciation) can easily become ambiguous. Consequently, the B/C ratio is used primarily in economic CBA to compare projects when public budgets are constrained.

## Slide 18
Economic Analysis and Financial Analysis
Financial analysis evaluates and compares project implementation options based on cash and cash flows, from the perspective of the investor/project owner. If the project owner must pay income tax, it is considered a financial cost. If imported equipment is subject to import duties, these are also financial costs.
Economic analysis evaluates and compares projects based on economic flows, from the perspective of the nation. Income tax is not an economic cost for the nation; it is termed a transfer payment—money transferred from one pocket to another. Customs duties are also not economic costs.
Therefore, the costs and benefits in economic analysis are not necessarily the same as those in financial analysis.

## Slide 19
Depreciation
Depreciation expense is the book value of an asset, used for accounting purposes, and is not in itself an economic or financial cost. Therefore, it is not included in economic analysis.
In financial analysis, depreciation is included to calculate the corporate tax liability that the enterprise must pay.

## Slide 20
Key Indicators
What measures project benefits?
In financial analysis, the following indicators are used:
Financial Internal Rate of Return (FIRR)
Payback Period
In economic analysis, we use:
Net Present Value (NPV): The present value of annual economic benefits minus the present value of annual economic costs, evaluated over the project’s economic life.
Economic Rate of Return (ERR): Measures the return not on equity but on the economic cost of investment.
It is important to note that a financial institution's loan approval decision is typically based on a financial analysis, not an economic analysis. The borrower (the industrial company or ESCO) should be mindful of this distinction when preparing the loan application and its supporting documentation.

## Slide 21
Definition
Where:
Bt = Benefits in year *t*
Ct = Costs in year *t*
r = Discount rate
n = Planning horizon
The Economic Rate of Return (ERR) is the discount rate that makes the Net Present Value (NPV) equal to zero (NPV = 0).

## Slide 22
Discount Rate
The discount rate (r) is measured as a percentage (%).
The discount rate in economic analysis represents the opportunity cost of capital for a nation's investments:
  At any given time, Vietnam has limited resources (skilled labor, natural resources, electrical power, investment capital).
  The fundamental question in economic analysis is whether Vietnam benefits more from investing these scarce resources in a hydroelectric project compared to other projects, such as building roads.
  The challenge is that no one knows exactly what the opportunity cost of capital is.

## Slide 23
Discount Rate
Regarding Discount Rates:
Historically, the discount rate typically reflects the "Economic Opportunity Cost of Capital" (EOCC). However, most companies use a fixed discount rate for many years. For example:
Is it reasonable to assume a constant EOCC over 35 years? This was done by the Ceylon Electricity Board when running the WASP model for power system planning.
In most cases, the selected discount rate is applied without thorough consideration—for instance:
In Peru and the Philippines, a rate of 14% was set arbitrarily high to avoid crowding out private projects.

## Slide 24
Economic Discount Rate
Ramsey Formula
The World Bank currently uses the Ramsey formula to calculate the discount rate (*r*):
Where:
  = pure time preference rate (reflects societal preference for current vs. future consumption),
  = elasticity of marginal utility of consumption (measures how utility changes with consumption),
  = expected growth rate of per capita consumption.
With the values set by the World Bank (, ), the formula simplifies to . This implies the discount rate is twice the growth rate of real GDP per capita.
However, whether using EOCC or Ramsey, the purpose of setting a discount rate is to determine the rate at which society is willing to trade off present consumption for future benefits.

## Slide 25
Economic Discount Rate
The government requires that the economic return of the proposed investment must exceed the (opportunity) cost of capital, based on the economic growth rate as per PMB guidelines:
GDP growth rate of 3% → Discount rate: 6%
GDP growth rate >6% → Discount rate: 12%
Over the past 50 years, Vietnam’s real GDP per capita growth has fluctuated between 0% to 5%.

## Slide 26
Financial Discount Rate
The discount rate (r) is measured as a percentage (%).
In financial analysis, the discount rate represents the opportunity cost of capital for the investor:
  The key question for the investor is whether the (relatively risky) project offers higher returns compared to safer investments like government bonds or savings accounts. Higher risk requires higher expected returns.
The discount rate in financial analysis is calculated based on the project's direct financial costs. It is the weighted average between:
  The interest rate on borrowed funds (e.g., commercial loans, concessional loans, or supported credit), and
  The minimum required rate of return on the investor's equity (MARR – Minimum Attractive Rate of Return).

## Slide 27
Weighted Average Cost of Capital (WACC)
WACC (Weighted Average Cost of Capital) is calculated as follows:
WACC = Interest rate*tdebt*(1- Corporate income tax rate)+ MARR * t equity
tDebt: % Proportion of borrowed capital in total investment
tequity: % Proportion of equity capital in total investment
Page 27

## Slide 28
3. ELIGIBILITY CRITERIA FOR SUB-PROJECTS

## Slide 29
Eligibility criteria for sub-projects
Eligible types of sub-projects for financing under the VSUEE project involve investments in retrofitting and upgrading (adjusting, replacing) existing components and systems to achieve energy efficiency. Exemplary investment sub-projects include:
Replacing inefficient industrial technologies with energy-saving solutions such as high-efficiency industrial boilers, furnaces, and more efficient heat exchange systems;
Recovering and utilizing by-product gases, waste heat, and pressure;
Installing high-efficiency electrical and electromechanical equipment, including lighting, motors, pumps, heating, and ventilation systems;
Optimizing industrial systems to minimize energy consumption;
Other sub-projects approved by the Ministry of Industry and Trade and the World Bank.

## Slide 30
Eligibility criteria for sub-projects
All eligible sub-projects must meet the following economic criteria:
Demonstrate a minimum achieved energy savings rate of ten percent (10%). (A lower energy savings rate may be accepted for specific industries with advanced energy technologies) by applying the following formula:
Es=(Eb – Ea)/Eb * 100%
Es – Energy savings rate (%)
Eb – Energy consumption before sub-project implementation (kWh, kJ, TOE)
Ea - Energy consumption after sub-project implementation (kWh, kJ, TOE)
Note: Projects related to waste gas or waste heat recovery are considered eligible without having to demonstrate the minimum energy savings rate.

## Slide 31
Eligibility criteria for sub-projects
All eligible sub-projects must meet the following financial criteria:
The project must have a payback period within ten (10) years.
The Internal Rate of Return (IRR) must be higher than ten percent (10%).

## Slide 32
Eligibility criteria for sub-projects
Environmental and Social Eligibility of Sub-Projects:
The Implementing Entity (IE) must obtain all necessary environmental approvals from competent environmental authorities at the national, provincial, and local levels, and submit copies of all required approval documents to the Project Financial Intermediary (PFI).
Sub-projects must undergo screening for safety and comply with the World Bank's environmental and social requirements, as well as domestic environmental and social regulations.

## Slide 33
4. APPRAISAL METHODOLOGY
Page 33

## Slide 34
1. Assessment of the borrower’s financial and business situation
For Borrowers that are manufacturing facilities or enterprises:
Evaluate the borrower’s industry indicators, trends, prospects, and market position; assess the management strength of the Implementing Entity (IE) and its corporate governance structure; analyze key business risks.
Analyze state guidelines and policies for the industry; review PFI (Project Financial Intermediary) guidelines and policies for the industry.
Financial status of the IE: Conduct a comprehensive analysis of the IE’s financial statements — including capital structure, operating profit margins, sales growth, debt repayment capacity, liquidity analysis, etc.

## Slide 35
1. Assessment of the borrower’s financial and business situation
For Borrowers that are ESCOs (Energy Service Companies):
Evaluate the borrower’s market position, customer base, prior experience, performance in previous ESCO projects, management strength, and corporate governance structure; analyze key business risks.
Review state guidelines and policies for the ESCO industry; assess PFI (Project Financial Intermediary) guidelines and policies for the industry.
Conduct a financial evaluation of the Borrower based on a comprehensive analysis of its financial statements — including capital structure, operating profit margins, sales growth, debt service coverage, liquidity analysis, etc.
Audited financial statements for the past 3 years must be reviewed.

## Slide 36
2. Financial assessment of the sub-project
The economic and financial analysis must be presented in a separate chapter.
The Borrower must complete the financial analysis spreadsheet provided by the PMB (Project Management Board) for the World Bank's review and issuance of a "no objection" notice. This requirement must be fulfilled in addition to the procedures required by the PFI (Project Financial Intermediary) under its routine commercial due diligence process.
Sub-project Financial Assessment:
Analyze the financial viability of the sub-project — calculate the Internal Rate of Return (IRR) on the investment.
Assess the impact on the Borrower’s profitability, cash flow, and balance sheet.

## Slide 37
2. Financial assessment of the sub-project
Additional Assessment for ESCO Borrowers:
Analyze the impact on the end-user's net cash flow and profitability throughout the loan term;
Total costs, including interest payable during the construction phase;
Contract performance terms: debt service payments, allocation of energy savings between the ESCO and the end-user; ESCO cash flow;
Level of guarantee for energy savings and how such guarantees are secured;
Estimated energy savings and energy cost savings – by year;
Other estimated cost savings – by year;
Total estimated cost savings – by year;

## Slide 38
2. Financial assessment of the sub-project
Additional Assessment for ESCO Borrowers:
Share of savings for the ESCO – by year;
Share of savings for the End-User – by year;
Debt amount;
Debt service cost – by year;
M&V (Measurement and Verification) cost – by year;
Ratio of total cost savings to debt service – by year;
Ratio of ESCO's total cost savings to debt service – by year;
Proposed Measurement and Verification (M&V) method.

## Slide 39
2. Financial assessment of the sub-project
All eligible sub-projects must ensure that the expected cash flow from energy savings related to the sub-project is sufficient to cover the sub-project investment costs (including interest during the construction period) within ten years, based on the following simple payback period (PBP) formula:
The energy savings payback period shall be calculated as follows:
Energy savings payback period = Total sub-project investment cost/ Average annual cash flow from energy savings

## Slide 40
2. Financial assessment of the sub-project
For industrial sub-projects:
Annual cash flow from energy savings=
[(Pa/Pb) x average annual energy expenditure of the 2 years prior to the sub-project]– [annual energy expenditure after the sub-project]
Where:
* Pa = expected annual output (production) after the sub-project;
* Pb = average annual output (production) of the 2 years prior to the sub-project
PBP < 10 years

## Slide 41
2. Financial assessment of the sub-project
For ESCO sub-projects:
The following two additional ratios must be considered:
* Energy savings from the sub-project / Debt service ratio
* ESCO's cash flow from energy savings / Debt service ratio

## Slide 42
3. Sub-project costs, financing plan, and loan repayment
Detailed breakdown of sub-project costs by component;
Basis and assumptions for cost estimation;
Analysis of funding sources for the sub-project;
PFI’s contribution to the total loan value for the sub-project;
Assessment of the legitimacy of the loan purpose and context;
Analysis of the repayment plan, repayment sources, and associated risks;

## Slide 43
4. Analysis of collateral and guarantees
Analysis of the guarantor, including operations, financial status, and creditworthiness;
Analysis of collateral/mortgage assets, including basic documentation, legality, validity, appraised value, and calculation of collateral/mortgage value;
For ESCO projects, analysis of the energy performance contract between the ESCO and the IE (Implementing Entity), projected savings, and the related Measurement and Verification (M&V) method to be used for confirming performance and ensuring sustainability.

## Slide 44
5. DATA AND
ASSUMPTIONS REQUIREMENTS
Page 44

## Slide 45
Input data requirements for project proponents
Capital and operating costs of the EE investment (broken down into imported and domestic components). Fixed O&M, variable O&M (based on production volume). For imported equipment quoted in USD, provide the exchange rate (and date) used for estimation. Schedule and estimates for planned equipment maintenance (and downtime).
For large projects, cost estimates must include contingency allowances.
Construction timeline and annual disbursement rates.
Expected economic lifespan, residual value.
Depreciation method, depreciable lifespan (may differ from economic lifespan).
Changes in operating costs.
If applicable, changes in thermal capacity, efficiency over time.
Estimated annual savings: fuel oil, diesel (liters/year), coal (tons/year with consistent calorific value and type), electricity, chemicals, water, etc.

## Slide 46
Input Data: Requirements for Project Proposers
Current plant-gate prices for energy (electricity, fuel)
Project proposer's estimates for exchange rates, inflation, fuel prices, and electricity prices
Self-consumption ratio
Proposed equity/debt ratio
Expected corporate tax rate (including deductions, incentives)
Page 46

## Slide 47
6. CASE STUDY

## Slide 48
7. DISCUSSION

## Slide 49
THANK YOU